Justifying the importance of color cues in object detection:

a case study on pedestrian

Qingyuan Wang

1,2

, Junbiao Pang

3

, Lei Qin

2

,

Shuqiang Jiang

2

, Qingming Huang

1, 2

1Graduate University of Chinese Academy of Sciences, Beijing, 100049, China

2Key Lab of Intell.Info.Process., Inst. of Comput. Tech., CAS, Beijing 100190, China

3

Beijing Municipal Key Lab. of Multimedia and Intelligent Software Technology, College of

Computer Science and Technology, Beijing University of Technology, 100124, China

{qywang, jbpang, lqin, sqjiang, qmhuang}@jdl.ac.cn

Abstract. Considerable progress has been made on hand-crafted features in object

detection, while little effort has been devoted to make use of the color cues. In this

paper, we study the role of color cues in detection via a representative object, i.e.,

pedestrian, as its variability of pose  or appearance is very common for  “general”

objects. The  efficiency of  color space  is first ranked by empirical comparisons

among  typical ones.  Furthermore, a color descriptor, called MDST (Max

DisSimilarity of different Templates), is built on those selected color spaces to

explore invariant ability and discriminative power of color cues. The extensive

experiments reveal two facts: one is that the choice of color spaces has a great

influence on performance;  another is that  MDST achieves better results than the

state-of-the-art color feature for pedestrian detection in terms of both accuracy and

speed.

Keywords:  Pedestrian detection, Color space analysis, Color descriptor, Invariant

descriptor.

1   Introduction

In recent years, detecting the predefined objects in images has been an attracting problem

in computer vision, e.g., face [13, 14, 15], pedestrian [4, 5, 6, 7, 8, 9]. Accurate detection

would have immediate impacts on many real applications,  such as intelligence

surveillance [1] and driver assistance systems [2, 3]. Detecting non-rigid objects in images

is still a challenging task, due to the variable appearance and the wide range of poses. In

this paper, pedestrian is used as a typical case, because its variable poses and diversity of

clothing are representative and challenging for “general” objects, e.g., animals, car, et [16].

Recently shape information [4, 5, 6],  mainly  described by gradients,  has been

exhaustively explored and successfully used in detection, and yet color cues do not attractFig. 1. The average positive examples of INRIA dataset are visualized in the different color spaces

and the corresponding channels. Some images show clear silhouette-like boundary, while other just

enhances parts of the pedestrians, e.g., head in YIQ space.

enough attention. Moreover, color cues have been facilely considered to be useless, due to

the variability in the color of clothing. In our best knowledge, we first try our best to

systematically evaluate the role of color cues, and show that color cues can achieve

competitive results in pedestrian detection. Our study is based on the following

methodology: 1) There are a variety of color spaces, yet which one is better for detection

is still a controversy problem [8, 9]; therefore, typical color spaces are naturally compared

(see Fig. 1.). 2) A simple yet efficient color descriptor is proposed to be evaluated on the

selected color spaces.

Although the INRIA pedestrian dataset [4], as our primary testbed, may be relatively

simple [9], our experiments about color cues still reap a huge harvest. First, we show that

there are significant differences of performance among color spaces, thus, the choice of

color spaces is very important in detection. Second, different coding schemes lead to

diverse accuracies, and thus the selection of coding method is a key to boost performance.

Third, the combination of color descriptors with the shape-based feature [4] shows the

complementary yet important role of color cues in object detection.

The remainder of this paper is organized as follows. In Sec. 2, we give an overview

of the related works. In Sec. 3, we introduce different color spaces and describe the details

on evaluating color spaces. Then our proposed color descriptor will be presented in Sec. 4.

In Sec.  5 we perform  the detailed experimental evaluations. Finally, we conclude this

paper in section 6.

2      Related Work

Color information is very popular in image classification [10][22], but it does not attract

enough attention in object detection, and most people still doubt the efficiency of color for

detection. On the other side, a few literatures use color cues in naïve approaches, and set a

minor role for color in detection.In HOG [4], the orientation of the gradient for a pixel is selected from the R, G and B

channels according to the highest gradient magnitude. Thus some color information can

be captured  by the number of  a  channel is chosen in HOG [4]. Comparing with HOG,

Schwartz et al. [7], further, construct a three bin histogram that tabulates the number of

times each color channel is chosen. So they call this color descriptor as color frequency.

This color  feature mainly captures the color information of faces, due to the possible

homologous skin color  in faces. However, the information of whole body tends to be

ignored as illustrated in Fig. 1.

Walk et al. [8] observe that the colors of pedestrians may be globally similar, e.g., the

color of faces is similar to the one of hands. Therefore,  color self-similarity (CSS) is

introduced to capture the similarities among whole body. This feature captures pair-wise

spatially statistics of color distribution, e.g., color of clothes ignored by the color

frequency descriptor [7]. On the other hand, the computational cost of CSS is intensive,

because  CSS calculates the global self-similarity within the detection window.  For

instance, the dimension of CSS for a 128x64 window is 8,128.

Both of the above works are integrated with  Support Vector Machine (SVM)

classification framework, while Dollar et al. [9] use color cues in boosting via an integral

channel features approach. The color features are firstly generated by summing the pixel

values in the pre-designed templates. The discriminative feature is chosen by boosting

classifiers. It is a type of first-order feature, and the disadvantages of the color frequency

descriptor [7] still exist in this coding method. On the other interesting side, Dollar et al.

[9] and Walk et al. [8] give totally different conclusion on using color spaces for object

detection. In this paper, the efficiency of color spaces will be first systematically ranked

by empirical comparisons.

3      Analysis of Color Space

In this section, the  typical color spaces are  introduced, and then evaluated to rank the

performance of color spaces for pedestrian detection.

3.1   Color Spaces

Color is usually described by the combined effect of three independent attributes

/channels. For example, R, G and B are the widely used color channels. There are many

other color spaces in computer vision or related communities, because different color

spaces can describe the same object from different perspectives. In this paper, we divide

the color spaces into three categories according to the application purposes.

Color spaces for Computer Graphics. These color spaces are mainly used in display

system, for example, RGB, HSV and HSI.  And RGB, HSV and HSI are chosen to be

evaluated in our experiment.Fig. 2. The HLC extract procedure. A three-channel color space is used as an example.

Color Spaces for TV System. YIQ and YUV are analogue spaces for NTSC (National

Television System Committee) [17] and  PAL (Phase Alternating Line) [18] systems

respectively, while YCbCr is a digital standard. And YIQ, YUV and YCbCr are all picked

in our experiment.

CIE Color Spaces. The  CIE (International Commission on Illumination) [19]  system

characterizes colors by a luminance parameter Y, and two color coordinates x and y.

Some typical CIE spaces, i.e., XYZ, LUV and Lab, will be evaluated.

In addition, in many applications in order to keep the luminance invariance, the

intensity attribute is discarded and only the chrominance is kept. So, in our experiment we

will also evaluate this kind of color spaces, including normalized RG, normalized HS and

normalized UV [8].

3.2   Evaluation of color spaces

One of our goals is to find and explain that which color space would be the best one for

pedestrian detection. On the other side, the color feature may have great influence on the

accuracy, and thus feature should be simple and unbiased to reflect the  ability of color

spaces.  As illustrated in Fig. 1, color histogram may be a good choice to describe the

distribution of colors.  A localized color histograms, termed HLC (Histogram of Local

Color), is advocated as our evaluation feature.

HLC. It firstly converts an image into different channels, and then  divides  each color

channel image into small spatial  non-overlapped regions (“block”).  In each block, a

local 1-D histogram of color values is  accumulated

1

. Next, the channel-level HLC is

constructed by concatenating the histograms in all blocks. The image-level HLC is finally

obtained by  concatenating the channel-level HLCs (see Fig. 2). In our experiments, we

compute histograms on 16×16 pixels blocks.

1During histogram calculation, trilinear interpolation is applied to avoid quantization effects.Fig. 3. The method of calculating the MDST for an example

4      Max DisSimilarity of Different Templates

As shown in Fig. 1,  the  boundary of the whole or parts of pedestrian can be clearly

illustrated. Our work is to explore a descriptor that can capture the boundary effectively

regardless of variability of clothing or its color. Max DisSimilarity of different Templates

(MDST), based on the max-coding, is designed to capture  the local boundary and  to

increase the translation invariance of feature.

MDST. Firstly, the image is divided into non-overlapped regions (we call it as “cells”).

The feature/“attribute” of a cell is calculated in the enlarged local area/”calculation unit”

2

which centers on the cell, as shown in  Fig. 3(a). In the calculation unit, 12 templates,

shown in Fig. 3(b), are designed to capture the local boundary information. The number 0,

1 and 2 indicate three different cells in a template. For the j-th cell in the i-th template, an

n-dimension color histogram, cell

ij

, is extracted to calculate the dissimilarity values.

ds dissim cell cell i j

ij i ij    ( , ) 1, 2,3...,12; {1, 2}

0

(1)

Where “ dissim ” is a function to measure the dissimilarity between two cells. There are

many possibilities to define dissimilarity for histogram comparison. In our experiments, a

number of well-known distance functions, L1-norm, L2-norm, chi-square-distance, and

histogram intersection, are all evaluated, and histogram intersection works best.

The dissimilarity  scores, mds

i

, in  the i-th template is calculated by max-pooling

between 0-1and 0-2 dissimilarity pairs,

2

In our experiment, we use a 3x3-cell to be the calculation unit as the oblique line indicates.Fig. 4. Evaluation of diverse color spaces on HLC. (a) The per-window evaluation result. (b) The

per-image evaluation result.

mds ds ds i

i i   max( , ) 1, 2,3...,12

i1 2

(2)

So, the feature  for a cell is extracted by assembling the score mds

i

in all 12

templates as

f mds mds mds mds [ , , ,..., ]

1 2 3 12

.                      (3)

The feature vectors further  are normalized in  a 2x2 cell (termed as  “block”), as

illustrated in Fig. 3(c). We get a 48-dimension feature over one block after the block-wise

normalization, and the MDST can concatenate features in all blocks. In our experiments,

the cell size is  8x8 pixels for a 128x64 window, which would have 1,536-dimension

MDST.

5      Experimental Results and Discussions

In our experiment, we utilize two evaluation protocols that are the per-window and perimage evaluation. The per-window evaluation methodology is to classify manually

normalized examples against windows sampled at a fixed density from images without

pedestrians, corresponding to the miss rate against False Positive Per Window (FPPW).

While in the per-image evaluation, a detector is densely scanned across an image with or

without pedestrians and nearby detections merged using non maximal suppression (NMS),

corresponding to the miss rate against False Positive Per Image (FPPI).

The per-window evaluation can avoid NMS, however, it does not measure errors

caused by detecting at incorrect scales, positions or false detections arising from body

parts [11]. While the per-image evaluation method takes into consideration of all the

impact factors. In addition, our experiment comparisons are mainly under 10

-4

FPPW and

10

0

FPPI, which is adopted by most evaluation schemes in pedestrian detection.Fig. 5. Comparisons between MDST and CSS. (a) The per-window evaluation result. (b) The perimage evaluation result.

Fig. 6. Comparisons between MDST+HOG and CSS+HOG. (a) The per-window evaluation result.

(b) The per-image evaluation result.

For all subsequent experiments, we use the stochastic optimization based linear SVM

[12], i.e., Pegasos, to train the detectors, due to the large number of training examples.

During the training procedure, one round of retraining (bootstrapping) protocol is utilized

as Dalal et al. suggested in [4].

5.1   Evaluation of color space

In Figs. 4(a) and 4(b), we plot the performance of HLC on various color spaces according

to the per-window and per-image evaluations. This figure clearly shows that the

perspective of describing colors has great influences on the performance.

Firstly, the performance of normalized RG, normalized HS and normalized UV [8]

are all worse than the corresponding RGB, HSV and YUV. According to the fact that the

human eyes have three different types of color sensitive cones [20], the response of the

eyes is best described in terms of three "tristimulus values". Therefore,  the intensity

attribute of a color space, ignored by normalized color space, may be critical to describe

pedestrian.Fig. 7. The first row is the detection results of HOG. The second row is the detection results of

HOG-CSS (HSV) and the third row corresponds to HOG-MDST (CIE-Lab) at FPPI = 10

0

.

Secondly, the four best performed spaces are ranked in a descendent order, CIE-Lab,

CIE-LUV, HSV and HSI. The color spaces in TV system are not as discriminative as any

one of the four ones. On the contrary, CIE-based color spaces (CIE-Lab and CIE-LUV)

are designed to approximate human vision  [19]; HSV and  HSI are  relevant  to the

perception of human eyes [21]. Therefore, the color spaces，CIE-Lab, CIE-LUV, HSV

and HSI, associate with the human perception, and  achieve better performance  for

detection.

5.2    The performance of MDST

To consider the influence of the color spaces on descriptors, we plot the per-window

and per-image evaluation curves of the MDST in Fig.  5. Not surprisingly, the

performances of the MDST on four color spaces  are consistent with the results of our

color space evaluation experiment. Therefore, CIE-Lab/CIE-LUV color spaces  could be

the best ones for pedestrian detection.

In these two Figs. 5(a) and 5(b),  the performances of MDST  are better than CSS

(HSV as suggested in [8]), which is the current state-of-the-art color descriptor. In terms

of computational cost, the dimension of MDST is 1,536, while the dimension of CSS is

8,128 for a 128x64 window. Thus,  the MDST is a better color descriptor for its lower

computational cost and better performance.

We will evaluate the augmented HOG-MDST feature to study whether the two

descriptors can complement with each other or not, because Histogram of Oriented

Gradients (HOG) [4] is the most successful shape  descriptor in pedestrian detection. In

Figs. 6(a) and 6(b), it can be seen that MDST raises detection rate 4% at 10

-4

FPPW and

6% at 10

0

FPPI, comparing with HOG. On the other side, the performances of different

color spaces are also consistent with the results of color space evaluation  under 10

-4

FPPW and 10

0

FPPI.Fig. 8. The average feature map of the 12 templates for INRIA dataset

In the comparison between MDST and CSS, the MDST combined with HOG has

better performance than CSS. In our experiment, the HOG-MDST (CIE-Lab) can achieve

86%  detection rate at  10

0

FPPI; while the HOG-CSS (HSV) feature can only achieve

83.5% detection, raising 4.5%. For a more intuitive comparison, we show the detection

results of HOG, HOG-CSS and HOG-MDST (CIE-Lab) in Fig. 7. Fig. 7(1) indicates that

MDST has no negative effect on detection; while from Figs. 7(2) and 7(3), we can get that

MDST has a superior accuracy than CSS in complex scenes.

5.3   Further discussions on MDST

The average feature maps of INRIA dataset are illustrated in Fig. 8. These average feature

maps (1) ~ (12) correspond to the result of templates (1) ~ (12) in Fig. 3(c), respectively.

These figures capture the coarse boundary around pedestrians.  The color cues achieve

translation invariance locally, because of the max-pooling used in these templates.

In addition, from Figs. 5(a), 5(b), 6(a) and 6(b), we find an interesting phenomenon,

that is, the MDST(CIE-Lab) on its own  achieves 18% higher  accuracy than CSS(HSV)

under FPPI; while, the difference between HOG-MDST(CIE-Lab) and HOG-CSS(HSV)

is just around 2% at FPPI=1. There may be some redundancies between HOG and MDST,

because MDST uses color cues to capture pedestrian boundary. However, MDST derived

from color cues still provides complementary information for shape-based features.

6      Conclusions

In this paper, our experiment justifies the role of color in object detection, and shows

color cues play an important role. First,  the typical color spaces are  systematically

evaluated for pedestrian detection. The results of our evaluation experiments indicate that

the choice of color spaces has a great influence on performance.  CIE-Lab/CIE-LUV

spaces, for pedestrian, are the most suitable color spaces. Secondly, the performance of

the MDST shows that max-coding scheme can effectively capture the local boundary

information and outperform the state-of-the-art.

In future work, we plan to evaluate MDST on more different objects, e.g., car, cat,

house [16], and explain more insights why max-coding scheme is efficient for color cues.Acknowledgements. This work was supported in part by National Basic Research

Program of China (973 Program): 2009CB320906, in part by National Natural Science

Foundation of China: 61025011, 61035001 and 61003165, and in part by Beijing Natural

Science Foundation: 4111003.

References

1. Viola, P., Jones, M., Snow, D.: Detecting pedestrians using patterns of motion and appearance.

In: 9th IEEE International Conference on Computer Vision, pp. 734--741( 2003)

2. Wojek, C., Walk, S., Schiele, B.: Multi-Cue Onboard Pedestrian Detection. In: 23rd IEEE Conf.

Computer Vision and Pattern Recognition, vol. 1, pp.794--801(2010)

3. Geronimo,  D.,  Lopez,  A., Sappa,  A.:  Survey of Pedestrian Detection for Advanced Driver

Assistance Systems. In: IEEE Transactions on Pattern Analysis and Machine Intelligence(2010)

4. Dalal, N., Triggs, B.: Histogram of oriented gradients for human detection. In: 18th IEEE Conf.

Computer Vision and Pattern Recognition, vol.1, pp. 886--893( 2005)

5. Maji,  S.,  Berg,  A. C., Malik,  J.: Classification Using Intersection Kernel Support Vector

Machines is efficient. In: 21th IEEE Conf. Computer Vision and Pattern Recognition(2008)

6. Felzenszwalb,  P.,  McAllester,  D.,  Ramanan,  D.: A Discriminatively Trained, Multi-scale,

Deformable Part Model. In: 21th IEEE Conf. Computer Vision and Pattern Recognition(2008)

7. Schwartz,  W.,  Kembhavi,  A.,  Harwood,  D.,  Davis,  L.: Human detection using  partial least

squares analysis. In12th IEEE International Conference on Computer Vision, pp. 24--31(2009)

8. Walk,  S.,  Majer,  N.,  Schindler,  K.,  Schiele, B.: New features and Insights for Pedestrian

detection. In: 23rd IEEE Conf. Computer Vision and Pattern Recognition, pp.1030--1037(2010)

9. Dollar, P., Tu, Z., Pernoa, P., Belongie, S.: Integral channel features. In: 20th British Machine

Vision Conference(2009)

10. Van de Sande, K. E. A., Gevers, T., Snoek, C. G. M.: Evaluation of color descriptors for object

and scene recognition. In: 21th IEEE Conf. Computer Vision and Pattern Recognition(2008)

11. Dollar,  P.,  Wojek,  C.,  Schiele,  B.,  Perona,  P.: Pedestrian Detection: A Benchmark. In22nd

IEEE Conf. Computer Vision and Pattern Recognition (2009)

12. Shalev-Shwartz, S., Singer, Y., Srebro, N.: Pegasos: Primal Estimated sub-GrAdientSOlver for

SVM. In: International conference on Machine learning (2007)

13. Rowley,  H.,  Baluja,  S.,  Kanade,  T.: Neural network-based face detection. In: IEEE

Transactions on Pattern Analysis and Machine Intelligence (1998)

14. Viola, P., Jones, M.: Rapid object detection using a boosted cascadeof simple features. In14th

IEEE Conf. Computer Vision and PatternRecognition, volume 1, pp. 511--518 (2001)

15. Huang,  C.,  Ai,  H.,  Li,  Y.,  Lao,  S.:  Vector boosting for rotation invariantmulti-view face

detection. In: 10th IEEE International Conference on Computer Vision, pages 446--453 (2005)

16. Everingham, M., Van~Gool, L., Williams, C. K. I., Winn, J., Zisserman, A.: The Pascal Visual

Object Classes (VOC) Challenge. In: International Journal of Computer Vision, jun (2010)

17. Wikipedia for NTSC information, http://en.wikipedia.org/wiki/NTSC

18. Wikipedia for PAL information, http://en.wikipedia.org/wiki/PAL

19. Wikipedia for CIE, http://en.wikipedia.org/wiki/International_Commission_on_Illumination

20. Ng, J., Bharach, A., Zhaoping, L.: A survey of architecture and function of the primary visual

cortex. In: Eurasip Journal on Advances in Signal Processing (2007)

21. Wikipedia for HSL and HSV information, http://en.wikipedia.org/wiki/HSL_and_HSV

22. Gevers, T., Smeulders, A.: Color Based Object Recognition. In :Pattern Recognition, Volume

32, Pages 453--464 (1997)