A Parallel Context Model for Level Information in

CABAC

Min Gao, Xiaopeng Fan, Qiang Wang, Debin Zhao

Department of Computer Science and Technology

Harbin Institute of Technology

Harbin, China

mgao.hit.vilab@gmail.com,{fxp, dbzhao}@hit.edu.cn

Wen Gao

School of Electronic Engineering and Computer Science

Peking University

Beijing, China

wgao@jdl.ac.cn

Abstract—Context-adaptive binary arithmetic coding (CABAC)

is one of the most time-consuming modules in H.264/AVC

decoder. A potential way to accelerate CABAC is by

parallelization. However, the context modeling process for level

information in CABAC is highly serial in nature and can not be

parallelized in the coefficient level. In order to improve the

throughput of CABAC, in this paper we present a parallel

context model for level information. The key feature of the

model is to use the total number of the significant coefficients

and the scanned position of the current significant coefficient in

the quantized transform coefficient block as the context

information. Since the context information is independent of the

previously decoded significant coefficients, parallel decoding in

coefficient level is achieved. In experiments, the proposed

context model achieves the similar compression efficiency as the

CABAC.

I. INTRODUCTION

The processes in context adaptive binary arithmetic coding

(CABAC) consist of the following three elementary steps: (1)

binarization: the non-binary valued syntax elements need to be

mapped into a sequence of binary decisions, so-called bins, by

the variable length coding method. (2) Context model: in the

context model of CABAC, the selection of the context is

determined by the previously decoded significant coefficients,

and the probability used for coding the next bin is updated

according to the value of the current coded bin. (3) Binary

arithmetic coding: the arithmetic coding is based on the

interval subdivision principle. The range, value and offset

used to determine the interval, on which the coded bin value is

identified uniquely, is updated in a serial fashion.

From the above description, the process of CABAC is

serial in nature. That will make CABAC engine run at

extremely high frequencies in order to decode high bit rate

video bit-stream and sometimes may be not feasible in the

worst case.

To improve the decoding throughput of CABAC, a lot of

parallel entropy coding techniques are proposed. An Nbins/cycle coding (NBAC) was introduced in [2], which

decodes N bins in one cycle to achieve N-fold improvement in

throughput. PIPE/V2V schemes were proposed in [3] and [4],

in which a parallel bin decoding scheme is employed. The

NBAC/PIPE/V2V schemes reduce the serial dependency in

binary arithmetic coding (BAC) block.

The context model process may be the bottle-neck of

CABAC, when increasing the throughput of BAC block. So

some parallel context models are proposed. Some parallel

context models for coefficient sign, significant coefficients,

and significant map are proposed in [5].And a coding order

that groups the significant map and the last significant map

according to their contexts is proposed in [6]. Besides, a

context model having the trait of parallel orientation for

variable length coding is proposed in [7].

However, the context modeling process for level

information in CABAC is still serial, for the selection of the

context for the current bin is determined by the previously

coded significant coefficients.

In this paper, we reexamine the CABAC scheme and

developed a new context model for level information in

CABAC, such that the context modeling of each level in a

block is parallel. The proposed context technique, in terms of

coding efficiency, is similar to the original CABAC scheme in

H.264/AVC.

II. OVERVIEW OF THE CONTEXT MODEL FOR SIGNIFICANT

COEFFICIENT IN CABAC

A. Decoding Process of The Syntax Element in CABAC

In CABAC [1], there are three syntax elements. The

significant map is a binary array indicating whether or not

each coefficient is significant. The last significant map is a

binary array indicating whether or not each significant

coefficient is the last significant one in the block. The level

information is the value of each significant coefficient

containing the absolute value and the sign information.

Usually, the decoding process for syntax elements in

CABAC is as follows. The significant map in the current

scanned position i is decoded to judge whether the coefficient

in the scanned position i is a significant coefficient or not. If it is a significant coefficient, the last significant map is decoded

to judge whether the significant coefficient is the last one in

the transform quantized block. After that, if the coefficient is a

significant coefficient, the level information is decoded to get

its value.

When decoding the level information, the absolute value

of the significant coefficient is a non-binary valued syntax

element, which needs to be mapped into a sequence of the

binary decisions by the binarization process UEG0 [1].

B. Context Model for Significant Coefficient in CABAC

In CABAC, the decoding of each syntax element requires

the context information. The context information in CABAC

gives the knowledge about the statistic information of the

syntax element. Different syntax elements have different

context information, and the context information is updated

during the decoding process.

The context model for the significant map and last

significant map are both the scanned position, such as a

coefficient coeff[i] scanned at position i, the context model of

its significant map and last significant map are determined as

follows:

( [ ]) ( [ ]) coeff i coeff i i

SIG LAST

                   (1)

From (1), we can see that there is no dependency between any

two significant coefficients in the context modeling.

The context models for the level information include the

model for the absolute value and the model for the sign

information.

For the absolute value, after binarization, bins with bin

index between 0 and 13 are coded by two adequate context

models.

The context of the first bin with bin index equal to 0 is

determined by (2).

4 , 1( ) 0

( , _ 0)

max(3, 1( )),

if NumLgt i

i bin index

Abscoeff NumT i otherwise











  (2)

And the context of the bins with bin index between 1 and 13 is

determined by (3).

( , _ ) 5 max(4, 1( )) i bin index NumLgt i

Abscoeff

       (3)

For all bins with bin index greater than 13 as well as sign

information, the bypass coding is used, in which the

probability is 0.5.

In the two context models just described above,

NumT1(i) denotes the accumulated number of previously

decoded levels with absolute value equal to 1, and

NumLgt1(i) denotes the accumulated number of previously

decoded levels with absolute value greater than 1. The two

counters  NumT1(i) and  NumLgt1(i) are related to the

current scan position i in the reverse scan order.

Thus the processes of updating the  NumT1(i) and

NumLgt1(i) bring about the context dependency between

levels, which make it difficult to decode the levels in

parallel.

Based on the observation, we proposed a new context

model that breaks the context dependency between levels.

III. THE PROPOSED CONTEXT MODEL FOR LEVEL

INFORMATION

It is known that the positions adjacent to the up-left corner

in the coefficient block transformed by DCT usually have

larger magnitude coefficients dual to the characteristic of

energy compact of DCT transform, and in the description

above about the context model in CABAC, the scanned

position is used as the context of the significant map and last

significant map. Thus the scanned position can be used as the

context indicator. But it is not enough. In our statistics, we

find the probability distribution of the level is different even in

the same scanned position when the total number of the

significant coefficients is different, as shown in Fig.1.

Figure.1 Probability distribution of the absolute value of the significant

coefficient at position 11 when the total number of significant coefficients N =

4 and N =10 in Football Qcif video.

Therefore, the combination of the total number of the

significant coefficients and the scanned position is used as the

context to indicate the probability distribution of the level.

The input of the binary arithmetic coding is the probability

of the bins generated by the binarization, so we use the

scanned position and the total number of the significant

coefficients as the primary context model to get the probability

distribution of the level, and then use the bin index as the

secondary context to estimate the probability of bins.

A. Primary Context

The primary context is defined on the random

variable ( , )

L

C Pos N

i

, which is defined as follows:

( , ) ( 1)

L i i

C Pos N Pos N B                                (4)

Where  Pos

i

represents the scanned position of the significant

coefficients in a DCT coefficient block (here the scanned

position is numbered in zig-zag scanning order),

and 0 Pos B

i

  .  N represents the total number of the

significant coefficients in a DCT coefficient block

and1  N B  , and B represents the number of the coefficients

including the zero coefficients in a DCT coefficient block. Equation (4) indicates that the range of  ( , )

L i

C Pos N is

between 0 and

2

B 1 for a DCT coefficient block with size

equal to B. Take  4 4 block as an example,  ( , )

L i

C Pos N can

have 256 different values. To balance the model accuracy

against the model cost and avoid the context dilution problem,

we quantize the context by using the distance  DAB

between

the probability distribution of the level under different

contexts defined by (5).

2

( ( | , ) ( | , )) AB A A A B B B

l

D p L l Pos N p L l Pos N            (5)

Where ( | , ) p L l Pos N  represents the probability of the level

L equal to l under the context ( , ) Pos N .

In our implementation, the number of the primary context

is reduced to four according to the statistics on the typical

video sequences by using the k-means cluster algorithm.

B. Secondary Context

To estimate the probability of the bins, the secondary

context is designed under each primary context.

Combined with the binarization process of UEG0, we can

calculate the probability of the bin  p j ( )

bin

with its bin index

j using (6), if we know the probability distribution of

level ( | , ) p L Pos N under some context. Then the probability

of Least Probable Symbol (LPS) ( ) LPS

p j and the value of

Most Probable Symbol (MPS)  ( ) MPS

val j can be inferred from

p j ( )

bin

by (7) and (8).

1

0

( | , )

( )

1 ( | , )

bin j

k

p L j Pos N

p j

p L k Pos N









  

(6)

( ) min( ( ),1 ( )) LPS LPS LPS

p j p j p j                         (7)

1 , ( ) 0.5

0 ,

( )

bin

MPS

p j

otherwise

val j

 





                              (8)

Thus we can use the bin index as the secondary context,

and the context model process of the bin generated by the

significant coefficient at the scanned position  i can be

described as follows: firstly, we get the probability distribution

of level information according to the scanned position i and

the number of the significant coefficients N in the quantized

transform coefficient block, then combined with the bin index

j of the current bin, we can get the probability of the LPS and

the value of the MPS of the current bin.

C. Analysis of The Parallelism

The proposed context model breaks the context

dependency between the successive significant coefficients,

thus the context modeling process for the levels can be

implemented in parallel. This subsection quantitatively

analyzes the data throughput by the number of the basic

operations used in the original and proposed decoding

schemes for the level.

The decoding scheme of the significant map and last

significant map is the same as CABAC, in the following we

mainly focus on the decoding of the level.

We assume that there are  N significant coefficients in a

quantized transform coefficient block. And the absolute value

of the significant coefficient is denoted by L. We also assume

that there is only one binary arithmetic decoder; it means that

the binary decoding process for all bins is serial.

TABLE I:  BASIC OPERATIONS OF THE DECODING PROCESS

index Basic operation Time cost

1 Add/Subtract  1

2 Shift 1

3 Table lookup 1

4 Compare (ie. a>b) 1

5 Logical and (&) 1

6 Decode one bit 3

TABLE II: THE NUMBER OF BASIC OPERATIONS IN THE

DECODING PROCESS FOR A LEVEL

Module

Basic operations

1 2  3  4  5 6

original

Context 1  1|2 1|2

Decoder L L    L L

proposed

Context  1

Decoder L L    L L

Table I list all the basic operations in the original and

proposed decoding process for the level information, and the

time cost of each basic operation. The basic operation of

decoding one bit consists of two subtractions to update the

range of the interval and the state of the arithmetic decoder

and a table look-up to update the probability for the next bin.

Table II lists the modules of the original and proposed

schemes, and gives the number of the basic operations to

decode a level in each module. If L  1, there are 2 context

modeling processes in the original decoding scheme.

Thus we can calculate the time cost to decode a block of

the original scheme Toriginal

and the proposed scheme Tproposed

according to the Table I and Table II by (10) and (11).

1, 1

0,

If L

Y

otherwise

 

 



(9)

1 1

3 2 ( ) 6

N N

original k k

k k

T N Y L

 

                         (10)

1

1 6

N

proposed k

k

T L



                            (11) Since the data throughput TP is inversely proportional to

the time cost, the data throughput improvement  TP

[%] of the

proposed one relative to the original is calculated by (12).

original proposed

TP

proposed

T T

T



                          (12)

IV. EXPERIMENTAL RESULTS

In this section, we present the coding performance and the

data throughput improvement of the proposed context model

relative to the original CABAC.

The experiment is done at JM17.2 under the main

configuration file. The frame structure is IBBPBBP mode and

Transform8x8Mode is disabled. The value of QP for B

pictures is set to QP (I/P) + 2, where the value of QP for I, P

pictures is set to 16, 20, 24, and 28. The test sequences include

Football,  Foreman, and  News in QCIF format, and  Bus,

Football, and Tempete in CIF format, and City, Harbour and

Ice in 4CIF format. In these test sequences, News in QCIF

format, Tempete in CIF format and Ice in 4CIF format are not

in the training set.

A. Coding Performance

TABLE III: CODING PREFORMANCE

Seq

BD-PSNR[dB] BD-Rate[%]

Football@QCIF 0.012 -0.135

Foreman@QCIF -0.006 0.112

News@QCIF 0.012 -0.173

Bus@CIF -0.005 0.092

Football@CIF 0.017 -0.271

Tempete@CIF -0.022 0.383

City@4CIF -0.007 0.202

Harbour @4CIF 0.019 -0.380

Ice@4CIF 0.003 -0.091

Average 0.0026 -0.029

From table III, it can be seen that the proposed context

model has the same coding efficiency as the original one. The

average bit rate (BD-Bit Rate) is decreased 0.029% relative to

the original one.

B. Data Throughput Improvement

From the statistics of the test sequences, we get the

probability distribution of the total number of the significant

coefficients  p N( ) and the conditional probability of the level

under the total number of the significant coefficients

p L l N ( | )  , the mean of the  Tproposed

, Toriginal

can be

calculated by (13) and (14) .

16

1

( ) 1 6 ( ) ( | )

proposed

N l

E T Nlp N p L l N



               (13)

16 16 1

1 1 0

16

1

( ) 3 ( ) 2 ( ) ( | )

6 ( ) ( | )

original

N N y

N l

E T Np N Nyp N p Y y N

lNp N p L l N

  



     

   

(14)

( ) ( )

( )

( )

original proposed

TP

proposed

E T E T

Avg

E T



                   (15)

Thus, the average data throughput improvement to decode

a quantized transform block under each QP can be calculated

by (15), as shown in table IV.

TABLE IV: DATA THROUGHPUT IMPROVEMENT [%] TO DECODE A

BLOCK

QP

Seq

16 20 24 28

Football@QCIF 23.8 27.9 31.6 34.5

Foreman@QCIF 27.2 30.0 32.7 34.9

News@QCIF 18.4 21.5 24.2 27.4

Bus@CIF 27.5 29.9 31.8 33.8

Football@CIF 26.8 30.0 32.6 34.6

Tempete@CIF 28.5 31.2 32.8 34.7

City@4CIF 35.5 35.5 34.9 35.8

Harbour @4CIF 30.9 33.7 34.6 35.2

Ice@4CIF 31.93 32.4 32.5 34.2

Average 27.847 30.233 31.967 33.900

V. CONCLUSION

The paper presents a new context model for level in

CABAC, which can parallelize the context modeling process

for level. From the experimental results, the new context

model has the similar compression efficiency with CABAC

and the average data throughput improvement to decode a

quantized transform block is between 27.847% and 33.900%

relative to the original one under the assumption that there is

only one binary decoder. If there is more than one binary

decoder, the more data throughput improvement is achieved.

VI. ACKNOWLEDGEMENTS

This work was partly supported by the National

Science Foundation of China, 60736043 and the Major State

Basic Research Development Program of China, 973

Program 2009CB320905。

VII. REFERENCES

[1] Detlev Marpe, HeikoSchwarz, and Thomas Wiegand, “Context-Based

adaptive binary arithmetic coding in H.264/AVC video compression

standard,” IEEE Transaction on circuits and systems for video

technology, vol. 13, pp. 620-636, July 2003.

[2] V. Sze and M. Budagavi, “Parallel CABAC,” ITU-T SG 16/Q.6

Doc.COM16-C334. Geneva, Switzerland, April 2008.

[3] M. Winken et. al, “Video coding technology proposal by Fraunhofer

HHI,” JCTVC-A116, Joint Collaborative Team on Video Coding

meeting. Dresden, Germany, Apirl 2010.

[4] D. He,  G. Korodi, G. Martin-Cocher, E. h. Yang, X. Yu and J. Zan,

“Video coding technology proposal by Research Motion,” JCTVCA120, Joint Collaborative Team on Video Coding meeting. Dresden,

Germany, Apirl 2010.

[5] Madhukar Budagavi and Mehmet Umut Demircin, “Parallel context

processing techniques for high coding efficiency entropy coding in

HEVC,” JCTVC-B088, Joint Collaborative Team on Video Coding

meeting. Geneva, Switzerland, July 2010.

[6] Dake He, Gergely Korodi and Gaelle Martin-Cocher, “Improving

throughput for V2V coding in HEVC,” JCTVC-B036, Joint

Collaborative Team on Video Coding meeting. Geneva, Switzerland,

July 2010.

[7] Q. Wang, D. Zhao, W, Gao and S. Ma, “High efficiency context-based

variable length coding with parallel orientation,” Proc. PCM’05. Jeju

Island, Korea, Nov 2005