A LOW BIT RATE VOCABULARY CODING SCHEME FOR MOBILE LANDMARK SEARCH

Rongrong Ji

⋆†

Ling-Yu Duan

⋆

Jie Chen

⋆

Hongxun Yao

† Wen Gao

⋆†

⋆

Institute of Digital Media, Peking University, Beijing 100871, China

†

Visual Intelligence Laboratory, Harbin Institute of Technology, Heilongjiang, 150001, China

ABSTRACT

We present a low bit rate vocabulary coding scheme in the

context of mobile landmark search. Our scheme exploits location cues to boost a compact subset of visual vocabulary,

which is discriminative for visual search and incurs low bit

rate query for eﬃcient upstream wireless transmission. To

validate the coding scheme, we have developed mobile landmark search prototype systems within typical areas including Beijing, New York City, Lhasa, Singapore, and Florence.

Our system maintains a single vocabulary in a mobile device, which can be eﬃciently adapted with the location information of city-scale mobile users. Thus multiple downloading of large vocabulary is completely avoided for normal city

tourists. In landmark search domain, we have reported superior performance over the state-of-the art works in compact

image descriptors or signatures [2][4][5].

Index Terms— landmark search, mobile visual search,

visual vocabulary, boosting, compact visual descriptor

1. INTRODUCTION

Recent years have witnessed a great popularization of camera

embedded mobile devices in our daily lives. With the ever

growing wireless Internet services, there are great potentials

for mobile landmark search with a wide range of applications.

Generally speaking, most existing mobile landmark search

systems follow a client-server architecture. A remote server

maintains a large scale landmark database, where landmark

photos are often tagged with GPS or human labeled locations.

Near-duplicated search is applied with an inverted indexing

mechanism, typically based on scalable bag-of-words models [1][8][9]. In online search, mobile users take a photo as

his landmark query, which is transmitted to the remote server

to identify its corresponding landmark. Consequently, its geographical location, photographing viewpoint, together with

its related tourism and even commercial information, could

be returned to the mobile user as query results.

In a typical scenario, the query photo transmission from

the mobile device to the remote server is over a bandwidthconstrained wireless network. Undoubtedly, sending an entire

image is time consuming, which would greatly degenerate the

mobile search experiences. Arising from the ever growing

Fig. 1. The developed mobile landmark search system.

mobile computing power, research eﬀorts have been devoted

to directly extracting landmark descriptors on a mobile device

for the subsequent low cost query transmission. Comparing

with previous works in compact local descriptors e.g. SURF

[14] and PCA-SIFT [15], more recent works in [2][3][4][6]

aim to achieve compression rates that are suitable for wireless

transmission in mobile visual search scenarios.

The ﬁrst group of works come from directly compressing

the local visual descriptors. For instance, Chandrasekhar et

al. proposed a Compressed Histogram of Gradient (CHoG)

[4] for compressive local feature description, which adopts

both Huﬀman Tree and Gagie Tree to describe each interest

point using approximate 50 bits. The work in [6] compressed

the SIFT descriptor with Karhunen-Loeve Transform, which

yields approximate 2 bits per SIFT dimension. Tsai et al. [13]

proposed to transmit the spatial layouts of interest points to

improve the discriminability of CHoG descriptors.

The second group of works transmits the bag-of-features

[2][3] instead of the original local descriptors, which gains

much higher compression rates without much lost of discriminability. Chen et al. proposed to compress the sparse bag-offeatures [2] by encoding position diﬀerence of non-zero bins.

It produced an approximate 2KB code per image for a vocabulary with 1M words. The work in [3] further compressed the

inverted indices of vocabulary tree [1] with arithmetic coding

to reduce the memory cost in a mobile device.

While compressing bag-of-features serves as a promising

solution for low cost wireless transmission, previous works

[2][3] still demand 2KB to 4KB visual descriptors per image.

In an unstable wireless network, such cost would still delay

the subsequent similarity ranking and results returning. In

addition, two key issues remain ignored in the state-of-the-art

compact visual descriptor design [2][3][4][6].

Location Insensitive Compression: The state-of-theart works in compressive landmark descriptors [2][3][4][6]Fig. 2. The proposed vocabulary coding pipeline for low bit rate wireless transmission.

solely rely on the visual content of a query photo, regardless

of its location context that can further improve the compression rate. On the contrary, more and more landmark photos

are associated with ever increasing geographical tags like

GPS or human labeled information [9][8][11]. Diﬀerent geographical locations (e.g. diﬀerent cities) often produce their

specialized visual appearances, which should be incorporated

into the design of eﬀective compression strategy.

Vocabulary Generality: Targeting at real-world landmark search applications, while maintaining a single vocabulary at the worldwide scale cannot obtain satisfactory

performance, current works prefer to maintain a vocabulary

per city [9][10] to ensure high recognition rates. Hence in

online search, when a mobile user enters a city, his mobile

device has to load the corresponding vocabulary, which is inconvenient and extremely time consuming for mobile users.

In this paper, we present a location aware vocabulary coding scheme. In each city, we compress the vocabulary model

via a vocabulary boosting strategy, which makes use of the

most frequent landmark queries in the city to learn a compact yet discriminative vocabulary. Once a mobile user enters

a city, the server transmits a downstream supervision (i.e., a

compact BoW boosting list), which ”teaches” the mobile device to transform the original vocabulary into a very compact

one. With this technique, we have successfully developed a

mobile landmark search prototype system, providing search

services in Beijing, New York City, Lhasa, Singapore, and

Florence (Snapshot in Figure 1). Quantitative comparisons

with state-of-the-arts works in compact visual descriptor and

signature [2][4][5] will be provided subsequently.

2. LOCATION AWARE VOCABULARY CODING

SVT Model for Scalable Search: Towards eﬃcient landmark search in a million scale database, the Scalable Vocabulary Tree (SVT) [1] is well exploited in previous works

[2][3][8][9]. SVT uses hierarchical k-means to partition local

descriptors into quantized codewords. A H-depth SVT with

B-branch produces M = B

H

codewords, and the scalable

search typically settles H = 6 and B = 10 [1]. Given a query

photo Iq with local descriptors Sq = [S

q

1

, S

q

2

, ..., S

q

J

], SVT

quantizes Sq by traversing in the vocabulary hierarchy to ﬁnd

the nearest codeword, which converts Sq to a BoW signature Vq = [V

q

1

, V

q

2

, ..., V

q

M

]. In search, desirable ranking aims

to minimize the following ranking lost with respect to the

ranking position R(x) of each photo Ix in a n-photo database:

LostRank =

∑N

x=1

R(x)Wx||Vq, Vx||Cosine (1)

where TF-IDF weighting is calculated similar to its original

form [16] in the document retrieval as:

Wx = [

n

x

1

n

x

× log(

N

NV1

), ...,

n

x

M

n

x

× log(

N

NVM

)] (2)

n

x

denotes the number of local descriptors in Ix; n

x

Vi

denotes

the number of local descriptors in Ix quantized into Vi

; N denotes the total number of images in the database; NVi

denotes

the number of images containing Vi

;

n

x

i

n

x serves as the term

frequency of Vi

in Ix; and log(

N

NVi

) serves as the inverted document frequency of Vi

in the database.

Modeling User Query Logs as Training Data: For a

given city containing n landmark photos [I1,I2, ...,In], we collect a set of user query logs containing photos [I

′

1

,I

′

2

, ...,I

′

nsample

],

which outputs the following ranking list:

Query(I

′

1) = [A

1

1

, A

1

2

, ..., A

1

R

]

... = ...

Query(I

′

nsample

) = [A

nsample

1

, A

nsample

2

, ..., A

nsample

R

]

(3)

A

j

i

is the ith returning of the jth query. We expect to still

obtain [A

j

1

, A

j

2

, ..., A

j

R

] for each jth query using a more compact vocabulary. Therefore, above queries and returning are

treated as ground truth in our subsequent boosting training.

Location Aware Vocabulary Boosting: We deal with vocabulary coding as an AdaBoost based codeword selection:

The weak learner is each single codeword, and learning is to

minimize the ranking discriminability lost with a minimized

coding length. We ﬁrst deﬁne [w1,w2, ..., wnsample

] as an error

weighting vector to the nsample in the user query log, which

measures the ranking consistency lost in the codeword selection. We then deﬁne the encoded vocabulary as C ∈ RK,

which is obtained from the original vocabulary V ∈ RM via

C = MT

V, where MM×K is a dimension reduction transform

from RM to RK. In the vocabulary boosting, MMT

is a diagonal matrix, where each non-zero diagonal position deﬁnes a

codeword selection/non-selection. At the tth iteration, we got

the current (t − 1) non-zero diagonal elements in MMT

. To

select the next tth discriminative codeword, we ﬁrst estimate

the ranking preservation of the current MMT

as:

Lost(I

′

i) = w

t−1

i

∑R

r=1

R(A

1

r

)WA1

r

||Mt−1

CI

′

i

, VAi

r

)||Cosine (4)Algorithm 1: Location Aware Vocabulary Boosting

1 Input: bag-of-words signatures V = {Vi}

n

i=1

; user query logs

{Query(I

′

r)}

R

r=1

; Boosting threshold τ; error weighting vector

[w1, w2, ...,wnsample

]; and boosting iteration t = 0.

2 Pre-Computing: Calculate LostRank

in each city using

Equation 5; Calculate

∑nsample

i=1 w

t

i

3 while {

∑nsample

i=1 w

t

i ≤ τ} do

4 Lost Estimation: Calculate LostRank by Equation 5.

5 Codeword Selection: Select Ct by Equation 6.

6 Error Weighting: Update [w1, ..., wnsample

] by Equation 7;

7 Transformation Renew: Update Mt−1

by Equation 8.

8 t + +;

9 end

10 Output: The compressed codebook Cregion = MT

V.

where i ∈ [1, nsample]; R(A

i

r

) is the current position of the originally ith returning of query I

′

i

; [w

t−1

1

,w

t−1

2

, ..., w

t−1

nsample

] is the

(t-1)th error weighting, measuring the ranking lost of the jth

query (j ∈ [1, nsample]). Then, the overall ranking lost is:

LostRank =

n∑sample

i=1

w

t−1

i

∑R

r=1

R(A

i

r

)WAi

r

||Mt−1

CI

′

i

, VAi

r

)||Cosine

(5)

the best new codeword Ct

is selected by minimizing:

Ct = arg min

j

n∑sample

i=1

w

t−1

i

∑R

r=1

R(A

i

r

)WAi

r

× ||VAi

r

, [Mt−1

+ [0, ..., pos(j), .., 0]M[0, ..., pos(t), .., 0]

T

K

]CI

′

i

||Cosine

(6)

where [0, ..., pos(j), .., 0]M is a M × 1 selection vector, which

selects the jth column into the linear projection; And the vector [0, ..., pos(t), .., 0]K is a K × 1 position vector, which maps

vj

into the new codeword Ct

. Subsequently, we update the

error weighting of each w

t−1

i

as:

w

t

i =

∑R

r=1

R(A

i

r

)WAi

r

||VAi

r

, [Mt−1

+ [0, ..., pos(j), .., 0]M[0, ..., pos(t), .., 0]

T

K

]CI

′

i

||Cosine

(7)

Also, the M at the tth round is updated as follows:

Mt

= Mt−1

+ [0, ..., pos(j), .., 0]M[0, ..., pos(t), .., 0]

T

K

(8)

The codebook boosting is stopped at

∑nsample

i=1

w

t

i

≤ τ. We summarize our Vocabulary Boosting in Algorithm 1.

3. IMPLEMENTATIONS AND RESULTS

User Interface Design: Figure 1 shows the user interface of

our mobile landmark search system, which is currently deployed on a HTC DESIRE G7 intelligent mobile phone.

Data Collection: We collected over 10 million geotagged photos from photo sharing websites of Flickr and

Fig. 3. The geographical distribution of Flickr and Panoramio

photos in Beijing. This GPS distribution can reveal users’

photographing behaviors during touring this city.

Panoramio. Our dataset covers typical areas including Beijing, New York City, Lhasa, Singapore, and Florence. Figure 3 shows the geographical photo distribution in Beijing.

Simulating User Query Logs: From the geographical

map of each city, we choose 30 most dense regions and 30

randomly selected regions. Since manually identifying all related photos of a landmark is intensive, for each of these 60

regions, we ask volunteers to manually identify one or more

dominant views. All near-duplicated landmark photos are labeled in its current and nearby regions. Then, we sample 5

images from each region to form the ground truth. It generates in total 300 user query logs for each city.

Parameters and Evaluation: From Beijing landmark

photo collection, we extract both SIFT [7] and CHoG [4] features from each photo. Then, we build a Scalable Vocabulary

Tree [1] to generate the initial Vocabulary V, which generates

a bag-of-words signature Vi for each database photo Ii

. We

use the vocabulary generated in Beijing to do search in ﬁve

cities, for each of which the boosting is carried out to build

the M transformation. We denote the hierarchical level as H

and the branching factor as B. In a typical settlement, we have

H = 6 and B = 10, producing approximate 100,000 codewords. We use Mean Average Precision at N (MAP@N) to

evaluate our system performance, which reveals its positionsensitive ranking precision in the top N positions.

Baselines: (1) Initial bag-of-words: Transmitting the entire BoW has the lowest compression rate. However, it provides the upper bound in MAP. (2) Word Frequency Compression: As the most straightforward scheme, we retain the

codewords with the top 20% highest IDF as the vocabulary

compression result. (3) Aggregating Local Descriptors [5]:

The work in [5] leverages aggregate quantization to obtain

compact signature. Its input is also the bag-of-words signature produced by the initial vocabulary V. (4) Tree Histogram

Coding [2]: Chen et al. used residual coding scheme over the

BoW histogram, which Is the most related work to ours.

Rate Distortion Analysis: We give the rate distortion

analysis in comparisons with state-of-the-art works in [2][4]Fig. 4. Compression rate and ranking distortion comparing

with [2][4][5] using our ground truth query set.

[5]. Figure 4 shows that we achieve the highest compression rates with equalized distortion (horizontal viewpoint), or

maintain the highest MAP ranking performance with equalized compression rates (vertical viewpoint).

Case Study: We discovered that some empirical queries

in our system happen to be taken at night. And some queries

occur in diﬀerent scales (from either nearby views or distant

views). There is also a common problem that queries are with

blurs (very common cases). We also selected some suboptimal queries with partial occlusions (objects or persons), as

well as photos of partial landmark views. Figure 5 shows that

our vocabulary coding can still well preserve the ranking precision, with comparisons to the Baselines (1)(4).

4. CONCLUSIONS

We have presented a novel location aware vocabulary coding scheme, which embeds location cues to boost a compact vocabulary subset for eﬀective and eﬃcient landmark

search. Our prototype system has demonstrated superior performance over state-of-the-art works in mobile visual descriptor and compact image signatures. Nowadays consumers increasingly seek relevancy in mobile technology. Mobile users

are quick to adopt location-based technology. We envision

that the location sensitive compression could bring great beneﬁts in real world mobile photo search for e-guide, such as

taking a photo and sending it to a cloud, and getting back a

guild service on landmark description, campus direction, museum introduction, and so on.

5. ACKNOWLEDGEMENTS

This work was supported in part by grants from the Chinese National Natural Science Foundation under contract No.

60902057, in part by the National Basic Research Program of

China under contract No. 2009CB320902, and in part by the

CADAL Project Program.

Fig. 5. Case study of illumination changes, scale changes,

blurred photographing, occlusions, and partial landmark

queries. Each photo on the left is the query, each line of returning results corresponds to an approach. Top: Vocabulary

Boosting; Middle: Original BoW feature or Tree Histogram

Coding [2]; Bottom: IDF Thresholding (top 20%).

6. REFERENCES

[1] Nister D. and Stewenius H. Scalable recognition with a vocabulary tree. CVPR. 2006.

[2] Chen D., Tsai S., and Chandrasekhar V. Tree histogram coding

for mobile image matching. DCC. 2009.

[3] Chen D., Tsai S., Chandrasekhar V., Takacs G., Vedantham R.,

Grzeszczuk R., and Girod B. Inverted index compression for

scalable image matching. DCC. 2010.

[4] Chandrasekhar V., Takacs G., Chen D., Tsai S., Grzeszczuk R.,

and Girod B. CHoG: Compressed histogram of gradients a low

bit-rate feature descriptor. CVPR. 2009.

[5] Jegou H., Douze M., Schmid C., Perez P. Aggregating local

descriptors into a compact image representation. CVPR. 2010.

[6] Chandrasekhar V., Takacs G., Chen D., et. al. and Girod B.

Transform coding of image feature descriptors. VCIP. 2009.

[7] Lowe D. G. Distinctive image features from scale-invariant keypoints. IJCV. 2004.

[8] Irschara A., Zach C., Frahm J., Bischof H. From SFM point

clouds to fast location recognition. CVPR. 2009.

[9] Schindler G. and Brown M. City-scale location recognition.

CVPR. 2007.

[10] Ji R., Xie X., Yao H., and Ma W.-Y. Hierarchical optimization of visual vocabulary for eﬀective and transferable retrieval.

CVPR. 2009.

[11] Crandall D., Backstrom L., Huttenlocher D., and Kleinberg J.

Mapping the world’s photos. WWW. 2009.

[12] Ji R., Xie X., Yao H., Ma W.-Y., and Wu Y. Vocabulary tree incremental indexing for scalable scene recognition. ICME. 2008.

[13] Tsai S., Chen D., Takacs G., Chandrasekhar V. Location coding for mobile image retrieval. MobileMedia. 2010.

[14] Bay H., Tuytelaars T., and Van Gool L. SURF: Speeded up

robust features. ECCV. 2006.

[15] Ke Y. and Sukthankar R. PCA-SIFT: A more distinctive representation for local image descriptors. CVPR. 2004.

[16] Salton G. and Buckley C. Term-weighting approaches in automatic text retrieval. Info. Proc. and Management. 1998.