Enhanced Line-based Intra Prediction with Fixed

Interpolation Filtering

Li Zhang, Siwei Ma, Wen Gao

Institute of Digital Media

Peking University,

Beijing, China

{li.zhang, swma, wgao}@pku.edu.cn

Xin Zhao

Key Lab of Intelligence. Information Processing

Institute of Computing Technology

Beijing, China

xzhao@jdl.ac.cn

Abstract—In this paper, a novel intra prediction algorithm,

named enhanced line-based intra prediction (ELIP), is proposed

to improve the traditional intra prediction methods for

image/intra-frame coding. Different from the existing schemes

where the interpolation filtering only depends on the intra

prediction mode, in the proposed ELIP, the linear filtering

coefficients are further refined by imposing both mode and

position dependencies. For each intra prediction mode and each

position within one block, a set of linear filtering coefficients are

obtained from off-line training using the least square method.

The proposed algorithm has been implemented in the latest

ITU-T VCEG KTA software. Experimental results demonstrate

that, compared with the intra coding scheme of KTA with new

intra coding tool enabled, up to 0.44dB additional coding gain is

achieved by the proposed method, while keeping applicable

computational complexity for practical video codecs.

Index Terms— Intra prediction, image coding, least square

method

I. INTRODUCTION

Reducing the spatial redundancies presented in an image is

the basis for image/video compression standards including

MPEG-2 [1] and H.264/AVC [2]. Intra prediction (IP) is such

a tool to represent image using prediction residual with much

lower energy, and is of great importance for compression tasks.

The development of intra prediction has passed several

decades. In MPEG-2, transform-domain intra prediction is

employed to code DC coefficients with differential prediction.

After that, researches are mainly focused on spatial-domain

intra prediction with multiple prediction modes and directions

selection [3][4][5], and a representative one is the scheme

defined in H.264/AVC [6].

In H.264/AVC, the line-based intra prediction is employed,

where the sample predictor block is created by extrapolating

the reconstructed pixels surrounding the target block along the

dominating direction. Moreover, to better capture the local

properties of video signals, for intra prediction, H.264/AVC

divides the block sizes into 4×4 (Intra4×4), 8×8 (Intra8×8) and

16x16 (Intra16×16). For both Intra4×4 and Intra8×8 modes,

nine prediction modes (i.e., eight directional modes plus one

DC mode) are employed for luminance samples. Additionally,

four prediction modes (vertical, horizontal, DC and plane

modes) are utilized for Intra16×16 luma blocks. For each case,

the encoder measures the efficiency of each candidate based

on a certain criteria, and selects the optimal one for the actual

coding. Furthermore, efforts have been made to further

improve the efficiency of intra prediction. Liu  et al. [7]

utilized two windows of reconstructed pixels from two

previous frames to train the linear prediction coefficients at

both encoder and decoder. In [8], Wang proposed a distancebased weighted prediction method to improve the prediction

efficiency of DC mode. Moreover, a weighted cross prediction

mode is also proposed in [9]. With the modified interpolation

method, the decorrelation ability is enhanced and higher

coding gain can be achieved. In [10], Marta proposed a new IP

scheme using different sets of prediction weight for each pixel

within one block, which is based on a two-pass scheme and

introduces high coding complexity and large delay.

In this paper, an enhanced line-based intra prediction

(ELIP) approach is proposed to further improve the intra

prediction accuracy. In ELIP, each pixel within the target

block is predicted using a linear weighted sum of spatially

neighboring samples. To derive the linear filtering coefficients,

the least square method is used for off-line training and the

training database is constructed with classified original

samples. Furthermore, the filtering coefficients are kept as

constant throughout the encoding or decoding process under

the consideration of computational complexity. It is noted that

different from the intra prediction method in H.264/AVC, the

linear filtering coefficients are both mode- and position-

dependent. That is, for different IP mode, samples located at

different positions within one block employ different linear

filtering coefficients. Therefore, higher prediction accuracy

can be achieved.

The rest of this paper is organized as follows. Section 2

presents the background of intra prediction. Section 3 gives a

detailed description of the proposed ELIP. Experimental

This work was supported in part by National Science Foundation (608330

13, 60803068, 61073083) and National Basic Research Program of China (973

Program,  2009CB320903).

978-1-4244-9472-9/11/$26.00 ©2011 IEEE  613results are reported in Section 4, followed by conclusions and

future work in Section 5.

II. SPATIAL INTRA PREDICTION IN H.264/AVC

In H.264/AVC, nine different spatial intra prediction

modes for 4×4 luma blocks are available, including one DC

mode and eight directional modes as illustrated in Fig. 1(a).

The prediction of a target block is derived by extrapolating the

neighboring reconstructed pixels along one specific direction

with fixed coefficients. Fig.1 illustrates 16 samples (labeled as

Ci

(i = 0~15) ) of one 4×4 block which are predicted by the

reconstructed samples of upper and left-hand reference pixels

of current block (labeled as Pj

(j = 0~13) ). For DC mode, the

prediction values of all the samples are the same. When the

upper and left-hand neighbor blocks exist, the prediction value

of Ci

can be calculated by

8

1

ˆ

( 4) 3

i j

j

C P

=

= + ∑  . (1)

For the vertical prediction mode labeled as mode 0 in Fig.

1(a), the predictor of samples Ci

(i = 0, 4, 8, 12) in the column

of the block next to the neighboring row sample with value P1,

the prediction is the value P1.

One advantage associated with such line-based intra

prediction is that it is easy for practical implementation.

However, it lacks of sufficient consideration for accurate

prediction. As pointed out in [11], the correlation between

two samples in natural images is inversely relative to their

distance. Therefore, samples at different positions within one

block should employ different prediction methods to generate

the predictor. Based on the above observation, it is motivated

to design the prediction filtering coefficients with both mode

and position adaptation.

Figure 1.  Spatial intra 4×4 prediction in H.264/AVC.

III. ENHANCED LINE-BASED INTRA PREDICTION

In this section, a brief overview of our proposed ELIP

method is presented first, and the technical details are

discussed in the following subsections, including the training

process and implementation.

A. Overview of ELIP

To restrain the increase of computational complexity as

much as possible, fixed interpolation filtering in the

conventional methods is used in the proposed ELIP. Each

sample within a target sub-block under some intra prediction

mode is predicted as a linear weighted summation of the

reconstructed samples in the left column and the above row

relative to the target block. However, there are two key

differences between ELIP and the conventional method:

1) ELIP employs different filtering coefficients for

samples located at different position within one

coding block.

2) Different reconstructed samples are used as

reference samples.

In the proposed ELIP, the predictor of the ith pixel Ci

(0 ≤

i ≤ 15) within the target sub-block can be obtained from its

neighboring samples as:

1

,

0

ˆ

( ) ( )

N

i k i j

j

C k W j P

−

=

= × ∑ . (2)

where k denotes the IP mode index. Pj

(0 ≤ j < N) represents

the jth neighboring reconstructed intensity value of the target

pixel Ci

. Wk, i

(j) is the derived linear prediction coefficient of

the  jth neighboring samples for the target pixel  Ci

under

prediction mode  k.  N represents the filter tap, that is the

number of neighboring samples utilized for prediction. For

vertical, horizontal and DC modes of Intra4×4, N is set to be 9

in our experiments and the corresponding 9 neighboring

samples for prediction are those within the left column and the

above row of the target block, labeled as P0 ~ P8 depicted in

Fig. 2(a). The 17 neighboring samples for vertical, horizontal

and DC modes of Intra8×8 are depicted in Fig. 2(b), labeled as

P0~P16. Note that the linear coefficient is mode and position

dependent. Each sample to be coded at different positions

within one sub-block or under different IP mode own variable

linear filtering coefficients. Therefore, the proposed ELIP is

able to better reduce the spatial redundancies among the target

samples and the reference samples, which can bring in higher

prediction accuracy and further coding efficiency.

Figure 2.  Reference sample definition in ELIP.

B. Off-line Training

Linear filtering coefficients Wk, i

(j) can be derived through

different ways. For example, we can apply either the average

or median filters to the neighboring samples. These methods

are easy for practical implementations but have the downside

of low accuracy. As it is well known that, the more accurate

the linear filtering coefficients are, the higher the coding

efficiency will be. To accurately derive  Wk,  i

(j), the least

square method is employed in our off-line training process.

The training process is described as follows:

C0 C1 C2 C3

C4 C5 C6 C7

C8 C9 C10 C11

C12 C13 C14 C15

P0 P1 P2

P3 P4

P5

P6

P7

P8

C0 C1 C2 C3

C8 C9 C10 C11

C16 C17 C18 C19

C24 C25 C26 C27

P0 P1 P2

P3

P4

P9

P10

P11

P12

C4 C5 C6 C7

C12 C13 C14 C15

C20 C21 C22 C23

C28 C29 C30 C31

C32 C33 C34 C35

C40 C41 C42 C43

C48 C49 C50 C51

C56 C57 C58 C59

C36 C37 C38 C39

C44 C45 C46 C47

C52 C53 C54 C55

C60 C61 C62 C63

P5 P6

P7

P8

P13

P14

P15

P16

(a) Intra4×4                                  (b) Intra8×8

0

1

3 4

7 5

6

8

C0 C1 C2 C3

C4 C5 C6 C7

C8 C9 C10 C11

C12 C13 C14 C15

P0 P1 P2

P3 P4 P9 P10 P11 P12

P5

P6

P7

P8

(a) Directional intra modes        (b) Boundary and inside samples

614Firstly, a training sequence is coded with the existing intra

prediction method. To better capture the texture information,

we utilize 8 widely used sequences in 1920×1080 format to

construct the training sequence. The first four frames of each

test sequence are extracted and construct one training

sequence, which is intra coded with rate-distortion

optimization on. To derive the linear filtering coefficients of

both Intra4×4 and Intra8×8, adaptive block-size transform is

also used in our simulation.

Secondly, sample databases for each position and each

prediction mode with sample classification are set up. Subblocks with the same IP mode based on the rate-distortion

decision will be treated as one category. Samples located in

one category at the original frame constitute one training

database. Note that we use the original samples, including

target sample  Ci

and its neighboring reference sample  Pj

,

instead of the reconstructed ones, to train a set of more

accurate filtering coefficients. To calculate the linear filtering

coefficients for each position related to one sub-block under

each IP mode in the next to be coded frame, we have to find

all the valid training samples in the training database. If the

sample in a training database can be treated as valid, two

more conditions should be satisfied besides the same IP mode

including:

1) It has the same coordinate relative to the sub-block

with the pixel to be predicted to make sure the linear

prediction is position dependent.

2) All the samples within the left column and the above

row of the sub-block must exist.

Thirdly, derive the linear filtering coefficients with the

least square method for each prediction mode and relative

position within one block. For all the valid training samples,

we approximate them as the linear weighted summation of

the neighboring samples. Take any sample Ci

for example, its

approximated value using IP mode k can be calculated as

8

1

ˆ

( 4) 3

i j

j

C P

=

= + ∑  . (3)

where Pj

represents the jth neighboring pixel values of Xi

, as

depicted in Fig. 1(b). The distortion between the actual and

the approximated value of the valid training sample Ci

under

IP mode k can be computed as

( ) ( )

2

ˆ

( ) ( ) ( ) D C k C k C k

i i i

= − .  (4)

where ( ) C k

i

denotes the actual value of sample Xi

under IP

mode  k and  ˆ

( ) C k

i

represents the approximated values

obtained by Eq. (3). Actually, ( ) C k

i

equals to Ci

under every

intra mode. Based on the above definitions, the optimal

filtering coefficients for intra mode  k  and position  i

correspond to those which minimize the distortion between

all the actual valid training sample values and the

approximated ones, which can be expressed as

( )

*

1

W( , )

( , ) argmin

m valid

N m

k i s S

W k i D s ×

∈

=

G ∑

G

. (5)

where Svalid represents the set of all the valid training samples

and sm represents the mth sample within

valid

S . According to

the least square method, the optimal prediction coefficient

vector

*

1

( , ) W k i N×

G

can be derived as

( ) ( )

1

*

1

( , )

T T

W k i P P P S N

−

×

=

G G

. (6)

where  S

G

denotes a column vector of valid training samples

with length of M. P denotes the neighboring sample matrix

for each pixel in  S

G

and it is a  M×N matrix, with  M

representing the number of valid training samples and  N

representing the number of neighboring pixels to be utilized

for each training sample.

With the above three process modules, the derivation of

linear filtering coefficients for each intra mode and each

relative position has been done. The derived filtering

coefficients will be used in the intra prediction process, and

they will not change throughout the encoding or decoding

process.

C. Implementation

Since the linear filtering coefficients derivation process is

performed with the least square method, they are not always

integers. To avoid floating-point operations,  Wk,  i

(j) is

quantized to a 16-bit integer. Equation (2) can then be

rewritten as

1

,

0

ˆ

( ) ( ( ) (1 15)) 16

−

=

= × + << >> ∑

N

i k i j

j

C k W j P . (7)

In our simulations, it is observed that for vertical,

horizontal and DC modes of Intra4×4, 9 neighboring samples

are good enough, and 17 neighboring samples are needed to

calculate the predictor for Intra8×8. Furthermore, to better

cooperate with the proposed ELIP, we update the transform

matrices for these three IP modes of Intra4×4 and Intra8×8 in

mode-dependent directional transform (MDDT) [12]. The

calculation process is the same as that in MDDT, which

utilizes the singular value decomposition (SVD) method for

off-line training.

IV. EXPERIMENTAL RESULTS

To verify the performance of the proposed intra prediction

method, the proposed ELIP is implemented on the latest KTA

software with version 2.6 [13]. Experiments are conducted on

H.264/AVC “High Profile” and all frames are coded as I

frames. In addition, the MDDT technique is enabled in both

the anchor and the proposed method in our test. The test set

covers a wide range of resolutions including QCIF (176×144),

CIF (352×288), 720p (1280×720), 1080p (1920×1080) and

1600p (2560×1600) formats. The coded frame number is 100,

60 and 30 for 720p (and below), 1080p and 1600p,

respectively. CABAC is turned on for entropy coding. The

615high complexity rate-distortion optimization is set. Although

the proposed method works only on three IP modes (vertical,

horizontal and DC) of 4×4 and 8×8 sub-block units, Intra4×4,

Intra8×8 and Intra16×16 modes are all enabled and adaptive

block-size transform is used in our test.

Eighteen test sequences covering different resolutions are

tested and listed in Table 1, where coding efficiency is

compared based on the methodology given in [13]. These

results are derived under four different QPs, including 20, 24,

28 and 32. From Table 1, it can be seen that over a wide range

of test set, our proposed ELIP achieves up to 0.44 dB coding

gain on average for these QPs. The rate-distortion

performance for sequence  Harbour in 720p format is also

shown in Fig. 3. Here “anchor” represents the result achieved

by the default intra prediction method in the KTA 2.6 software

with MDDT on. It is observed that the proposed ELIP

outperforms the anchor in the full range of bitrates.

TABLE I.  CODING GAIN OF ELIP OVER KTA WITH MDDT

Resolution  Sequence

△PSNR

(dB)

Resolution  Sequence

△PSNR

(dB)

720p

(60Hz)

City 0.30

QCIF

(15Hz)

Bus 0.17

Harbour 0.44 City 0.25

Raven 0.18 Harbour 0.40

Night 0.17

CIF

(30Hz)

Bus 0.24

1080p

(50Hz)

Crowdrun 0.18 Bike 0.27

Parkjoy 0.17 City 0.23

Wisley2 0.18 Harbour 0.40

1600p

(30Hz)

Peopleon

Street

0.21 Flower 0.27

Traffic 0.16 Tempete 0.24

Average  0.22  0.27

Figure 3.  RD curves of Harbour (720p @ 60HZ)

V. CONCLUSIONS AND FUTURE WORK

In this paper, an enhanced line-based intra prediction

algorithm is proposed to further explore the spatial

redundancies. For each IP mode, each sample within a target

block is predicted as the linear weighted sum of the

reconstructed pixels surrounding the target block. The linear

filtering coefficients are derived off-line with the least square

method and classified original samples are used to construct

the database. Experimental results demonstrate that the

proposed ELIP presents better prediction accuracy and

achieves superior coding gain with applicable computational

complexity.

In the current ELIP, only three IP modes (vertical,

horizontal, DC) of Intra 4×4 and Intra8×8 are replaced. In the

near future, extensions to the remaining intra prediction

directions will also be investigated as well as Intra16×16.

Moreover, reduction of the filter tap for lower algorithm

complexity will also be further investigated.

REFERENCES

[1] ITU-T. Information Technology - Generic Coding of

Moving Pictures and Associated Audio Information: Video.

ITU-T Recommendation H.262 | ISO/IEC 13818-2

(MPEG-2), 1995.

[2] ITU-T Recommendation H.264 and ISO/IEC 14496-10

(MPEG-4) AVC: “Advanced Video Coding for Generic

Audiovisual Services,” Mar. 2005.

[3] G. Bjøntegaard, “Coding Improvement by Using 4×4

Blocks for Motion Vectors and Transform,” in SG16/Q15.

VCEG, 3

rd

Meeting, Document Q15-C23, Dec. 1997, ITUT.

[4] D. Wang, “Improvement of H.26L Intra Block Prediction,”

ITU-T Q.6/SG16 VCEG, VCEG-L09, Jan. 2001.

[5] G. Conklin, “New Intra Prediction Modes,” ITU-T

Q.6/SG16 VCEG, VCEG-N54, Sep. 2001.

[6] T. Wiegand, G. Sullivan, G. Bjontegaard and A. Luthra,

“Overview of the H.264/AVC Video Coding Standard,”

IEEE Trans. on Circuits and Systems for Video

Technology, vol. 13, no. 7, pp. 560-576, Jul. 2003.

[7] L. Liu, Y. Liu, and E. Delp, “Enhanced Intra Prediction

Using Context-Adaptive Linear Prediction,” Proc. of

Picture Coding Symposium (PCS) 2007.

[8] S. Yu, Y. Gao, J. Chen and J. Zhou, “Distance-based

Weighted Prediction for H.264 Intra Coding,” IEEE IET

International Conference on Audio, Language and Image

Processing, pp. 1477-1480, July 2008.

[9] L. Wang, L. Po, Y. Uddin, K. Wong and S. Li, “A Novel

Weighted Cross Prediction for H.264 Intra Coding,” IEEE

International Conference on Multimedia & Expo, pp. 165-

168, May 2009.

[10] M. Karczewicz, “Improved Intra Prediction,” ITU-T

Q.6/SG16 VCEG, VCEG-AF15, April 2007

[11] J. O’Neal, JR. and T. Natarajan, “Coding Isotropic

Images,” IEEE Trans. Inform. Theory, vol. IT-23, pp.697-

707, Nov. 1977.

[12] Y. Ye and M. Karczewicz, “Improved H.264 Intra Coding

Based on Bi-directional Intra Prediction, Directional

transform, and Adaptive Coefficient Scanning,”

Proceedings of the 2008 IEEE International Conference on

Image Processing (ICIP), pp. 2116-2119, Oct. 2008.

[13] “jm11.0kta2.6,”

“http://iphome.hhi.de/suehring/tml/down- load/KTA,”

Oct. 2009.

[14] G. Bjontegaard, “Calculation of Average PSNR

Differences between RD-Curves,” ITU-T Q.6/SG16

VCEG, VCEG-M33, Apr. 20.