AUTO-REGRESSIVE MODEL BASED ERROR CONCEALMENT SCHEME FOR

STEREOSCOPIC VIDEO CODING

Xinguang Xiang

1

, Debin Zhao

1

, Siwei Ma

2

, and Wen Gao

2

1

School of Computer Science and Technology, Harbin Institute of Technology,

Harbin 150001, P.R. China

2

Institute of Digital Media, Peking University, Beijing, 100871, P.R. China

ABSTRACT

Stereoscopic video is an important manner for 3-D video

applications, and robust stereoscopic video transmission has

posed a technical challenge for stereoscopic video coding.

In this paper, an auto-regressive (AR) model based error

concealment scheme is proposed for stereoscopic video

coding to address the challenging problem. The proposed

error concealment scheme includes a temporal AR model

for independent view, and a temporal-interview AR model

for inter-view predicted view. First, appropriate motions and

disparities for lost blocks are derived. Then, the proposed

AR model coefficients are computed according to the spatial

neighboring pixels and their temporal-correlated and

interview-correlated pixels indicated by the selected

prediction directions. Finally, applying the AR model, each

pixel of the lost block is interpolated as a weighted

summation of pixels in the reference frame along the

selected prediction directions. Simulation results show that

the performance of the proposed scheme is superior to

conventional temporal error concealment methods for

stereoscopic video coding.

Index Terms—  Stereoscopic video coding, error

concealment, auto-regressive  model, temporal, temporalinterview

1. INTRODUCTION

Recent years have seen increased research efforts for

stereoscopic video coding, as stereoscopic video has a wide

variety of 3-D applications. Stereoscopic video, which

consists of video sequences of the same scene captured by

two cameras from different views at the same time, is an

important form of 3-D video. Different from single-view

video, stereoscopic video often has strong inter-view

correlations among different views. Thus the popular

stereoscopic video coding frameworks often adopt both the

disparity compensation prediction (DCP) [1] for the interview prediction and motion compensation prediction (MCP)

for the single-view prediction.

On the other hand, robust video transmission over

error-prone networks is a technical challenge for video

coding. Error concealment, which is performed at the

decoder side to fill up the lost video contents, is a major

technique to deal with the challenge. Error concealment in

the traditional single view coding has been widely exploited

[2-6]. Temporal replacement (TR) [2], which utilizes the

zero motion vector (MV) to reconstruct a lost macroblock

(MB), is a simpler error concealment scheme. A very

popular and widely accepted technique, the boundary

matching algorithm (BMA), is proposed in [3-4] to select an

optimal MV to substitute for the lost one. In [5], Chen et al.

proposed a technique which combines the overlapped

motion compensation and the side match criterion. Refined

boundary matching algorithm (RBMA) is proposed to

conceal different regions of  a lost block with different

motion vectors in [6]. However, these techniques are all

designed for single-view video coding, so they will be

inefficient if directly applied to stereoscopic video coding,

as the inter-view correlation is not considered and exploited.

To our knowledge, few works [7] have been reported

on the error concealment for  stereoscopic video coding.

How to effectively perform error concealment for

stereoscopic video coding is still an unanswered question.

Auto-regressive (AR) model [8], which is an efficient

description of random process, is able to have desirable

performance for interpolation. In this paper, utilizing the

temporal and interview correlation in stereoscopic video and

the superior property of the AR model, we propose an autoregressive (AR) model based error concealment scheme for

stereoscopic video coding. The proposed error concealment

scheme includes a temporal AR model for independent view,

and a temporal-interview AR model for inter-view predicted

view. First, the boundary matching algorithm (BMA) is

utilized to select a best motion vector (MV) and a best

disparity vector (DV) for each lost block from the prediction

vectors of available neighboring blocks. Then, we compute

our proposed AR model coefficients according to the spatial

neighboring pixels and their temporal-correlated and

interview-correlated pixels indicated by the selected best

prediction directions. Finally, applying the AR model, each

pixel of the lost block is interpolated as a weighted summation of pixels in the reference frame along the

selected best prediction directions.

The rest of this paper is organized as follows. Section 2

describes the proposed algorithm in detail. Section 3 reports

the simulation results. Section 4 concludes this paper.

2. THE PROPOSED AUTO-REGRESSIVE MODEL

BASED ERROR CONCEALMENT

The basic prediction structure of stereoscopic video coding

is shown in Fig. 1, where the left view is predicted only by

MCP, called independent view, and the right view is

predicted by both MCP and DCP, called inter-view

predicted view.

Fig. 1 The basic prediction structure of the two-view based

stereoscopic video coding

The proposed AR model aims to recover the lost data

in current frame, based on the picture data in correlated

frames from temporal and interview directions indicated by

appropriate motions and disparities. Fig.2 illustrates the

proposed AR model based error concealment scheme. We

utilize the BMA technique to select appropriate prediction

directions for the lost MB, and utilize the pixels in

neighboring MBs to derive AR model coefficients. Finally,

we recover the lost pixels by their temporal-correlated and

interview-correlated pixels with the proposed AR model.

Note that the proposed scheme is composed of a temporal

AR model for independent view, and a temporal-interview

AR model for inter-view predicted view.

2.1. Selection of prediction directions

In order to choose appropriate prediction vectors which are

used as the prediction directions for AR model, we utilize

the BMA criterion. The cost function of BMA is defined as

the absolute difference between the external boundary of the

lost MB in the current frame and the internal boundary of

the replacing MB in the reference frame, and it is

formulated as follows:

15

0

[| ( , 1) ( , )| | ( , 16) ( , 15 )|]

0 0 0 0

0

15

0

[| ( 1, ) ( , )| | ( 16, ) ( 15 , )|]

0 0 0 0

0

Cost

BM

x x

r r

P x y P x v y v P x y P x v y v

x y x y

x x

y y

r r

P x y P x v y v P x y P x v y v

x y

y y

= +

∑ − − + + + + − + + +

=

= +

+ − ∑ − + + + + − + +

=

=

x y

+

(1)

where (x0, y0) denotes the coordinate of the top-left pixel in

the lost MB, and (vx

, vy

) denotes the candidate vector. P and

P

r

denote the pixels of the current and reference frames,

respectively. For each lost MB, we can get some candidate

motion vectors and disparity vectors from neighboring

available prediction vectors. While the zero motion vector

and the zero disparity vector are also candidates. The

motion vector which results in the smallest temporal

direction cost is selected as  the best motion. Similarly the

disparity vector which results the smallest interview

direction cost is selected as  the best disparity. Note that,

only motions are selected for independent view while both

motions and disparities are selected for inter-view predicted

view.

Fig. 2 Flowchart of the proposed auto-regressive based error

concealment algorithm for stereoscopic video coding

2.2. Temporal AR model for independent view

Fig. 3 Temporal AR model for independent view

The proposed temporal AR model for independent view is

shown in Fig.3. Suppose Xc be a region of m pixels in the

current frame, and Xt

be the region of pixels in the

temporal-correlated frame along the temporal motion

direction. For each pixel

( , ) c

X i j

in the region Xc

located at (i,

j), we find its temporal corresponding pixel in Xt

, indicated

by the temporal motion vector (mvx

,  mvy

). Then we can

approximate the current pixel as a weighted summation of

pixels within a spatial window, centered on the corresponding pixel in the temporal-correlated frame. The

approximate value

( )

ˆ

, X i j

c

can be represented as

( ) ( ) ,

ˆ

, ,

R R

u R v R

X i j

c x X i u mv j v mv

t

α

= − = −

= + ∑ ∑ + + + i

y u v (2)

where α u v,

is the temporal AR coefficient located at (u, v),

and  R denotes the radius of the spatial window, thus the

window size n is  (2 1) (2 1) R R + × + .

Due to the piecewise characteristics of nature image,

we assume the AR coefficients

remain the same for all the pixels in the region. Then,

according to Eq. (2), we can obtain

, , 1 ,

( , , ,

t

α α α α = − − − − + R R R R R R … )

X X f ( )t

ˆ

c

= α (3)

where  f ( ) Xt

is a function which transfer Xt

to a  m×n

dimensional matrix. For each pixel in Xt

indicated by the

temporal motion, the function gets a spatial window

centered on the pixel.

Note that, for each pixel within the lost MB, we can

approximate its value by the proposed AR model. The

temporal motion has been selected by BMA, so we need to

compute the AR coefficients for the lost MB.

Based on the piecewise characteristics of nature image,

we assume the AR coefficients and the motion remain the

same for the lost MB and the four neighboring MBs around

the lost MB, as shown in Fig. 2. Thus utilizing the available

neighboring MBs and the motion selected by BMA, we can

compute the AR coefficients for the lost MB.

Mean squared error (MSE) criterion and the least

square (LS) algorithm are utilized to compute the AR

coefficient vectorα . For all the available neighboring MBs

we define the resulting MSE as

( ) ( )

2

2

X X X ˆ ˆ

ε c c c

= − E

(4)

Here we select the AR coefficient vector α which

results in the least

( )

2

ε Xˆ

c

u v,

as the optimum coefficients.

According to the least square (LS) algorithm, for each

coefficientα , we set

( ) ( ( ) )

2

, ,

2

X Xˆ X X

u v u v

c c c t

d E d E f

d d

α

α α

− −

= = 0

)

= + × + (2 1) (2 1) R

X c

(5)

Note that  is a  dimensional matrix, where

is the total number of pixels which is utilized for training

AR model coefficients, and  n R is the size

of spatial window. Then, according to Eq. (5) we can derive

(Xt

f m n×

m

( ) ( ) ( ) ( )

1

( X ) X ( X )

T T

t t t

α f f f

−

= (6)

Utilizing the coefficients derived by Eq. (6), we can

easily recover the lost MB according to Eq. (3).

2.3. Temporal-interview AR model for inter-view

predicted view

Fig. 4 depicts the proposed temporal-interview AR model

for inter-view predicted view. Suppose Xv

be the region of

m pixels in the interview-correlated frame along the

interview disparity direction. Then, applying the temporalinterview AR model, the approximate value  ( )

ˆ

, Xc

i j can be

represented as

( ) ( )

( )

,

,

ˆ

, ,

,

R R

c t x u v

u R v R

R R

v x y

u R v R

X i j X i u m v j v m v

X i u d v j v d v

y

u v

α

β

= − = −

= − = −

= + + + +

+ + + + +

∑ ∑

∑ ∑

i

i

u v,

(7)

where α is the temporal AR coefficient located at (u, v),

and  βu v,

is the interview AR coefficient located at (u, v).

Furthermore, we can obtain

( ) ( ) X X X ˆ

c v t

= + f g α β (8)

where  g (Xv ) is a function which transfer Xv

to a  m×n

dimensional matrix. For each pixel in Xv

indicated by the

interview disparity, the function gets a spatial window

centered on the pixel.

Suppose Ψ=( f g (X , X t

) ( v)) be a m×2n dimensional matrix,

and

( ) , , 1 , , , 1 ,

( , , , , , , , )

t

R R R R R R R R R R R R

α

ω α α α β β β = =

β − − − − + … … − − − − +

Xˆ

c

be the

temporal-interview AR coefficient vector.

Then we obtain

= Ψ ω (9)

Similarly as previous section, for each lost MB,

utilizing the motion vector and disparity vector selected by

BMA, and the available neighboring MBs, we can compute

the temporal-interview AR coefficients for the lost MB. For

all the available neighboring MBs, according to MSE

criterion and the LS algorithm, we can derive

( )

1

X

T T

ω c

−

= Ψ Ψ Ψ (10)

Utilizing the coefficients derived by Eq. (10), we can

easily recover the lost MB according to Eq. (9).

Fig. 4 Temporal-interview AR model for inter-view

predicted view

3. SIMULATION RESULTS

We utilize the H.264/AVC reference software JM 10.0 to

simulate a stereoscopic video coding system, as shown in

Fig. 1. The left view is encoded independently with MCP,

and the right view is predicted with both MCP and DCP.

Then they are transmitted to the decoder respectively. The video sequences  Race1 and  Rena are encoded using the

IPPP GOP structure for 240 frames within each view. Each

row of MB composes a slice and is transmitted in a separate

packet. The packet loss rates (PLR) at 5%, 10%, and 20% [9]

are tested in experiments. The QP is set to 28 and the first I

frame in a GOP in each view is error free for all tests. We

compare our proposed stereoscopic AR error concealment

scheme (AR) with temporal replacement (TR) method, the

error concealment method of JM (JM), which only perform

error concealment process in  the temporal direction of a

single view. For the proposed AR scheme, the radius of the

spatial window R is set to be 1.

Firstly, we assume that the independent view sequence is

transmitted correctly and the inter-view predicted view

sequence is transmitted with packet loss. Under the

condition, there’s no error propagations from the

independent view to the inter-view predicted view, thus we

can test the performance of our proposed temporalinterview AR model for the inter-view predicted view.

Table 1 shows the PSNR performance results of different

error concealment schemes for the inter-view predicted

view under the given conditions. AR has 3.70dB~6.70dB

error concealment performance improvement than TR,

1.58dB~3.32dB improvement than JM. The results indicate

that the proposed AR scheme can utilize inter-view

correlations to improve the error concealment quality for the

inter-view predicted view.

For both the independent and inter-view predicted view

sequences are transmitted with the same PLR, Table 2

shows the PSNR performance comparison of the three

different methods. AR has 3.71dB~6.05dB error

concealment performance improvement than TR,

0.62dB~1.23dB improvement than JM.

Table 1 Average PSNR (dB) performance comparison of

different error concealment schemes for the inter-view

predicted view

Video

sequence

PSNR

(dB)

Packet loss rate

5%  10%  20%

Rena

TR  35.30  32.79  30.24

JM  36.85  34.57  32.26

AR  39.00  37.32  35.58

Race1

TR  29.58  27.07  25.00

JM  33.82  31.75  29.53

AR  35.40  33.55  31.70

4. CONCLUSIONS

Robust stereoscopic video transmission has posed a

technical challenge for stereoscopic video coding. In this

paper, combining the temporal and interview correlation in

stereoscopic video and the superior property of the AR

model, we propose an auto-regressive model based error

concealment scheme which is composed of a temporal AR

model for independent view and a temporal-interview AR

model for inter-view predicted view. Applying the proposed

AR model, each pixel of the lost block is interpolated as a

weighted summation of pixels in the reference frames along

the prediction directions. Motions and disparities for lost

blocks are selected by the boundary matching algorithm.

And the proposed AR model coefficients are computed

according to the spatial neighboring pixels and their

temporal-correlated and interview-correlated pixels

indicated by the selected  best predicted directions.

Simulation results show that the proposed algorithm can

improve the performance of reconstructed stereoscopic

video sequences.

Table 2 Average PSNR (dB) performance comparison of

different error concealment schemes

Video

sequence

PSNR

(dB)

Packet loss rate

5%  10%  20%

Rena

TR  32.84  29.57  27.43

JM  35.84  32.99  30.63

AR  36.55  33.61  31.37

Race1

TR  28.49  25.71  23.98

JM  33.17  30.53  28.52

AR  34.26  31.76  29.64

5. REFERENCES

[1] M. E. Lukacs, “Predictive coding of multi-viewpoint

image sets”, Proc. IEEE ICASSP 86, pp. 521 – 524, 1986.

[2] Aign S. and Fazel K., “Temporal and spatial error

concealment technique for hierarchical MPEG-2 video

codec”, IEEE International Conference on Communications,

Vol. 3, pp.1778-1783, June 1995.

[3] W. M. Lam, A. R. Reilbman and B. Liu, “Recovery of

lost or erroneously received motion vectors”,  Proc. IEEE

ICASSP 93, pp. V417-V420, April 1993.

[4] S. Tsekeridou and I. Pitas, “MPEG-2 error concealment

based on block-matching principles”, IEEE Transactions on

Circuits and Systems for Video Technology, vol. 10, pp.

646-658, June 2000.

[5] Mei-Juan Chen, Liang-Gee Chen and Ro-Min Weng,

“Error concealment of lost motion vectors with overlapped

motion compensation”, IEEE Transactions on Circuits and

Systems for Video Technology, vol. 7, Issue 3, pp. 560-563,

June 1997.

[6] T. Chen, X. Zhang, and Y. Q. Shi, “Error concealment

using refined boundary matching algorithm”, International

Conference on Information Technology: Research and

Education, pp.55-59 Aug. 2003.

[7] S. Knorr, C. Clemens, M. Kunter and T. Sikora, “Robust

concealment for erroneous block bursts in stereoscopic

images”, Proc. of 3DPTV2004, pp.820-827, Sept. 2004.

[8] X. Wu, K. U. Barthel, and W. Zhang, “Piecewise 2D

autoregression for predictive image coding”,  Proc. IEEE

International Conference on Image Processing, pp. 901-904,

1998.

[9] S. Wenger, “Error patterns  for internet experiments”,

ITU-T SG16 Doc. Q15-I-16r1, 1999.