Sparsely Encoded Local Descriptor for Face

Recognition

Zhen Cui

1,2,3

, Shiguang Shan

1,2

, Xilin Chen

1,2

, Lei Zhang

4

1

Key Lab of Intelligent Information Processing, Institute of Computer Technology, Chinese Academy of Science (CAS), Beijing,

100190, China

2

Graduate University of CAS, Beijing, 100190, China

3

School of Computer Science and Technology, Huaqiao University, Xiamen, 361021,China

4

Department of Computing, The Hong Kong Polytechnic University, Hong Kong, China

{zcui, sgshan}@ jdl.ac.cn

Abstract—In this paper, a novel Sparsely Encoded Local

Descriptor (SELD) is proposed for face recognition. Compared

with K-means or Random-projection tree based previous

methods, sparsity constraint is introduced in our dictionary

learning and sequent image encoding, which implies more stable

and discriminative face representation. Sparse coding also leads

to an image descriptor of summation of sparse coefficient vectors,

which is quite different from existing code-words appearance

frequency(/histogram)-based descriptors. Extensive experiments

on both FERET and challenging LFW database show the

effectiveness of the proposed SELD method. Especially on the

LFW dataset, recognition accuracy comparable to the best

known results is achieved.

Keywords-local descriptor; Random-projection tree; Sparse

coding;  face verification; face identification

I. INTRODUCTION

In the past few decades, face recognition has attracted

significant attention due to its wide potential applications in

public security, law enforcement, etc. Numerous methods or

techniques have been presented as surveyed in [1], and

considerable progress had been achieved. Currently, many face

recognition systems have been able to work well under wellcontrolled conditions with cooperative users. However, as

discovered by MBGC [2] and LFW evaluation [3], face

recognition under uncontrolled environment with

uncooperative users remains a great challenge. To successfully

address this problem, how to represent faces plays the key role.

In the past decade, local descriptor based face

representation, which models image micro-patterns, has formed

a blowout [4,5,6,7,8,9,10,11,12,13,14,15], due to their

robustness to extrinsic variations. A large portion of these

methods are based on manually designed local patterns. For

example, by combining the sign of the difference of central

pixel intensity from those of its neighboring pixels, LBP [7]

implicitly encodes the micro-patterns of the input image such

as flat areas, spots, lines and edges. Since the sign is invariant

to monotonic photometric change, LBP is robust to lighting

variation to some extent. Many LBP variations or extensions

have also been proposed. Zhao and Pietikäinen extended LBP

to the spatial-temporal domain [12]. In order to make LBP

robust to random and quantization noise in near-uniform face

regions, Local Ternary Patterns (LTP) [13] have also been

proposed. By combining Gabor filtering with LBP, Local

Gabor Phase Patterns (LGBP) [9] was proposed to extend LBP

to multiple resolution and orientation. Later on, Histogram of

Gabor Phase Patterns [8] and Local Gabor XOR Pattern [14]

were further proposed to exploit the Gabor phase information.

In addition, some local descriptors originally proposed for

other object recognition tasks were also introduced for face

recognition, such as Histogram of Oriented Gradients (HOG)

[10] or SIFT [11,15]. Manually designing local pattern avoids

complicated learning process. Nevertheless creating an optimal

descriptor is non-trivial. One has to balance between the

discriminative power and the robustness against data variance.

In contrast to the above handcrafted approaches whose

patterns are predefined manually, the texton-based methods

typically learn some visual primitives as code-words from a

large number of local face image patches and utilize the

frequency of the code-words as face representation.

Considering that high-level facial semantic features consist of

those low-level micro visual structures, Meng et al. proposed

Local Visual Primitives (LVP) for modeling and recognition

[16], which learns LVP by K-means clustering. Xie et al. [17]

further applied the K-means clustering approach to patch sets

sampled from the Gabor filtered face images and then

quantized codes of each patch,  at last concatenated blockbased histograms of patterns to describe the whole face.

Ahonen et al. [18] also tried K-means cluster to build local

filter response codebook. More recently, Cao et al. [6] pointed

that quantized codes based on K-means usually tend to have

uneven distribution, so the resulting code histogram would be

less informative and less compact. So they applied Randomprojection tree [19] to replace K-means clustering.

Another recent progress in face recognition field is the

sparse representation based method. In [20], Wright et al.

proposed to recognize a face through finding its sparse

coefficients with respect to the whole training set as the

dictionary and seeking for the face whose samples result in the

smallest reconstruction error by using their corresponding

sparse coefficients. In case of multiple well-aligned samples

per person, the method reports impressive accuracy, especially

when faces are partially occluded. Zhang et al. [21]

incorporated the face labels in the dictionary-learning stage to Concatenated code

summation

Block-wise sparse

code summation

Pixel-wise sparse

code vectors

Pixel-wise sampled

intensity vectors

Sampling

template

Preprocessed

input image

y11 y12… y1w

y21 y22… y2w

... …

yh1

yh2… yhw

r

*  PCA

α11α12…α1w

α21α22…α2w

... …

αh1αh2…αhw

SELD feature

Sparse Dictionary Learnt Offline

Figure 1.  Overview of the proposed SELD-based face representation extraction

obtain an efficient dictionary that retains the representative

power while making the dictionary discriminative. Yang et al.

[22] used the image local Gabor feature for sparse

representation, and proposed an associated Gabor occlusion

computing algorithm to handle the occluded face image. Above

methods are all holistic representation based methods, thus not

as robust as local methods. Furthermore, the sparse

representation method proposed in [20] can work only for

scenario where each face has multiple enrolled face images.

Therefore, it can not be applied to face verification scenario as

evaluated by the FRGC or LFW protocol.

To address above problems, in this paper, we enhance

texton-learning based local descriptor method by introducing

sparse coding, thus propose Sparsely Encoded Local Descriptor

(SELD). Simply speaking, in our SELD method, sparsity

constraint is introduced during the local visual primitive

dictionary learning and sequent image encoding, which is

distinctly unlike K-means clustering or Random-projection tree

as in previous methods [6, 16, 17]. As is validated recently by

many researchers, sparsity implies more discriminative power

and stableness of the representation.

Another big difference of our SELD method from previous

texton-based methods [6, 16, 17] is that, our description is

sparse coefficient vector based, rather than code-words

frequency (or histogram) based. Specifically, during the image

encoding stage, the coefficient vector of the sparse coding is

computed at each image position, and then summed together to

form the local descriptor of some image blocks. Compared

with frequency (or histogram) based methods, coefficient

vector is similar to some soft clustering, thus implies more

robustness to variations in image appearance.

Compared with sparse representation method in [20], our

SELD method is a more general face representation. As a face

descriptor, our method can be easily applied to face verification

and face identification with single sample per person, which are

impossible for methods like in [20].

The proposed SELD method is extensively validated by

experiments on two face databases: the Labeled Faces in the

Wild (LFW) [3] which is designed for unconstrained face

verification, and the FERET database [23] which is used for

face identification. Especially on the LFW, besides the

comparisons of our method with previous methods based on Kmeans or Random-projection tree, we also compare with

existing state-of-the-art approaches that reported best known

results on LFW. Comparable accuracy is achieved by our

methods.

II. SPARSELY ENCODED LOCAL DESCRIPTOR

In this section, we first present the flowchart of the

proposed SELD method for face recognition. Then we describe

the critical steps of our method in detail, including how to learn

the sparse dictionary and how to sparsely encode a face image.

A. Overview of SELD for face recognition

As mentioned above, our method is essentially an enhanced

texton-based method. Therefore, it follows similar idea to bagof-words method. The main difference lies in the sparsity

constraint in dictionary learning and the non-frequency based

descriptor. Intuitively, the overall flowchart of the proposed

SELD-based face representation method is illustrated in Fig.1

and explained as follows.

As shown in Figure 1, we first align and normalize the

original images geometrically and filter it using a DoG filter to

remove both high-frequency noise and low-frequency

illumination variations. Then, at each pixel, an intensity vector

is formed by sampling its neighbor pixel’s intensity according

to a pre-defined sampling template. In the next step, the

intensity vector at each pixel is sparsely encoded with the

offline-learned sparse dictionary under non-negative constraint,

which generates a sparse code vector, i.e., the sparse coefficient

vector. With these sparse code vectors computed, the face

image is spatially partitioned into some blocks, and the sparse

code vectors in each block are summed together to form a

descriptor of the block. Next, the accumulated vectors of all the

blocks are concatenated together to form a single vector, which

is finally reduced in dimensionality by principal component

analysis (PCA) to generate the SELD feature of the input face

image. For face recognition or verification, cosine similarity of

two SELD features can be used to match two face images.

B. Sparse Dictionary Learning

Research on general over-complete dictionaries mostly

commenced over the past decade and is still intensely ongoing.

Such dictionaries bring the prosperity in the definition of a

signal representation. Given an over-complete dictionary

matrix  D=[d1,d2,…,dk

]∈R

n×K

, K>n that contains K  prototype signal-atoms, a signal y∈R

n

can be represented as a sparse

linear combination of these atoms.

In this paper, we use the K-SVD algorithm [24] to train the

over-complete dictionary. K-SVD is an iterative method that

alternates between sparse coding of the examples based on the

current dictionary and a process of updating the dictionary

atoms to better fit the data. Formally, given a training set with

N samples, K-SVD’s objective function is

2

F 0 0

,

min       s.t.  ,

i

D X

Y DX i x T − ∀ ≤ (1)

where  X=(x1,x2,…,xN) with  xi∈R

n

are the sparse coefficient

vectors for training sample yi

, k is the number of code-words in

the dictionary, and ‖·‖0  is the l0 norm.

The K-SVD algorithm has two stages: in the first stage, D

is fixed, and the above optimization problem is a search for

sparse representation with coefficients summarized in the

matrix. It may be solved by any pursuit algorithm; the second

stage is updating the dictionary together with the non-zero

coefficients. In this stage, the algorithm updates each column in

the dictionary,  dk

, and the coefficients,  xR

i

, the i-th row in X.

The objective function (1) can be re-written as

2

2

2

F

k

k k R

F

k

k R

i k

i

F i R

Y DX Y d x ⎟ − d x = E − d x

⎠

⎞

⎜

⎝

⎛

− = − ∑

≠

(2)

Then SVD is applied to Ek

and get Ek=U△V. Then, we choose

the first column of U and the first column of V multiplied by

△11

as the updated dk

,  xR

k

respectively.

With the above K-SVD method, our sparse dictionary is

learned by the following steps:

1) Preprocess each normalized image in the training face

image set by DoG filtering.

2) Sample patches of size p×p pixels from DoG filtered

images to form the patch set S. If we have N training images

and sample c patches from each image, there are c×N patches

in S. All sampled patches are normalized to zero mean and

unit length.

3) For patch set S, K-SVD algorithm is utilized to

construct the sparse dictionary Dn×K, where K is the nunber of

codewords in the dictionary.

In the above learning algorithm, one of the problems might

be how many patches should be sampled for training. In

principle, it seems that we should sample as densely as possible

to obtain a large number of patches. However, this implies very

time-consuming K-SVD. Fortunately, we empirically find that

only thousands of patches are sufficient for our purpose. So, the

patches can be sampled rather sparsely in each image.

C. SELD-based face representation

After the sparse dictionary D is learned, we then describe in

this section how to utilize it to extract SELD feature for any

input testing face image. As shown in Fig.1, given an input

image already normalized and filtered by DoG, we first sample

patches centered at each pixel and normalize the sampled

intensity vectors to zeros mean and unit length. Then, we apply

sparse coding to encode the sampled intensity vectors to sparse

code vectors.  Formally, let the sampled intensity vector at

pixel (i,j) be yij

. Its sparse code vector αij

is then computed by

the following optimization:

2

ij ij

min     . .   ( ) 0

F 1

y D s t l

α

α α λ α α = − + ≥ (3)

where ‖·‖1 is the l1 norm. As shown in (3), in our implement,

non-negative constraint is introduced to guarantee all the

entries of the sparse coefficient α non-negative. The reason we

impose this constraint is that intuitively we need an additive

combination of the code-words to represent each patch.  This is

also consistent with our sequent summation of the sparse code

vectors in each image block.

After encoding, the input image is converted to “sparse

code” map. The encoded image is then divided into an  m×n

grid of blocks. Then, we add all the nonnegative codes in each

block to form one sparse code vector for this block. Next, the

accumulated vectors of all the blocks are concatenated together

to form a single vector describing the whole face image.

If we use the concatenated vector as the final descriptor, the

dimension of the resulting face feature may be very high. A

high-dimensional feature not only results in curse of

dimensionality but also large complexity in memory and

computation. Therefore, Principle Component Analysis (PCA)

is further applied to further reduce the dimensionality and

obtain the final SELD feature.

With the extracted SELD feature, many metrics can be

used to compute the similarity or distance between two face

images for face verification by threshold or identification by

nearest neighbor. In this paper, we select the most commonly

used cosine similarity.

III. EXPERIMENTS

In order to evaluate the proposed approach, we carry out

extensive experiments on LFW benchmark [3], where we not

only compare our method with previous methods based on Kmeans or Random-projection tree but also compare with

existing state-of-the-art approaches that reported best known

results on LFW. Finally, we also compare our method with Kmeans method for face identification on FERET database [23].

A. Experimental setting

The LFW benchmark is designed for unconstrained face

verification with face images containing large variations in

pose, age, expression, race and illumination.  There are two

evaluation modes proposed by the LFW organizer: the imagerestricted and the image-unrestricted training mode. This paper

only considers the restricted mode. Under this mode, the whole

standard testing set consists of ten subsets and each subset

contains 300 same-person pairs and 300 different-person pairs.

The performance of an algorithm is measured by a 10-fold

cross validation procedure. The final average recognition rate

serves as the evaluation criterion. For face identification, we

used FERET database and its evaluation protocol to evaluate

our method.

In all experiments, DoG filters withσ1=2.0 andσ2= 2.0 are

used. The size of the sampling template is set to 5×5. Default dictionary size is set to 256. The PCA preserves 98% of the

total energy.

B. Face verification evaluation on LFW

The original size of each image in LFW is 250×250 pixels.

All face images are cropped to 80×150 pixels just by simply

cutting out the center of the aligned version images provided by

Wolf et al. [25]. In the block-wise SELD feature extraction

stage, the face images are divided into 5×10 blocks to obtain 50

summed sparse code vectors.

Experiment 1: comparison with K-Means and Randomprojection tree

The first experiment aims to validate the discriminative

power and stableness of the proposed SELD by evaluating on

LFW according to the LFW image-restricted evaluation mode.

We compare the proposed sparse dictionary learning method

with previous methods, i.e., K-means and Random-projection

tree [19]. In the experiment, 500 images are randomly selected

from the LFW training set to train the dictionary. Note that we

find the size of training set has little influence on the final

performance.

The mean accuracy curves of the three methods are shown

in Fig.2, with the horizontal axis different number of codewords in the dictionary. Meanwhile, the ROC curves of the

three methods are also plotted in Fig.3 when the number of

code-words is 256. From these two figures, it is clear that the

proposed method outperforms the other previous methods in

terms of both mean accuracy and ROC. Especially, from the

ROC curves, we can see that, our method works impressively

better than the other two methods especially when false

positive rates are small. Please note that, we have tried our best

to rigidly implement the Random-projection tree algorithm as

in the [19], but its performances are still slightly inferior to the

K-means, which seems slightly different from results in [6].

In addition, from Fig.2, we can find that the performances

of the three methods all increase with the increase of the code

number. However, to balance the computational cost, we select

256 as the default code number in our following experiments.

Figure 2.  Performance comparison vs. learning method.  We studied the

mean accuracy of the learned descriptors using three learning method: Kmeans, Random-projection tree and the proposed sparse coding with different

code number. Note that here we do not use PCA in order to reflect the

comparison essentially.

Figure 3.  Demonstrate the effects of three different encoding methods in

terms of ROC curves.

Figure 4.  The effects of removing the first R dimensions of SELD feature

generated by PCA

Experiment 2: effect of removing some leading PCA features

In the second experiment, we investigate the effects of

removing the first R dimension from the SELD feature

obtained by PCA. The reason that we focus on this point lies in

the fact that, there are large variations in the LFW images,

which implies the leading eigenvectors encode mostly

variations in lighting, pose, and other large variances rather

than those in identity. Therefore, we guess removing some of

the leading eigenvectors should lead to performance

improvement. The results are plotted in Fig.4. From the figure,

it is clear that our above-mentioned guess is validated: by

removing the first several dimensions, about 4 percents’

improvement can be achieved.

Experiment 3: fusion of multiple block-wise SELD

In above experiments, a fixed block partitioning method,

i.e., 5×10 blocks, is used to extract single SELD feature.

Intuitively, we have other choices to partition the image and

extract multiple block-wise SELD features. Thus, when

matching a pair of images, multiple similarities can be

computed and fused together by sum rule or SVM. Following

this idea, we tried five different block partitioning modes:

5×10, 4×8, 3×6, 2×4, 1×10, which is similar to the hierarchical

spatial pyramid structure [26]. We name this method as

“Multiple block-wise SELD fusion” in short.  Figure 5.  Our face verification methods compared with one of the state-ofthe-art methods in [6], which learn dictionary based on Random-projection

tree.

Figure 6.  Face verification comparison on the LFW benchmark in restrict

protocol.

In Fig.5, above method and single SELD are evaluated on

LFW under image-restricted mode and compared with one of

the best known method on this testing [6]. In Fig. 5, the method

“Single LE+holistic” means using the single best LE to

represent the holistic face, where the encoder is Randomprojection tree. The method “Multi LE+comp”, reporting the

best performance in [6], not only divides the holistic face into 9

components by component-level face alignment, but also fuses

four different encoded local descriptors to fed into linear SVM.

It also exploits pose-adaptive adjustment. In contrast, our

“Multiple block-wise SELD fusion” method only exploits

single sampling template and single dictionary. And the sparse

coding is also conducted only once. So, it is evidently more

elegant than “Multi LE+comp”.

From Fig.5, it is clear that “Multiple block-wise SELD

fusion” performs impressively better than “Single SELD”,

which implies that different block partitioning strategies are

complementary mutually. From Fig.5, the proposed “Single

SELD” consistently outperforms “Single LE” by a 4~5

percents improvement. Our “Multiple block-wise SELD

fusion” is also comparable to “Multiple LE+comp”. However,

as mentioned above, “Multiple LE+comp” in [6] is more

complicated than our “Multiple block-wise SELD fusion”

method.

Comparison with other best known results on LFW

To better validate our method, we also compare our

methods with other previous state-of-the-art approaches

[5,6,27,28, 29] on the same LFW evaluation, as shown in Fig.

6. From the figure, it is clear that our method is among the best

ones. In addition, it is worth pointing out that, besides the

training data in LFW, the method in [27] utilized an external

large-scale datasets for feature extraction and classifier

designing.

C. Face identification on FERET

LFW evaluation focuses on face verification. In this

section, we perform experiments on the FERET dataset [23] to

verify the performance of our approach for face identification.

According to the FERET evaluation protocol, algorithms

were evaluated against different categories of images including

some variations such as lighting change, people wearing

glasses, and the time between the acquisition dates of the

database image. This database consists of one standard gallery

(1196 images of 1196 subjects) and four probe sets: Fb (1195

images of 1195 subjects), Fc (194 images of 194 subjects),

Duplicate I (722 images of 243 subjects) (abbreviated as DupI),

and Duplicate II (234 images of 75 subjects) (abbreviated as

DupII).

On this database, we align and normalize the face image

into 80×88 pixels. 300 frontal images are randomly selected

from the FERET training CD as the training set to learn the

dictionary. In our method, the sampling patch size is 5×5

pixels, and the face images are divided into 6×6 blocks.

The results of our method are compared with K-means and

LVP method [16] in Table 1. In order to compare with LVP,

we apply the histogram intersection as similarity measure.

From Table 1, we can get several major observations. First, all

method have almost equal performance on Fb dataset. Second,

the SELD method is superior to local encoded method based

K-means, 8, 4 and 4 percentage points improvement on Fc,

DupI and DupII dataset respectively. Third, our method also

significantly outperforms LVP method [16] except on Fb

dataset.

D. Discussion

As evaluated in above experiments, the proposed SELD

method works impressively better than similar method based

on K-means or Random-projection tree. So, what is the source

of the performance gain? To answer this question, we need to

analyze the main different between our method and previous

ones. As mentioned above, the main difference lies in two

points: 1) sparsity constraint is introduced in our method during

the dictionary learning, as well as during the image encoding

using the dictionary; 2) block-wise summation of the sparse

coding coefficients are used rather than the appearance

frequency (histogram) of the code-words.

TABLE I.  RECOGNITION PERFORMANCE ON THE FERET DATABASE

Descriptor Fb Fc DupI DupII

LVP [16] 0.97 0.70 0.66 0.50

K-means 0.95 0.76 0.64 0.58

SELD 0.95 0.84 0.68 0.62 The key of the first difference is “sparsity”, which has been

proved in recent literature very effective for both representation

and discrimination. Compared with K-means or Randomprojection tree which learn local visual patterns that most

frequently appears, sparse dictionary learning focuses more on

the effective representation of the local patches, which endow

the code-words more representation power.

The second difference actually reflects the difference of

exclusive model selection and additive model summation. Give

a sampled patch, traditional methods always encode it to one

single code-word by vector quantization. However, our method

encodes it to a vector associated with all the code-words. In

other words, traditional methods use single code-words to

express a patch, while our method expresses it with a linear

combination of all the code-words, which we believe can lead

to a more stable representation.

IV. CONCLUSION

In this paper, we propose sparsely encoded local descriptor

(SELD) for robust face recognition. Unlike traditional K-means

or Random-projection tree based dictionary learning method,

sparse dictionary is leaned by introducing sparsity constraint.

The encoding procedure is also changed from exclusive codeword assignment to sparse coding. Correspondingly, codewords frequency based descriptor is replaced by block-wise

summation of sparse coding coefficients vector. The above

characteristics endow the proposed SELD better performance,

as validated by the LFW evaluation. Results comparable to the

best known results are achieved.

In this paper, the proposed SELD method is only validated

on face recognition problem. Nevertheless, SELD is not limited

to face recognition, since it is not specially designed for face

recognition. Therefore, we will apply it to other possible

applications, e.g., object categorization.

ACKNOWLEDGMENT

This paper is partially supported by Natural Science

Foundation of China under contracts No.61025010, and

No.60833013; National Basic Research Program of China (973

Program) under contract 2009CB320902; and Hi-Tech

Research and Development Program of China under contract

No.2009AA01Z317.

REFERENCES

[1] W. Zhao, R. Chellappa, P. J. Phillips, and A. Rosenfeld, “Face

recognition: A literature survey,” ACM Comput. Surv., vol. 35, no. 4,

pp.399–458, 2003.

[2] P. J. Phillips, P. J. Flynn, J. R. Beveridge, W. T. Scruggs, A. J. O’ Toole,

D. Bolme, K. W. Bowyer, B. A. Draper, G. H. Givens, Y. M. Lui, H.

Sahibzada1, J. A. Scallan III, and S. Weimer, “Overview of the Multiple

Biometrics Grand Challenge”, in Proc. International Conference on

Biometrics, 2009.

[3] G. Huang, M. Ramesh, T. Berg, and E. Learned-Miller, “Labeled faces

in the wild: A database for studying face recognition in unconstrained

environments,” University of Massachusetts, Amherst, Technical Report

07-49, 2007.

[4] G. Hua and A. Akbarzadeh, “A robust elastic and partial matching

metric for face recognition,” in Proc. ICCV, 2009.

[5] Y. Taigman, L. Wolf, T. Hassner, and I. Tel-Aviv, “Multiple One-Shots

for utilizing class label information,” in Proc. BMVC, 2009.

[6] Z. Cao, Q.Yin, J.Sun, and X.Tang, “Face recognition with learningbased descriptor,” in Proc. CVPR, 2010.

[7] T.Ahonen, A.Hadid and M.Pietikäinen, “Face description with local

binary patterns: application to face recognition,” IEEE Transactions on

Pattern Analysis and Machine Intelligence 28 (12) (2006) 2037–2041.

[8] B. Zhang, S. Shan, X. Chen, W. Gao, “Histogram of Gabor phase

patterns (HGPP): a novel object representation approach for face

recognition,” IEEE Transactions on Image Processing 16 (1) (2007) 57–

68.

[9] W. Zhang, S. Shan, W. Gao, X. Chen, H. Zhang, “Local Gabor binary

pattern histogram sequence (LGBPHS): a novel non-statistical model for

face representation and recognition,” in Proc. ICCV, 2005.

[10] A. Albiol, D. Monzo, A. Martin, J. Sastre, and A. Albiol, “Face

recognition using HOG–EBGM,” Pattern Recognition Letters, Vol.29,

pp.1537-1543, 2008.

[11] D. Lowe, “Distinctive image features from scale-invariant keypoints,”

International Journal of Computer Vision, 60(2):91–110, 2004.

[12] G. Zhao andM. Pietikäinen, “Local binary pattern descriptors for

dynamic texture recognition,” in Proc. of ICPR, volume 2, pages 211–

214, 2006.

[13] X. Tan and B. Triggs, “Enhanced local texture feature sets for face

recognition under difﬁcult lighting conditions,” in International

Workshop on Analysis and Modeling of Faces and Gestures, 2007.

[14] S. Xie, S. Shan, X. Chen, J. Chen, “Fusing Local Patterns of Gabor

Magnitude and Phase for Face Recognition,” IEEE Transactions on

Image Processing, vol.19, no.5, pp1349-1361,May.2010.

[15] M. Bicego, A. Lagorio, E. Grosso, and M. Tistarelli,  “On the Use of

SIFT Features for Face Authentication,” in Computer Vision and Pattern

Recognition Workshop (CVPRW'06), 35, 2006.

[16] X. Meng, S. Shan, X. Chen, W. Gao, “Local visual primitives (LVP) for

face modeling and recognition,” in International Conference on Pattern

Recognition (2006) 536–539.

[17] S. Xie, S. Shan, X. Chen, X. Meng, and W. Gao, “Learned local gabor

patterns for face representation and recognition,” Signal Processing,

89(12):2333–2344, 2009.

[18] T. Ahonen and M. Pietik¨ainen, “Image description using joint

distribution of filter bank responses,” Pattern Recognition Letters.

30(4):368–376, 2009.

[19] Y. Freund, S. Dasgupta, M. Kabra, and N. Verma, “Learning the

structure of manifolds using random projections,” in Proc. NIPS, 2007.

[20] J. Wright, A.Yang, A. Ganesh, S.Sastry, and Y.Ma, “Robust face

recognition via sparse representation,” IEEE Transactions on Pattern

Analysis and Machine Intelligence, pages 210-227, 2009.

[21] Q. Zhang and B. Li, “Discriminative K-SVD for dictionary learning in

face recognition,” in Proc. CVPR, 2010.

[22] M. Yang and Lei Zhang, “Gabor Feature based Sparse Representation

for Face Recognition with Gabor Occlusion Dictionary,” in Proc. ECCV

2010.

[23] P. Phillips, H. Moon, S. Rizvi, P. Rauss, “The FERET evaluation

methodology for face-recognition algorithms,” IEEE Transactions on

Pattern Analysis and Machine Intelligence 22 (10) (2000) 1090–1104.

[24] M. Aharon, M.Elad, and A.Bruckstein, “K-SVD: An algorithm for

designing overcomplete dictionaries for sparse representation,” IEEE

Transactions on signal processing, 54(11):4311,2006.

[25] L.Wolf, T.Hassner, and Y.Taigman, “Similarity scores based on

background samples,” in Proc. ACCV, 2009.

[26] J. Yang, K. Yu, T. Huang, “Supervised translation-invariant Sparse

Coding,” in Proc. CVPR, 2010.

[27] N. Kumar, A. Berg, P. Belhumeur, and S. Nayar, “Attribute and Simile

classifiers for face verification,” in Proc. ICCV, 2009.

[28] M.Guillaumin, J. Verbeek, C. Schmid, I. LEAR, and L.Kuntzmann, “Is

that you? Metric learning approaches for face identification,” in Proc.

ICCV, 2009.

[29] N.Pinto, J.DiCarl0, and D.Cox, “How far can you get with a modern

face recognition test set using only simple features,”in Proc.CVPR,2009.88