Seasonal and interannual variations in carbon dioxide

exchange over a cropland in the North China Plain

H U I - M I N L E I and D A - W E N YA N G

State Key Laboratory of Hydroscience and Engineering, Department of Hydraulic Engineering, Tsinghua University,

Beijing 100084, China

Abstract

In China, croplands account for a relatively large form of vegetation cover. Quantifying carbon

dioxide exchange and understanding the environmental controls on carbon ﬂuxes over

croplands are critical in understanding regional carbon budgets and ecosystem behaviors.

In this study, the net ecosystem exchange (NEE) at a winter wheat/summer maize rotation

cropping site, representative of the main cropping system in the North China Plain, was

continuously measured using the eddy covariance technique from 2005 to 2009. In order to

interpret the abiotic factors regulating NEE, NEE was partitioned into gross primary production (GPP) and ecosystem respiration (Reco). Daytime Reco was extrapolated from the relationship between nighttime NEE and soil temperature under high turbulent conditions. GPP was

then estimated by subtracting daytime NEE from the daytime estimates of Reco. Results show

that the seasonal patterns of the temperature responses of Reco and light-response parameters

are closely related to the crop phenology. Daily Reco was highly dependent on both daily GPP

and air temperature. Interannual variability showed that GPP and Reco were mainly controlled

by temperature. Water availability also exerted a limit on Reco. The annual NEE was 585 and

533 g C m

2

for two seasons of 2006–2007 and 2007–2008, respectively, and the wheat ﬁeld

absorbed more carbon than the maize ﬁeld. Thus, we concluded that this cropland was a

strong carbon sink. However, when the grain harvest was taken into account, the wheat ﬁeld

was diminished into a weak carbon sink, whereas the maize ﬁeld was converted into a weak

carbon source. The observations showed that severe drought occurring during winter did not

reduce wheat yield (or integrated NEE) when sufﬁcient irrigation was carried out during

spring.

Keywords: carbon sequestration, ecosystem respiration, eddy covariance, gross primary production,

net ecosystem exchange, summer maize, winter wheat

Received 29 September 2009 and accepted 31 October 2009

Introduction

Increasing atmospheric CO2 concentrations may be one

of the most crucial issues related to climate change in

the future. Consequently, there is much interest in

studying carbon ﬂux dynamics in order to ﬁnd ways

to increase carbon sequestration in terrestrial ecosystems. Since 1990s, a network of eddy covariance sites

across a variety of ecosystem biomes has been set up

(Baldocchi et al., 2001), which aims at providing estimates of carbon ﬂuxes, understanding the variations in

carbon dioxide exchange in terms of environmental

controls, and supporting the derivation of model parameters. To date, studies on carbon dioxide exchange

have actively focused on forests and grasslands because

these certainly play an important role in the global

carbon cycle (Goulden et al., 1996; Owen et al., 2007;

Aires et al., 2008). In contrast, agroecosystems have been

of relatively less concern (Falge et al., 2002). Croplands

are regarded as strong contributors to the regional

carbon budget (Buyanovsky & Wagner, 1998; Anthoni

et al., 2004b) and they are particularly signiﬁcant in

China where the cropland biome covers the third largest area, following forests and grassland (Liu et al.,

2005). The carbon balance in agroecosystems may

be readily handled as farm ﬁelds are intensively

managed (Baker & Grifﬁs, 2005), facilitating the increase in carbon sequestration through changes in crop

management.

The North China Plain occupies an agricultural area

of about 1.8  10

5

km

2

, which accounts for 18.6% of the

total agricultural area in China (Wu et al., 2006). Wheat/

maize rotation cropping with tillage represents the

main cropping system on this plain. More than 50% of

the nation’s wheat and 33% of its maize are supplied by

Correspondence: D.-W. Yang, tel. 186 10 62796976, fax 186 10

62796971, e-mail: yangdw@mail.tsinghua.edu.cn

Global Change Biology (2010) 16, 2944–2957, doi: 10.1111/j.1365-2486.2009.02136.x

2944 r 2010 Blackwell Publishing Ltdthis region (Kendy et al., 2003). To our knowledge, few

studies have investigated the carbon dioxide exchange

in this region. Li et al. (2006) have reported 2-year

continuous measurements of NEE in a wheat/maize

double cropping system. However, continuous and

long-term measurements of NEE are still necessary to

explore the seasonal and interannual variations in carbon ﬂux components and how they are controlled by

climate variables.

In this study, we reported on three and a half years of

carbon ﬂuxes over a typical irrigated wheat/maize

rotation cropland, including four full winter wheat

seasons and three full summer maize seasons. The main

objectives were to (1) quantify the carbon ﬂuxes including gross primary production (GPP), ecosystem respiration (Reco), and net ecosystem exchange (NEE) using the

eddy covariance technique; (2) investigate the seasonal

variations in the characteristics of CO2 exchange, and

(3) examine the interannual variability in CO2 exchange

in response to environmental drivers.

Materials and methods

Site description

The Weishan ﬂux site is located on a cropland in the

North China Plain about 450 km south of Beijing, China

(N36139

0

, E116103

0

, 30 m asl). The climate is warm temperate and semi-humid. Its mean annual temperature is

about 13.3 1C and its mean annual precipitation is about

532 mm. The summer precipitation from June to September accounts for nearly 70% of the annual precipitation. The mean annual irrigation is about 215 mm and is

diverted from the Yellow River, primarily concentrated

in late February and March when winter wheat is

turning green (i.e., leaves are strongly erect).

A ﬂux tower was set up in the middle of a

400 m 200 m quadrilateral area surrounded by poplar

shelterbelts (Populus tomentosa Carr.). The site provides

a fetch of 400 m in the dominant wind direction with

unstable conditions. In the source area of the eddy

covariance system, only a small fraction of ground

was covered by trees, roads, and channels. Winter

wheat is sown in October after deep tillage and is

harvested in June of the following year, leaving a partial

straw cover on the ﬁeld. Summer maize is sown in June

under no-till and is harvested in October, with cornstalks ground up onto the ﬁeld.

The topography in this region is very ﬂat. The soil

texture of the root zone is silt loam. Soil organic matter

in the winter wheat season of 2008 at the depths of 5, 10,

30, 50, and 100 cm was 1.7%, 1.7%, 0.9%, 0.4%, and 0.3%,

respectively.

Measurements and data acquisition

The ﬂux of CO2 (Fc

) was continuously measured using

an eddy covariance system at a height of 3.7 m. The

system consisted of a 3D sonic anemometer (CSAT3,

Campbell Scientiﬁc Instruments Inc., Logan, UT, USA)

and an open-path infrared gas analyzer (IRGA, model

LI-7500, LI-COR Inc., Lincoln, NE, USA) to measure the

three components of wind velocity, sonic temperature,

and concentrations of water vapor and CO2. The data

were recorded with a data logger (CR5000, Campbell

Scientiﬁc Instruments Inc.) at a frequency of 10 Hz.

Postprocessing calculations, using the TK2 software

package (Mauder & Foken, 2004), included density

ﬂuctuation correction (Webb et al., 1980), spectral loss

correction (Moore, 1986), planar ﬁt coordinate rotation

(Wilczak et al., 2001), sonic virtual temperature conversion, and spike detection (Vickers & Mahrt, 1997). The

energy balance was examined for ‘closure’ by checking

the equality of the sum of latent heat (lE) and sensible

heat (H) ﬂuxes to the available energy (Ra) (Ra 5 Rn–G).

For the half-hourly values, the coefﬁcients a and b in the

linear regression model (lE 1H)5 aRa 1b were 0.74,

0.76, 0.75 and 10.85, 8.04, 3.82W m

2

in 2006, 2007, 2008,

respectively. These values were in the range reported by

most ﬂux sites (Wilson et al., 2002), and the energy

imbalance at our site may have been due to the horizontal advection (Li & Yu, 2007), underestimation of

soil heat ﬂux, neglect of energy storage in canopy and

top soil, and underestimation of latent and/or sensible

heat ﬂuxes. In this study, CO2 ﬂux was not corrected for

energy balance underestimation, as some researchers

have suggested (Twine et al., 2000).

Continuous complementary measurements included

standard climatological and soil parameters. Rainfall

was measured using a tipping bucket rain gauge

(TE525MM, Campbell Scientiﬁc Instruments Inc.). Wind

speed and direction (05103, Young Co., Traverse City,

MI, USA) were measured at a height of 10.0 m. Air

temperature and relative humidity (HMP45C, Vaisala

Inc., Helsinki, Finland) were measured 1.6 m above the

ground. Downward and upward solar and longwave

radiation (CNR-1, Kipp & Zonen, Delft, the Netherlands) and photosynthetically active radiation [(photon

ﬂux density) PPFD] (LI-190SA, LI-COR Inc.) were measured above the canopy at a height of 3.5 m. Soil

temperature (Campbell-107, Campbell Scientiﬁc Instruments Inc.) and volumetric soil water content (TRIMEEZ/IT, IMKO, Ettlingen, Germany) were measured at

0.05, 0.10, 0.20, 0.40, 0.80, and 1.60 m depths in both

plots. Two soil heat ﬂux plates (HFP01, Hukseﬂux,

Delft, the Netherlands) were placed at 3.0 cm depth.

Crop yield data before 2009 were collected from a

nearby agrometeorological site of the China MeteoroloC A R B O N D I O X I D E E X C H A N G E O V E R A C R O P L A N D 2945

r 2010 Blackwell Publishing Ltd, Global Change Biology, 16, 2944–2957gical Administration, which is about 19 km away from

our site and has a similar crop management and fertilization. The dry yield of winter wheat in 2009 was

determined gravimetrically after the samples had been

dried for 14 h at 80 1C. Replicate samples (n 54) were

collected by clipping the crop within a 1 m 1 m frame.

Soil respiration (Rs

) was measured from March 2009

to June 2009 with an automated soil CO2 ﬂux system

(LI-8100, LI-COR Inc.). The inner diameter of the soil

collar was 10 cm, and the chamber offset between the

soil surface and the lower edge of the chamber base

plate was 3 cm. For each measurement, observations

were repeated for three counts, and the soil respiration

values were estimated by averaging. The surface soil

temperature and soil water content at a depth of 10 cm

were measured concurrently with the attached temperature probe and soil moisture probe (EC-10, Decagon Devices Inc., Pullman, WA, USA). Four sample

points around the ﬂux tower were selected randomly

to place the soil collars. The observations were performed during daytime from 13:00 to 15:00 hours every

3 days on sunny days.

Data quality and gap ﬁlling

The eddy covariance data were visually screened for

anomalous values outside the range normally encountered. Nonstationary and integral turbulence tests

(Foken & Wichura, 1996) were employed to detect

unfavorable data. The results of both tests were combined to give a quality ﬂag on a scale from 1 to 9 (Table 9

in Mauder & Foken, 2004). The responses of the ﬂuxes

to environmental factors were established from halfhourly data with ﬂags 1–3 which were classiﬁed as the

highest quality data.

The major problem in calculating long-term rates is

low-turbulence conditions at night. Commonly, data of

Fc with low turbulence were excluded using the threshold of friction velocity (u*) (Massman & Lee, 2002). We

studied the dependence of CO2 ﬂux on friction velocity

in the rapid growth season of crops. As illustrated in

Fig. 1, the nighttime ﬂuxes measured below u*

o0.1 m s

1

were underestimated. Therefore, all nighttime data with u*o0.1 m s

1

were rejected. Data collected during rainy periods were also excluded. This

threshold was similar to those observed over short

crops (Anthoni et al., 2004a; Li et al., 2006; Moureaux

et al., 2006).

The unfavorable data detected by nonstationary and

integral turbulence tests (labeled with ﬂags 7–9) and

spike detection were gap-ﬁlled using the ‘look-up’ table

method which is based on the empirical relationships

among CO2 ﬂuxes and PPFD, and air temperature when

meteorological data are available (Falge et al., 2001). In

the case of missing meteorological data, the mean

diurnal variation method was applied using a 7-day

data window (Falge et al., 2001). Nighttime Fc data with

u*o0.1 m s

1

were gap-ﬁlled with the Vant Hoff equation, which will be introduced later. The missing daily

average temperature, daily solar radiation, and daily

precipitation data were spatially interpolated from a

nearby meteorological station network [see Yang et al.

(2004), for more details].

Calculation of NEE, GPP, and Reco

The NEE (mmol m

2

s

1

) was linked to the eddy covariance ﬂux (Fc

, mmol m

2

s

1

) by the following equation:

NEE ¼ Fc þ Fst

; ð1Þ

where Fst

is the storage ﬂux, which reﬂects the accumulation and depletion of CO2 in the canopy volume.

Fst was estimated based on the assumption that halfhour changes in CO2 concentration at the 3.7 m level are

representative of the whole layer below the eddy covariance system (Flanagan et al., 2002), as follows:

Fst ¼

hDc

Dt

; ð2Þ

where h is the height of the ﬂux measurement system

and Dc is the change in CO2 concentration during the

time interval, Dt.

NEE is the sum of GPP and Reco. GPP represents CO2

assimilation by photosynthesis of the vegetation, and

Reco consists of respiratory CO2 release from soil, stems,

and foliage. Nighttime NEE values are equal to Reco

because GPP equals 0. Thus, the daytime Reco was

estimated from a regression model using the relationFig. 1 Relationship between friction velocity (u*) and nighttime

0.5 h CO2 ﬂux (Fc

). Only data from the rapid growth period (15

April–15 May, 2007 for winter wheat, and 19 July–30 September,

2007 for summer maize) were included in this analysis.

2946 H . - M . L E I & D . - W. YA N G

r 2010 Blackwell Publishing Ltd, Global Change Biology, 16, 2944–2957ship between nighttime NEE (deﬁned as downward

solar radiation o20W m

2

) during high turbulence

(u*40.1 m s

1

) and soil temperature (Ts

) at a depth of

5 cm. GPP is a residual of observed NEE and estimated

Reco in daytime. When calculating Reco, the same procedure using a short-term temperature-dependent method, which is based on the Vant Hoff equation [Eqn (3)],

was applied using the method described by Reichstein

et al. (2005). The purpose was to avoid the confounding

effects of crop phenology and soil water on the temperature response function, which is as follows:

Reco ¼ Rref expðbTsÞ; ð3Þ

where Rref

(the reference respiration when Ts 50 1C)

and b are the regression parameters. The temperature

sensitivity coefﬁcient (Q10) was calculated using the

following equation:

Q10 ¼ expð10bÞ: ð4Þ

The short-term temperature sensitivity parameter b

for one crop growth season was averaged from all estimates, in 15-day subperiods, with the inverse of the

standard error as a weighing factor. The temperature

independent level of respiration (i.e., the Rref parameter) for each day was estimated using the least

squares spline approximation from all estimates for

each 4-day period.

Light response model

There are ﬁve basic models used for describing the

partial dependence of NEE on PPFD (Gilmanov et al.,

2003), in which the Michaelis–Menten rectangular hyperbola model (Suyker et al., 2004; Xu & Baldocchi,

2004) and the nonrectangular hyperbola model

(Soegaard & Thorgeirsson, 1998; Hirata et al., 2007) were

usually used. We compared these two light-response

models. Results showed that the nonrectangular hyperbola equation gave a better ﬁt according to the measures

of relative standard error and coefﬁcient of determination, which is expressed as follows:

NEE ¼

1

2y

ðaPPFD þ Fmax

ﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃﬃ

ðaPPFD þ FmaxÞ

2

4aFmaxyPPFD

q

Þ  g; ð5Þ

where a is the initial slope of the light response curve,

Fmax is the maximum CO2 ﬂux at inﬁnite light, g is the

daytime average ecosystem respiration, and y is the

curvature parameter (0  y  1). The parameters were

determined with daytime data for each day via a nonlinear weighted least squares ﬁt. The weighting factors

were the reciprocal of the standard deviations of the

observations with similar meteorological conditions

within a time window of  7 days (Lasslop et al.,

2008). At least six half-hourly nongap-ﬁlled data points

with u*40.1 m s

1

were required to ﬁt the parameters.

Parameters were not included when the relative standard error was 460%, and the coefﬁcient of determination was o0.6, or when parameter values were negative

or above 0.17 for a, 20 mmol m

2

s

1

for g, or

150 mmol m

2

s

1

for Fmax. These thresholds were considered to be the upper limits of realistic values.

In the absence of direct measurements of daytime

Reco, it was useful to compare g with the observed Reco

during the corresponding dark periods. As a more

direct comparison, g was then corrected for the soil

temperature difference between day and night (Gilmanov et al., 2003), which is as follows:

Reco;pred ¼ g expðkTðTs;d  Ts;nÞÞ; ð6Þ

where Reco,pred is the predicted nighttime-average ecosystem respiration, Ts,d is the daytime-average soil

temperature, Ts,n is the nighttime-average soil temperature, and kT 5 0.069 (1C)

1

.

Results and discussion

Seasonal and interannual variations in environmental

variables and crop development

Figure 2 shows the seasonal and interannual variations

in weekly average values for air temperature, vapor

pressure deﬁcit (VPD), PPFD, soil water content (0–

80 cm averaged), and weekly cumulative precipitation.

The seasonal sums of PPFD during the winter wheat

season (between October 15 and June 8) were 4911, 4379,

4810, and 4109mol m

2

in the years of 2005–2006, 2006–

2007, 2007–2008, and 2008–2009, respectively; whereas

seasonal sums of PPFD during the summer maize

season (between June 15 and October 14) were 3272,

2656, and 2591 mol m

2

in the years of 2006, 2007, and

2008, respectively. The seasonal averages of air temperature for the four winter wheat periods speciﬁed above

were 8.14, 8.88, 8.00, and 8.39 1C, respectively, whereas it

was 23.93, 22.62, and 22.69 1C for the three summer

maize seasons speciﬁed above, respectively. The VPD

curves showed that the seasonal average of VPD during

the wheat rapid growth season (March–May) was higher than that during the maize season. Precipitation

primarily occurred from June to September. The seasonal cumulative precipitations for the four winter wheat

periods were 102.4, 113.9, 120.8, and 236.1 mm, respectively; and it was 215.4, 382.3, and 324.1 mm for the three

summer maize seasons, respectively. The climate in the 3

years was drier than in the normal year. The unsynchronized seasonality between precipitation and VPD resulted in more droughts during the winter wheat season

C A R B O N D I O X I D E E X C H A N G E O V E R A C R O P L A N D 2947

r 2010 Blackwell Publishing Ltd, Global Change Biology, 16, 2944–2957than during the summer maize season. The soil water

content was generally high because of sufﬁcient irrigation during the wheat season and sufﬁcient precipitation

during the maize season. In particular, the winter wheat

experienced extreme drought stress from fall of 2008 to

spring of 2009 (Tao et al., 2009). The soil water content

during this period was very low until the ﬁrst irrigation

in late February of 2009. The soil water content during

the maize season of July 2006 also demonstrated slight

water stress. The PPFD, air temperature, and precipitation showed great interannual variability, providing an

opportunity to study the climate variability on carbon

dioxide exchange, which will be discussed later in

the paper.

Photosynthetically active radiation (PAR) albedo had

a good negative correlation with the leaf area index

(LAI) (Xu & Baldocchi, 2004; Burba & Verma, 2005).

Thus, PAR albedo was used as an alternative indicator

of crop development because consecutive measurements of the LAI were unavailable during these study

periods. Figure 3 illustrates the seasonal and interannual variations in PAR albedo. It decreased slightly in

November with the emergence and tillering of winter

wheat, and then increased in winter due to leaf withering during the dormant stage. It remained relatively

constant until the leaves became strongly erect in late

February. The peak of PAR albedo appeared in late

April or early May for the wheat season (the period

Fig. 2 Seasonal and interannual variations in the weekly averages (or sums) of daily mean air temperature (Ta

), daily mean vapor

pressure deﬁcit (VPD), daily total photosynthetic photon ﬂux density (PPFD), daily total precipitation (P), and soil water content (SWC,

0–80 cm averaged). Vertical arrows indicate irrigation events.

2948 H . - M . L E I & D . - W. YA N G

r 2010 Blackwell Publishing Ltd, Global Change Biology, 16, 2944–2957from late April to early May is referred to as the ‘rapid

growth season’ for wheat). After the planting of maize

in June, the PAR albedo decreased rapidly during the

elongation stage in July, reaching a minimum in early

August, and then increased rapidly from late September (the period from August to early September is

referred to as the ‘rapid growth season’ for maize).

The seasonal variations in PAR albedo showed similar

patterns in each year, but with signiﬁcant interannual

variability. The wheat in 2006–2007 had the lowest PAR

albedo, but senesced earlier than those in the other

years. Severe drought, occurring before March of 2009,

was shown to not reduce the LAI of wheat through the

inter-comparison of wheat’s PAR albedo values in the

years of 2005–2006 and 2008–2009.

Comparison of estimated and observed respiration using

different approaches

Nighttime respiration can also be estimated from the

light-response curve. Comparison of the estimated daytime average respiration (the effect of soil temperature

differences between day and night has been accounted

for) with the measured nighttime NEE showed a good

agreement (Fig. 4). A linear regression over the 3-year

period yielded a slope 5 0.95 (R

2

50.83). Therefore,

when eddy covariance measurements at night were

unavailable, it was concluded that daytime respiration,

estimated from the light response curve, could be used

to gap-ﬁll the nighttime NEE after necessary temperature corrections. The good agreement between the two

estimates also suggested that the uncertainties, primarily in the NEE–PPFD regression model and the nonturbulent processes at night, may be quite limited.

The daytime average ecosystem respiration estimated

from the light response curve was also compared with

the daytime soil respiration observed with the chamber

(Fig. 5). These were in good agreement despite the

spatial heterogeneity of the chamber measurements.

Theoretically, ecosystem respiration should be greater

than soil respiration, as we did not measure the respiration of foliage and stems. However, the measurements

from the chamber were slightly greater than the estimates from the light response curve. Our chamber

measurements were performed during the period from

13:00 to 15:00 hours, when the soil respiration was

slightly higher than the daytime average values because

of the slightly higher soil temperature (data not shown).

Other studies have also shown there is signiﬁcant

uncertainty when comparing eddy covariance measurements with chamber measurement (Loescher et al.,

2006). This uncertainty can even cause to that the

chamber estimates to be substantially higher than the

eddy covariance estimates (Lavigne et al., 1997; Law

et al., 1999). The comparison between the two different

Fig. 3 Seasonal and interannual variations in weekly averages of daily photosynthetically active radiation (PAR) albedo (upward PAR/

downward PAR, averaged from 10:00 to 14:00 hours).

Fig. 4 Comparison of observed nighttime average (u*40.1m s

1

)

with the predicted values of 7-day averages of ecosystem respiration. Predicted values were calculated from daytime estimates using

the temperature coefﬁcient kT 50.069(1C)

1

(Q10 52.0). Error bars

indicate standard deviation of the means.

C A R B O N D I O X I D E E X C H A N G E O V E R A C R O P L A N D 2949

r 2010 Blackwell Publishing Ltd, Global Change Biology, 16, 2944–2957observation methods suggested that soil surface respiration was the largest source of ecosystem respiration at our site, and it validated the reliability of the

eddy covariance measurement.

Temperature response of respiration

Figure 6 shows the relationship between soil respiration

and soil temperature. The Q10 value ranged from 4.0 in

March to 2.1 in April of 2009, showing an obvious

seasonal trend with crop phenology. A declining trend

in soil respiration with soil temperature was observed

in late May and early June due to the senescence of

wheat.

The short-term Q10 values of the ecosystem respiration for each crop season are listed in Table 1. They

ranged from 2.0 to 2.3 for winter wheat seasons and 1.4

to 3.9 for summer maize seasons. The short-term Q10

value of ecosystem respiration was higher than that of

soil respiration for 2008–2009, as ecosystem respiration

is composed mainly of soil respiration. The Rref parameter showed a clear seasonal trend with crop phenology (Fig. 7), indicating that the temperature function

was greatly affected by crop development. The measured values of Q10 were within the reported Q10

values, which can show wide variations (Raich & Schlesinger, 1992). Other published results in agroecosystems

have also indicated wide variations in Q10. For example,

the Q10 values of 3.6–20.1 for maize were observed in

Nebraska, USA (Suyker et al., 2004). In Canada, Pattey

et al. (2001) observed Q10 values ranging from 1.5 to 2.6

for maize growing under a high rate of nitrogen fertilization and from 1.3 to 2.5 under a low rate. Soegaard

et al. (2003) reported a Q10 value of 2.3 at 10 1C during

the period from late April to late August for summer

wheat in Denmark.

Seasonal patterns of light-response parameters

Figure 8 demonstrates the seasonal course of light

response parameters, a, Fmax and g. In general, the

seasonal patterns of these parameters closely followed

crop phenology (Fig. 3). The a values for winter wheat

ranged from about 0.01 mmol m

2

s

1

in its dormant

stage to around 0.055 mmol m

2

s

1

at its rapid growth

stage. The a values ranged from 0.005 mmol m

2

s

1

at

the early growth stage to 0.065 mmol m

2

s

1

at the rapid

growth stage for summer maize. The Fmax ranged from

around 30–65 mmol m

2

s

1

for winter wheat, and

reached up to 65 mmol m

2

s

1

for summer maize.

Fig. 5 Comparison of soil respiration observed from chamber

and ecosystem respiration estimated from light response curves,

March 2009–May 2009. Error bars indicate standard deviation of

the means of observations from four points.

Fig. 6 Responses of soil respiration (Rs

) to soil temperature (Ts

)

at a depth of 10 cm. Data were from the winter wheat season in

2009. The black solid line indicates the nonlinear regression

based on all available data for this season (long-term sensitivity

approach), whereas grey solid line indicates the nonlinear regression based on the data for each month (short-term sensitivity

approach).

Table 1 Q10 values for each crop season

Year Crop

Short-term

Q10

Longterm Q10

2005–2006 Winter wheat 2.2 2.3

Summer maize 1.6 1.3

2006–2007 Winter wheat 2.0 2.7

Summer maize 1.4 2.3

2007–2008 Winter wheat 2.0 2.3

Summer maize 3.9 1.6

2008–2009 Winter wheat 2.3 2.7

2950 H . - M . L E I & D . - W. YA N G

r 2010 Blackwell Publishing Ltd, Global Change Biology, 16, 2944–2957Statistically, the peak values of a for the C3 wheat were

slightly lower than those for the C4 maize because a C4

plant has higher light use efﬁciency for photosynthesis

than a C3 plant (Hollinger et al., 2005). The quantum

yield reported from our site was comparable with other

published data. Anthoni et al. (2004b) reported an a

value of 0.063 mmol m

2

s

1

during the rapid growth

season for winter wheat. Ruimy et al. (1995) reported an

Fig. 7 Examples of seasonal variations in Rref

: (a) summer maize season in 2008 (Q10 53.9); (b) winter wheat season from 2008 to 2009

(Q10 52.3). Dots, ﬁtted from nighttime observed NEE; Solid line, spline approximation from the dot values.

Fig. 8 Seasonal dynamics of light-response parameters: (a) apparent quantum efﬁciency (a); (b) saturated gross photosynthesis (Fmax);

(c) daytime average ecosystem respiration (g). Dots, weekly mean values.

C A R B O N D I O X I D E E X C H A N G E O V E R A C R O P L A N D 2951

r 2010 Blackwell Publishing Ltd, Global Change Biology, 16, 2944–2957a of maize ranging from 0.03 to 0.06 mmol m

2

s

1

.

Suyker et al. (2004) reported an a of maize ranging from

0.02 to 0.04 mmol m

2

s

1

.

The estimated daytime average g varied closely with

temperature, ranging from around 1 mmol m

2

s

1

in

winter to approximately 9 mmol m

2

s

1

in summer.

However, it was clearly reduced in June when the two

crops were in a rotation period, reﬂecting the impact of

photosynthetic activity on ecosystem respiration.

Seasonal and interannual variations in CO2

exchange

Figure 9 shows the seasonal variations in daily cumulative GPP, Reco, and NEE over the course of the study.

The courses of GPP and NEE showed signiﬁcant seasonal variations that were closely related to crop development and phenology. Within each year, NEE had two

positive periods, when the crops were harvested in

early June and early October. The values of NEE in

the winter wheat ﬁeld reached their minimum at 10 to

11 g C m

2

day

1

in late April. The minimum daily

NEE in the summer maize ﬁeld appeared in August,

ranging from 11 to 15 g C m

2

day

1

. In comparison, Li

et al. (2006) reported slightly lower minimum values of

10 to 13 g C m

2

day

1

for NEE in the summer maize

ﬁeld and 8 to 9 g C m

2

day

1

in the winter wheat

ﬁeld. Similar values of minimum daily NEE have been

also reported in other areas, for instance, 10 to

12 g C m

2

day

1

for wheat in Germany (Anthoni

et al., 2004b), and 12 to 19 g C m

2

day

1

for maize

in the United States (Hollinger et al., 2005). The minimum values of NEE for summer maize were larger than

those for winter wheat, which is in line with the results

reported by Falge et al. (2002), who indicated that the

maximum CO2 uptake of C4 plants was higher than that

of C3 plants. The pattern of ecosystem respiration Reco

was similar to the daytime averaged ecosystem respiration g derived from the light-response curve (Fig. 8).

The maximum daily values of Reco in wheat seasons did

not correspond to the days with the highest GPP values,

instead occurring later after the peak GPP with the

evolution of temperature. However, the variation in

daily Reco in maize seasons was synchronous with the

variation in daily temperature. This suggested that Reco

was linked to the changes in both temperature and GPP.

Table 2 lists the annual and seasonal sums of GPP,

Reco, and NEE. We expected that the missing data from

13 November, 2007 to 16 March, 2008 would not bring

excessive underestimation of the annual and seasonal

sum values, as the crop ﬁeld was only a small carbon

sink in this period when the winter wheat was dormant.

The interannual variation in NEE was large, which was

due to both the interannual changes in GPP and Reco.

The seasonal sums of NEE for wheat ranged from 303

to 395 g C m

2

, whereas they were between 201 and

244 g C m

2

for maize. Winter wheat absorbed more

Fig. 9 Seasonal variations in (a) daily gross ecosystem production (GPP), (b) daily ecosystem respiration (Reco) and (c) daily net

ecosystem exchange (NEE). PW, plant dates for winter wheat; HW, harvest dates for winter wheat; PM, plant dates for summer maize;

HM, harvest dates for summer maize.

2952 H . - M . L E I & D . - W. YA N G

r 2010 Blackwell Publishing Ltd, Global Change Biology, 16, 2944–2957CO2 than did summer maize because more light was

absorbed by the wheat. The annual GPP, Reco, and NEE

in 2006–2007 and 2007–2008 were 2008, 1423,

585 g C m

2

and 1668, 1135, and 533 g C m

2

, respectively. The seasonal sums of GPP for both wheat and

maize showed that temperature played an important

role in controlling GPP. Higher average air temperatures led to a larger GPP. However, no signiﬁcant

correlation was found between PPFD and GPP, or for

SWC and GPP. Both the comparisons between wheat

seasons in 2005–2006 and 2008–2009 and the comparisons between maize seasons in 2007 and 2008 showed

that ecosystem respiration Reco was controlled mainly

by temperature and soil water content. A higher Reco

could result from a higher temperature and/or higher

soil water content.

Uncertainties in estimated CO2

exchange

There is a potential systematic bias in estimating Reco

and NEE as the nighttime measured Fc

in low-turbulence conditions. The dependence of NEE on the nighttime friction velocity (u*) threshold could be site

speciﬁc, as annual NEE was quite sensitive to u* at

some sites (Anthoni et al., 2004b), and insensitive to u*

when u* was greater than a certain threshold at other

sites (Xu & Baldocchi, 2004). Figure 10 shows the impact

of different u* thresholds on the estimated seasonal

sums of NEE. NEE became less negative as u* increased

from 0.0 to about 0.1 m s

1

. Increasing u* after 0.1 m s

1

only slightly affected the estimated NEE. The differences in estimated NEE between uncorrected and corrected values at u*5 0.1 m s

1

were only 32, 46, and

13 g C m

2

for the three seasons. Thus, nighttime low u*

was shown to have limited impacts on the estimated

seasonal sum of NEE at our site.

As an alternative approach, ecosystem respiration can

be estimated using long-term sensitivity (parameters b

and Rref are estimated from all available Reco and

temperature data during one growth season or a year)

(Li et al., 2006; Moureaux et al., 2006). However, Reichstein et al. (2005) recommended an algorithm, used in

this study, which deﬁnes a short-term sensitivity of

ecosystem respiration. We compared the results from

these two approaches. As shown in Fig. 11, winter

wheat shows summer active vegetation and summer

maize shows summer passive vegetation. Thus, the

GPP of summer maize would be expected to be underestimated using long-term temperature sensitivity,

whereas the GPP of winter wheat would be expected

to be overestimated (Reichstein et al., 2005). This

Table 2 Annual and seasonal sums of NEE, GPP, and Reco

Season Year Ta (1C)

PPFD

(mol m

2

)

SWC

(v/v)

GPP

(g C m

2

)

Reco

(g C m

2

)

NEE

(g C m

2

)

Yield

(g m

2

)

Cgr

(g C m

2

)

NEE 1

Cgr

(g C m

2

)

Annual 2006–2007 13.74 7169 0.28 2008 1423 585 – – –

2007–2008* 13.16 7545 0.27 1668 1135 533 – 615 82

Winter wheat

(10.15–6.08)

2005–2006 8.14 4911 0.31 961 636 326 645 250 76

2006–2007 8.88 4379 0.28 1114 720 394 675 261 133

2007–2008* 8.00 4810 0.28 782 479 303 637 247 56

2008–2009 8.39 4109 0.27 967 572 395 656w 295 100

Summer maize

(6.15–10.14)

2006 23.93 3272 0.27 – – – 706 267 –

2007 22.62 2656 0.28 872 672 201 – – –

2008 22.69 2591 0.26 880 636 244 975 368 124

*Data from 13 November, 2007 to 16 March, 2008 were missing.

wDry yield.

Mean air temperature, mean daily cumulative PPFD, mean soil water content, and crop yield are also presented.

Ta, daily mean air temperature; PPFD, photosynthetically active radiation; SWC, soil water content; GPP, gross primary production;

Reco, ecosystem respiration; NEE, net ecosystem exchange; Cgr

, carbon in grains.

Fig. 10 Dependence of seasonal sums of net ecosystem exchange (NEE) on nighttime friction velocity (u*). Three full

seasons were selected with no large gaps.

C A R B O N D I O X I D E E X C H A N G E O V E R A C R O P L A N D 2953

r 2010 Blackwell Publishing Ltd, Global Change Biology, 16, 2944–2957consideration was conﬁrmed in our analysis of GPP.

Using long-term temperature sensitivity, the GPP of

summer maize was underestimated ranging from 0.1%

to 5.7% in different seasons, whereas the GPP of winter

wheat was overestimated ranging from 0.5% to 8.1% in

different seasons. Although the Q10 values estimated by

the two approaches were somewhat different (Table 1),

the seasonal sums of GPP showed nonsigniﬁcant bias

between the two approaches. However, the short-term

sensitivity method is still recommended, as the seasonal

variations in ecosystem respiration would be biased for

the dramatic growth dynamics and/or soil moisture

effects (Reco would be overestimated in the early and

late growth stages and be underestimated in the rapid

growth stage) if the long-term temperature sensitivity is

used (as shown in Fig. 6).

Comparison of annual NEE with other ecosystems

The annual NEE was 533 and 585 g C m

2

yr

1

in the

years of 2006–2007 and 2007–2008, respectively. As

compared with other annual cropping agroecosystems,

our site with the winter wheat/summer maize rotation

cropping system is a relatively strong carbon sink (see

Table 3). In contrast, the temperate mixed forest in

Northeast China and a steppe in central Mongolia both

acted as relatively weak carbon sinks. Our data also

showed that the carbon sink of the wheat/maize rotation system, with one tillage per year, was not different

from that of the no-till cropland, which is similar to the

results reported by Baker & Grifﬁs (2005).

The main difference between agroecosystems and

natural ecosystems in terms of carbon budget on a

regional scale is that crop grains are harvested and

ﬁnally transformed to CO2, which is again released to

the atmosphere. We assumed that all of the crop straws

were returned to the ﬁeld, and the carbon in grains (Cgr

)

was estimated by crop yield (Y), which is as follows:

Cgr ¼ ð1  Wgr

ÞfcY; ð7Þ

Fig. 11 Examples of the statistical relationship between daily

average air temperature and reference respiration (Rref

) estimates. Data were from the 2008 maize season and the 2008–

2009 wheat season.

Table 3 Comparison of annual net ecosystem exchange (NEE) among different ecosystems

Site Latitude Vegetation

Temperature

(1C)

Precipitation

(mm)

NEE

(g C m2

yr

1

) Period Source

Weishan, China 36139

0

N Wheat/maize

rotation, irrigated,

tillage

13.3 532 533 to 585 2006–2008 This study

Nebraska, USA 41110

0

N Maize, irrigated,

no-till

11.0 570 381 to 517 2001–2004 Verma et al. (2005)

Illinois, USA 40100

0

N Maize, rainfed,

no-till

– – 576 1997–2002 Hollinger et al. (2005)

Gebesee, Germany 51106

0

N Winter wheat,

rainfed, tillage

9.7 505 185 to 245 2001 Anthoni et al. (2004a)

Ponca City, USA 36146

0

N Winter wheat,

rainfed, -

14.8 966 273 1–232 days

during 1997

Gilmanov et al.

(2003)

Yucheng, China 36150

0

N Wheat/maize

rotation, irrigated,

tillage

13.1 582 761 to 1097 2003–2004 Zhang et al. (2008)

Changbaishan,

China

42124

0

N Temperate mixed

forest

3.6 695 242 to 279 2003–2005 Yu et al. (2008)

Hentiy, Mongolia 47113

0

N Grazed steppe 1.2 196 41 2003–2004 Li et al. (2005)

2954 H . - M . L E I & D . - W. YA N G

r 2010 Blackwell Publishing Ltd, Global Change Biology, 16, 2944–2957where Wgr

[0.140 for wheat and 0.155 for maize (Li et al.,

2006)] is grain water content, and fc

[0.450 for wheat and

0.447 for maize (Li et al., 2006)] is the fraction of carbon

in the grain. Taking into account the carbon released by

grains, the carbon sink in the wheat ﬁeld was greatly

diminished, whereas the maize ﬁeld was turned

into a slight carbon source (Table 2). Annually, our site

is a weak carbon source if grain carbon loss is considered for the years of 2007–2008. This is similar to

other reported results (Anthoni et al., 2004a; Verma

et al., 2005).

Possible impacts of climate change on carbon dioxide

exchange

As mentioned above, interannual variations in GPP

were mainly determined by temperature, whereas interannual variations in Reco were affected by both

temperature and soil water content. The variation in

NEE depended on the relative contributions from GPP

and Reco. From our analysis, although northern China

encountered a severe drought during the period from

November 2008 to January 2009, neither the seasonal

sum of NEE nor the yield of winter wheat in the season

of 2008–2009 was reduced comparing with that in the

other years. Previous study has shown that winter

wheat was most insensitive to water stress in its dormant stage and more sensitive to water stress from stem

elongation to heading stages and from heading to

milking stages (Zhang et al., 1999). Certain soil water

stress in the early vegetative growth period could lead

to higher grain yield as a result of small reduction in

biomass and an improvement in harvest index (Kang

et al., 2002). Thus, the yield (or NEE) of winter wheat

would not decrease as a result of the winter drought, as

long as sufﬁcient irrigation is carried out in late February when the wheat is turning green. According to the

IPCC report (IPCC, 2001) and modeling work (Yu et al.,

2008), the air temperature in northern China will increase and northern China will become more xeric as

global warming progresses. Our study’s results suggested that GPP would increase with increasing temperature, and that Reco would also increase if sufﬁcient

irrigation is maintained. Owing to the complexities in

crop management and the uncertainties of future climate change, more long-term measurements based on

various approaches are needed to investigate the response of carbon sequestration to climate change.

Conclusion

We have presented measured NEE and estimates of

GPP and ecosystem respiration from 2005 to 2009 using

an eddy covariance technique for winter wheat/summer maize double cropping ﬁelds in the North China

Plain. Comparisons of eddy covariance measurements

with chamber measurements suggested that ecosystem

respiration was primarily composed of soil respiration

for this cropland. Seasonal variations in the response of

nighttime NEE to temperature and the response of

daytime NEE to light showed close association with

crop development and phenology (expressed as PAR

albedo). Daily Reco was highly dependent on both GPP

and temperature. Interannual variations in Reco and

GPP were mainly controlled by temperature. Soil water

availability also imposed signiﬁcant limitations on Reco

during the drought periods. Nighttime low u* was

shown to have a limited impact on the estimated

seasonal sums of NEE. An algorithm, deﬁning a shortterm temperature sensitivity of ecosystem respiration,

estimated similar integrated GPP as that estimated by

an algorithm with long-term temperature sensitivity.

Short-term temperature sensitivity algorithm, however,

avoids the bias in seasonal variations. The annual NEE

was 585 and 533 g C m

2

for the 2006–2007 and

2007–2008 seasons, respectively. Seasonal sums of NEE

for wheat ranged from 303 to 395 g C m

2

, and they

were 201 to 244 g C m

2

for maize. Integrated NEE

showed that both winter wheat and maize ﬁelds were

strong carbon sinks. However, when the harvest was

taken into account, the wheat ﬁeld was diminished to a

small carbon sink, whereas the maize ﬁeld was converted to a small carbon source. The annual NEE showed

that the winter wheat/summer maize cropping ﬁeld was

a small carbon source in 2007–2008, if grain harvest was

considered. We observed that severe droughts during fall

and winter did not have negative impacts on the seasonal sum of NEE or the yield of wheat.

Acknowledgements

This research was supported by the National Natural Science

Foundation of China (Project no. 50679029 and no. 50811140089)

and the Doctoral Program Foundation of Institutions of Higher

Education of China (Project No. 2007000307). The authors would

like to express their appreciation to two anonymous reviewers,

whose comments and suggestions led to signiﬁcant improvements in the manuscript.

References

Aires LMI, Pio CA, Pereira JS (2008) Carbon dioxide exchange above a

Mediterranean C3/C4 grassland during two climatologically contrasting years. Global Change Biology, 14, 539–555.

Anthoni PM, Freibauer A, Kolle O et al. (2004a) Winter wheat carbon

exchange in Thuringia, Germany. Agricultural and Forest Meteorology,

121, 55–67.

Anthoni PM, Knohl A, Rebmann C et al. (2004b) Forest and agricultural

land-use-dependent CO2 exchange in Thuringia, Germany. Global

Change Biology, 10, 2005–2019.

C A R B O N D I O X I D E E X C H A N G E O V E R A C R O P L A N D 2955

r 2010 Blackwell Publishing Ltd, Global Change Biology, 16, 2944–2957Baker JM, Grifﬁs TJ (2005) Examining strategies to improve the carbon

balance of corn/soybean agriculture using eddy covariance and mass

balance techniques. Agricultural and Forest Meteorology, 128, 163–177.

Baldocchi DD, Falge E, Gu L et al. (2001) FLUXNET: a new tool to study

the temporal and spatial variability of ecosystem-scale carbon dioxide,

water vapor, and energy ﬂux densities. Bulletin of the American Meteorological Society, 82, 2415–2434.

Burba GG, Verma SB (2005) Seasonal and interannual variability in

evapotranspiration of native tallgrass prairie and cultivated wheat

ecosystems. Agricultural and Forest Meteorology, 135, 190–201.

Buyanovsky GA, Wagner GH (1998) Carbon cycling in cultivated land

and its global signiﬁcance. Global Change Biology, 4, 131–141.

Falge E, Baldocchi D, Olson R et al. (2001) Gap ﬁlling strategies for

defensible annual sums of net ecosystem exchange. Agricultural and

Forest Meteorology, 107, 43–69.

Falge E, Baldocchi D, Tenhunen J et al. (2002) Seasonality of ecosystem

respiration and gross primary production as derived from FLUXNET

measurements. Agricultural and Forest Meteorology, 113, 53–74.

Flanagan LB, Wever LA, Carlson PJ (2002) Seasonal and interannual

variation in carbon dioxide exchange and carbon balance in a northern

temperate grassland. Global Change Biology, 8, 599–615.

Foken T, Wichura B (1996) Tools for quality assessment of surfacebased ﬂux measurements. Agricultural and Forest Meteorology, 78,

83–105.

Gilmanov TG, Verma SB, Sims PL et al. (2003) Gross primary production

and light response parameters of four Southern plains ecosystems

estimated using long-term CO2

-ﬂux tower measurements. Global Biogeochemical Cycles, 17, 1071, doi: 10.1029/2002GB002023.

Goulden ML, Munger JW, Fan SM et al. (1996) Exchange of carbon dioxide

by a deciduous forest: response to interannual climate variability.

Science, 271, 1576–1578.

Hirata R, Hirano T, Saigusa N et al. (2007) Seasonal and interannual

variations in carbon dioxide exchange of a temperate larch forest.

Agricultural and Forest Meteorology, 147, 110–124.

Hollinger SE, Bernacchi CJ, Meyers TP (2005) Carbon budget of mature

no-till ecosystem in North Central region of the United States. Agricultural and Forest Meteorology, 130, 59–69.

IPCC ed. (2001) Climate Change 2001: The Scientiﬁc Basis. Contribution of

Working Group I to the Third Assessment Report of the Intergovernmental

Panel on Climate Changes. Cambridge University Press, Cambridge,

New York.

Kang S, Zhang L, Liang Yet al. (2002) Effects of limited irrigation on yield

and water use efﬁciency of winter wheat in the Loess Plateau of China.

Agricultural Water Management, 55, 203–216.

Kendy E, Ge´rard-Marchant P, Walter MT et al. (2003) A soil-water-balance

approach to quantify groundwater recharge from irrigated cropland in

the North China plain. Hydrological Processes, 17, 2011–2031.

Lasslop G, Reichstein M, Kattge J et al. (2008) Inﬂuences of observation

errors in eddy ﬂux data on inverse model parameter estimation.

Biogeosciences, 5, 1311–1324.

Lavigne MB, Ryan MG, Anderson DE et al. (1997) Comparing nocturnal

eddy covariance measurements to estimates of ecosystem respiration

made by scaling chamber measurements at six coniferous boreal sites.

Journal of Geophysical Research, 102, 28977–28985.

Law BE, Baldocchi DD, Anthoni PM (1999) Below-canopy and soil CO2

ﬂuxes in a ponderosa pine forest. Agricultural and Forest Meteorology, 94,

171–188.

Li SG, Asanuma J, Eugster W et al. (2005) Net ecosystem carbon dioxide

exchange over grazed steppe in central Mongolia. Global Change Biology,

11, 1941–1955.

Li L, Yu Q (2007) Quantifying the effects of advection on canopy

energy budgets and water use efﬁciency in an irrigated wheat

ﬁeld in the North China Plain. Agricultural Water Management, 89,

116–122.

Li J, Yu Q, Sun X et al. (2006) Carbon dioxide exchange and the mechanism

of environmental control in a farmland ecosystem in North

China plain. Science in China Series D: Earth Science, 49 (Suppl. II),

226–240.

Liu J, Liu M, Tian H et al. (2005) Spatial and temporal patterns of China’s

cropland during 1990–2000: an analysis based on Landsat TM data.

Remote Sensing of Environment, 98, 442–456.

Loescher HW, Law BE, Mahrt L et al. (2006) Uncertainties in, and

interpretation of, carbon ﬂux estimates using the eddy covariance

technique. Journal of Geophysical Research, 111, D21S90, doi: 10.1029/

2005JD006932.

Massman WJ, Lee X (2002) Eddy covariance ﬂux corrections and uncertainties in long-term studies of carbon and energy exchanges. Agricultural and Forest Meteorology, 113, 121–144.

Mauder M, Foken T (2004) Documentation and instruction manual of the

eddy covariance software package TK2. Universita¨t Bayreuth, Abt.-

Mikrometeorologie, Arbeitsergebnisse (Print, ISSN 1614–8916; Internet,

ISSN 1614–8926).

Moore CJ (1986) Frequency response corrections for eddy correlation

systems. Boundary-Layer Meteorology, 37, 17–35.

Moureaux C, Debacq A, Bodson B et al. (2006) Annual net ecosystem

carbon exchange by a sugar beet crop. Agricultural and Forest Meteorology, 139, 25–39.

Owen KE, Tenhunen J, Reichstein M et al. (2007) Linking ﬂux network

measurements to continental scale simulations: ecosystem carbon

dioxide exchange capacity under non-water-stressed conditions. Global

Change Biology, 13, 734–760.

Pattey E, Strachan IB, Boisvert JB et al. (2001) Detecting effects of nitrogen

rate and weather on corn growth using micrometeorological and

hyperspectral reﬂectance measurements. Agricultural and Forest Meteorology, 108, 85–99.

Raich JW, Schlesinger WH (1992) The global carbon dioxide ﬂux in soil

respiration and its relationship to vegetation and climate. Tellus, 44B,

81–99.

Reichstein M, Falge E, Baldocchi D et al. (2005) On the separation of net

ecosystem exchange into assimilation and ecosystem respiration:

review and improved algorithm. Global Change Biology, 11, 1424–1439.

Ruimy A, Jarvis PG, Baldocchi DD et al. (1995) CO2 ﬂuxes over plant

canopies and solar radiation: a review. Advances in Ecological Research,

26, 1–68.

Soegaard H, Jensen NO, Boegh E et al. (2003) Carbon dioxide exchange

over agricultural landscape using eddy correlation and footprint

modelling. Agricultural and Forest Meteorology, 114, 153–173.

Soegaard H, Thorgeirsson H (1998) Carbon dioxide exchange at leaf and

canopy scale for agricultural crops in the boreal environment. Journal of

Hydrology, 212–213, 51–61.

Suyker AE, Verma SB, Burba GG et al. (2004) Growing season carbon

dioxide exchange in irrigated and rainfed maize. Agricultural and Forest

Meteorology, 124, 1–13.

Tao S, Wei J, Sun J et al. (2009) The severe drought in east China during

November, December and January 2008–2009. Meteorological Monthly,

35, 3–10 (in Chinese with English abstract).

Twine TE, Kustas WP, Norman JM et al. (2000) Correcting eddy-covariance ﬂux underestimates over a grassland. Agricultural and Forest

Meteorology, 103, 279–300.

Verma SB, Dobermann A, Cassman KG et al. (2005) Annual carbon

dioxide exchange in irrigated and rainfed maize-based agroecosystems. Agricultural and Forest Meteorology, 131, 77–96.

Vickers D, Mahrt L (1997) Quality control and ﬂux sampling problems for

tower and aircraft data. Journal of Atmospheric and Oceanic Technology, 14,

512–526.

Webb EK, Pearman GI, Leuning R (1980) Correction of the ﬂux measurements for density effects due to heat and water vapour transfer.

Quarterly Journal of the Royal Meteorological Society, 106, 85–100.

2956 H . - M . L E I & D . - W. YA N G

r 2010 Blackwell Publishing Ltd, Global Change Biology, 16, 2944–2957Wilczak JM, Oncley SP, Stage SA (2001) Sonic anemometer tilt correction

algorithms. Boundary-Layer Meteorology, 99, 127–150.

Wilson K, Goldstein A, Falge E et al. (2002) Energy balance closure at

FLUXNET sites. Agricultural and Forest Meteorology, 113, 223–243.

Wu D, Yu Q, Lu C et al. (2006) Quantifying production potentials of winter

wheat in the North China plain. European Journal of Agronomy, 24,

226–235.

Xu L, Baldocchi DD (2004) Seasonal variation in carbon dioxide exchange

over a Mediterranean annual grassland in California. Agricultural and

Forest Meteorology, 1232, 79–96.

Yang D, Li C, Hu H et al. (2004) Analysis of water resources variability in the Yellow River of China during the last half century using

historical data. Water Resources Research, 40, W06502, doi: 10.1029/2003

WR002763.

Yu G, Zhang L, Sun X et al. (2008) Environmental controls over carbon

exchange of three forest ecosystems in eastern China. Global Change

Biology, 14, 2555–2571.

Zhang H, Wang X, You M et al. (1999) Water–yield relations and water-use

efﬁciency of winter wheat in the North China plain. Irrigation Science,

19, 37–45.

Zhang Y, Yu Q, Jiang J et al. (2008) Calibration of Terra/MODIS gross

primary production over an irrigated cropland on the North China

plain and an alpine meadow on the Tibetan Plateau. Global Change

Biology, 14, 757–767.