timal Dam Operation during Flood Season using a Distributed Hydrological Model

and a Heuristic Algorithm

Oliver Cristian SAAVEDRA VALERIANO, Researcher

Department of Civil Engineering, University of Tokyo

(7-3-1 Hongo, Bunkyo-ku, Tokyo 113-8656)

Toshio KOIKE, Professor

Department of Civil Engineering, University of Tokyo

(7-3-1 Hongo, Bunkyo-ku, Tokyo 113-8656)

Kun YANG, Professor

TEL, Institute of Tibetan Plateau Research, Chinese Academy of Sciences

(Beijing 100085, China)

Dawen YANG, Professor

Department of Hydraulic Engineering, Tsinghua University

(Beijing 100084, China)

Abstract: A  physically based distributed hydrological model is coupled with  an

optimization algorithm for joint dam operation  to reduce flood peaks down stream. The

decision variables are the release-inflow ratios. The heuristic algorithm seeds different

release scenarios attempting to find the most suitable combination. The objective is to

reduce the flood peak down stream, and the objective function is to minimize the difference

between the simulated and threshold discharges. The latter depends on the purpose of flood

management at the basin. Here, it is proposed as the mean discharge during heavy rainfall

and is used to start special dam operation. In order to  fulfill the objective function, the

reservoirs are expected to release before the flood event takes place and close gates during

the flood peaks to replenish the released water beforehand.  The developed system was

applied to the upper Tone River in Japan where the optimal release schedule from two key

dams was obtained. The observed weather radar products  were input to the hydrological

model to simulate the discharge within the river network. Then, the simulated inflows were

input to the dam storage functions. The release is routed down stream and the river

discharge is evaluated at the control point. The results indicate that the proposed integrated

operation can  effectively reduce  a  flood  peak suggesting  the feasibility  of  real-time

operation in future developments.

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

Key words: Flood peak reduction, Multi-reservoir operation, Optimization algorithm,

Optimal dam release, Tone River, Japan

INTRODUCTION

Extreme events, like heavy rainfall, usually occur due to large water cycle fluctuations at

global and regional scales, while disasters and damages occur at local scale. The Fourth

Assessment Report of the Intergovernmental Panel on Climate Change (IPCC) summarized

and projected the trends of precipitation in past and future as follows: "the frequency of

heavy precipitation events has increased over most land areas, consistent with warming and

observed increases of atmospheric water vapor."; and "It is very likely that heavy

precipitation events will continue to become more frequent.", respectively (IPCC, 2007).

The flood hazards will be intensified due to the global warming. This situation is

particularly evident in humid regions such as South East Asia affected by tropical cyclones.

Also known as typhoons, they bring expected heavy rainfall good for agriculture but they

might turn in to extreme flood peaks causing  tremendous  disasters in urbanized or

cultivated areas. A flood peak can be dramatically reduced by appropriate dam operation

assuming that the dam’s reservoir capacity is sufficient to attenuate floods. The application

of existing rule curves according to present water level and inflow conditions has a

limitation during these extreme events. The experience and judgment of dam operators is

also required to evaluate downstream situation. Therefore, an optimal release system might

be very useful to assist dam operators in decision making during extreme events.

The mathematical approaches to face the optimal reservoir operation during the 60’s and

70’s were summarized by Yeh (1985). It was distinguished mainly fours models: linear,

dynamic, and nonlinear programming, and simulation. The simulation approach was

suggested to be efficient to overcome some limitations of the three former traditional

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

programming methods (Wurbs, 1993; Chen, 2003). A couple of decades later Labadie

(2004) reported the benefit of heuristic programming models to optimize reservoir

operation systems. For instances, Oliveira and Loucks (1997) reported the optimization of

operating rules for multi-reservoir systems taking advantage of genetic algorithm (GA).

Only lately, Chen (2003) and Ngo et al. (2007) successfully applied a simulation model

with real-coded GA and Shuffled Complex Evolution (SCE) in Taiwan and Vietnam

respectively. These studies focused on the optimization of the rule curves, but again the

dam operators might still require an assistance tool during extreme events. To overcome

this lack and expand the application of heuristic algorithms in dam operation, this work

attempts optimal release of a multi-reservoir system by setting a threshold discharge at a

protecting point to reduce flood peaks. Then, the existing rule curves are not the targeted

variables to be optimized; instead the release as a function of decision variables in eventbased approach. Different from later three reports, this study is conceived towards real-time

operation using forecast input in future works.

The main goal of the present study is to evaluate the success of a coupled hydrologicreservoir-optimization scheme for predicting and reducing downstream flood peaks during

heavy rainfall. The simulation model chosen is the Geo-morphological Based Hydrological

Model (GBHM) developed by Yang et al. (2002b). A simple mass balance is used for dam

network operation. The control problem is solved by the SCE attempts to find the most

suitable value within a feasible parameter space (Duan et al., 1992). The efficiency and

robustness of the SCE has been shown  by comparing against a variety of methods (e.g.

Hogue et al., 2000; Cheng et al., 2005 among others). This algorithm is well-known in

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

hydrology community mainly for parameter estimation of rainfall-runoff models. This work

extends the application of the SCE as integrated reservoir operation during heavy rainfall.

The present paper is divided into six sections. The problem formulation and solution with

proposed system is introduced in the Methods section.  The application in Tone River is

presented in the Application section. The following section gives the obtained results and

discussion, and the last section presents concluding remarks.

METHODS

In this section, the problem is stated and the solution is searched through a combined

system. This includes a distributed hydrological model, dam network operation function,

and optimization algorithm.

Problem Formulation

The optimization problem for the operation of multi-reservoir system during heavy rainfall

is stated as below:

Objective: Minimize the flood peak at the control point downstream by having enough

flood volume attenuation at the reservoirs beforehand.

Strategy: Minimize the difference between the simulated  Q

t

sim and threshold discharge

Qthre at the control point during the optimization horizon.

Objective function: Minimize Z the difference of Q

t

sim and Qthreas:

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

2

( )

_

t

sim thre

t T

Q Q

Minimize Z

T



  

 

  

 

 



(1)

where t is the time step of the simulation model and T represents the set of all discrete time

steps over the period that the optimization is being performed. Besides the model

parameters and input data, the simulated discharge at the control point depends on the

release of upper dams as:

( )

t

Q f index

sim

 dam

(2)

Optimize: the decision variables indexdam are defined as release-inflow ratios. Their upper

boundary is set to the maximum observed ratio of outflow to inflow from available records.

The lower boundary is set to zero meaning the gates are completely closed.

Constraints: The main dam constraints are:

- If the suggested release exceeds the maximum capabilities according to water level, the

latter is assigned.

- If the release exceeds available stored flood volume, then release is assigned according to

available inflow.

- If water level reaches maximum, then free overflow is activated according to spillway

capabilities.

Solution approach

Reported literature (Cranmer, 2001; Yang et al., 2004; Saavedra et al., 2006 and others) has

demonstrated that distributed hydrological models fed by radar product inputs can improve

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

the estimation of stream flow. This is an advantage to track spatial variability and calculate

the inflow to different reservoirs simultaneously. Due to proven performance and efficiency

(Yang et al., 2002b), the GBHM was selected as a simulation model. The SCE was chosen

as optimization algorithm to be combined with the GBHM to solve the formulated problem.

In the present system SCE drives the GBHM seeding different decision variables defining

the release in order to obtain the simulated discharge at the control point. Then, the

objective function is evaluated as seen in  Eq. 1 and  Fig. 1. This function requires a

threshold discharge Qthre which is introduced to consider the situation downstream in the

optimization process. Actually, it suggests the system to start under the presence of a

potential flood event. Then, it can be understood as the edge stream flow at the control

point to begin a special flood management using upstream dams. It is expected to be higher

than the annual mean average Qyr_mean. This study proposes to calculate Qthre by averaging

all hourly discharge values Qi

that exceed the annual mean stream flow. In this way, the

flood peaks due to heavy rainfall are targeted.

1

;

N

i

thre

i

Q

Q



n

                       Q Q i yr mean

 _

(3)

where  n is the number of records. The intersection of the simulated discharge and the

threshold defines two stages as seen at right side of Fig. 1. The gap volume during stage I is

expected to be reduced by releasing water from the upper dams. While during stage II, the

opposite, simulated flood peak is expected to be reduced by partial or total gates’ closure.

The dam release is proposed as a linear function of the inflow similarly as Hanasaki et al.

(2006) proposed in yearly basis balance applications. However, here the proportionality

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

coefficient is the decision variable, indexdam

*

dam dam

release Inflow index     (4)

The number of decision variables is defined by the number of dams considered. At each

SCE iteration loop,  the objective function z is calculated and the best performances are

considered for next seeding.

Selection of simulation model

The GBHM is a physically-based hydrological model that simulates hydrological processes

using the governing equations of continuity, momentum and energy in two modules, Yang

et al. (2002a). The computational unit is a geometrically symmetrical hillslope, a rectangular inclined plane with a defined length and unit width, Yang  et al. (2002b). The

inclination angle is given by the surface slope, and bedrock is assumed to be parallel to the

surface. First, a hillslope module simulates hydrological processes such as canopy,

interception, evapo-transpiration, infiltration, surface flow, and subsurface flow, as well as

exchanges between groundwater and surface water. The vertical plane is divided in several

layers including canopy, soil surface, unsaturated zone and groundwater layer. The actual

interception is determined by the precipitation amount and the deficit of canopy water

storage. The actual evapo-transpiration is calculated as evaporation from canopy water

storage, transpiration from root zone, evaporation from surface storage and evaporation

from soil surface. The unsaturated zone is divided in several layers and the subsurface flow

is governed by Richards’ equation. The surface runoff is generated due to infiltration and

saturation excess flowing through the hillslope, Yang et al. (2002a). Actually, the surface

Fig. 3

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

runoff and subsurface flow become the lateral inflow to the river. The equations for the

ground water flow are mass balance and Darcy’s law. Second, the River network routes

water using the kinematic wave approach which is solved by finite-difference

approximation. This simulation sequence is performed at each sub-basin and linked by the

Pfafstetter scheme Verdin & Verdin (1999). The topography obtained from Digital

Elevation Models (DEM) defines the flow direction and accumulation pattern of the basin.

Moreover, every sub-basin is divided into a number of flow intervals. These intervals

follow the flow path from outlet to sources. Actually, a flow interval is defined by two

contour lines of flow distance from outlet obtained using a geographical information system

(GIS). The flow interval length can be defined as twice the simulation grid size. The River

flow routing module then conducts gathered water from each flow interval from sources to

the outlet direction along the main River channel which is lumped within each sub-basin.

This procedure dramatically reduces computing time because it  is a one-dimensional

simulation relying on the geo-morphological properties of the basin. See the double framed

box in Fig. 1

Dam operation module

The stream flow within the river network might be altered by the existing dams. Therefore,

a dam function is needed. First, the inflow Qin is calculated at upstream flow interval by

the GBHM as intake to the dam (Yang et al., 2004; Saavedra et al. (2006). A simple storage

function approach was used to express the change in volume within a time interval ∆t, as

the  inflow minus outflow from  a  dam (Ponce, 1989). Then,  the  reservoir storage at the

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

current time step, V2, can be obtained as

1 2

2

2 1

2

Q in Q in

V V Q out t

    

       

   

(5)

where the subscript 1 refers to the last time step. Note that the release  Q

2

out is assumed

constant between time steps 1 and 2. Both inflows Q

1,2

in to the reservoir are provided by the

GBHM as in the dashed box of Fig. 1. The last time step volume V1 needs to be set as initial

condition. Then, using the h-v curve the water level can be calculated. In normal conditions,

the release can be calculated using an operational rule curve. However, during heavy rainfall

the release needs manual operation. Here, it is a linear function of the inflow and the decision

variable is suggested by the SCE. Once the release is defined, flow is routed downstream by

the GBHM.

Selection of optimization algorithm

The heuristic algorithm SCE which searches for the global optima developed by Duan et al.

(1992) was chosen. The efficiency and robustness of SCE has been shown by comparing

against a variety of methods (e.g. Hogue et al., 2000; Cheng et al., 2005 among others).

This has being used widely in calibration of hydrological models, but here the application is

in dam operation. Firstly, a sample of points is distributed stochastically over the feasible

decision variable space by defining the lower and upper bounds  of each variable to be

optimized. Every point is meant to represent a member of a population for which only the

best fit will be kept. Each individual is characterized by its genetic information, which is a

complete set of variable values. By changing the genetic information the population

Fig. 1

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

develops towards an optimum fit. To this purpose the initial sample is partitioned into

several sub-samples, namely complexes. In  each complex, the varying combination of

points produces offspring  by the downhill simplex procedure of Nelder (1965). The

probability of an individual taking part in the reproduction is proportional to its fitness. The

former points with lower fitness are replaced by the offspring.

STUDY AREA

The upper Tone River basin, our target area, is located in the northern headwaters of the

Tone River basin, in the Kanto region of Japan, as indicated in gray on the left side of Fig.

2. The Tone River is a very important source of water supply, irrigation and power

generation for the Tokyo Metropolitan area and surroundings. Therefore, its management is

crucial for  the region. A delineated basin area of 3300 km

2

was defined down to  the

Maebashi discharge gauge as seen in Fig. 2. The main River channel flows north to south.

The elevation varies from 100 to about 2500 m and the mean is about 1020 m. The longterm average precipitation is about 1500 mm per year. In addition, heavy rainfall events

occur from July to October and are commonly associated with typhoons and seasonal front

activities. Particularly, typhoons bring the highest heavy rainfall such as the one recorded in

the region took place in September 1947 with 171 mm within 3 days caused by typhoon

Catherine, resulting in catastrophic flooding with 1.6 million people affected. At that event,

the flooding area also included Tokyo metropolitan area since the embankment was broken.

Input data

Fig. 2

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

Firstly, an aggregated 500 m grid from an original 50 m resolution of the Digital Elevation

Model (DEM) was employed as the computing grid. Secondly, land use, soil type and

geological maps were prepared for the study area using GIS. A 100 m resolution land use

data available for the region was classified into 6 categories. Among them, forest and

grasslands were the most dominant representing 79.3 % and 9.5 % of the total area

respectively. Thematic maps such as  surface terrain slope, topsoil depth, and hillslope

length were then derived from the basic data above using GIS (Saavedra et al. 2006). The

observed radar products  calibrated with rain gauge was obtained from the Automated

Meteorological Data Acquisition System (AMeDAS) and delineated to the study area. The

temporal resolution is 1 hour at 2.5 km.

Reservoir characteristics

Upstream of Iwamoto gauge, there are five multi-purpose operating dams, see Fig. 2. Their

main characteristics are summarized in Table 1. Their storage capabilities vary according

to the topography and height of embankment. The reservoirs are operated using their own

rule curves which are independent among them. During the flood season, the operation

becomes manual where the release is decided according to the actual water level of the

reservoir, the inflow to the reservoir and the water use demand (MOC, 1995). Moreover, in

an extreme event, the reservoir release is determined according to the judgment/experience

of the director of the reservoir operation office, considering the state of the reservoir and

the downstream flood conditions. The normal operation for each reservoir was simulated

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

already by Yang et al. (2004). This study attempts to support the reservoir operation office

during extreme events to define the suitable reservoir release after an integrated

consideration of the reservoirs, simulated inflow, and situation downstream.

Hydrological model calibration

Model parameters were calibrated by minimizing the difference between observed and

simulated discharges at gauges. The RMSE error was chosen to focus in the peaks of the

hydrographs. In decreasing order of sensitivity: the saturated hydraulic conductivity,

volumetric soil moisture, soil anisotropic, maximum surface storage were calibrated for

each soil and land use type.

RESULTS AND DISCUSSION

The objective of this application was to examine the effectiveness of the coupled GBHMSCE system in optimal dam operation during flood event 21-23 August 2001, one of the

highest peaks within the last decade. The hydrological model GBHM runs at 1-h time step.

The initial conditions  such as  the  soil moisture and ground water depth  were obtained

running the model from 1

st

of June until 20

th

of August 2001 using the observed data.

The operation of Sonohara and Fujiwara dams was chosen to be optimized with a typical

24-h operation horizon. These two dams are located within the main streams (see Fig. 2)

and their large drainage areas (see Table 1) play a key role for flood control in Upper Tone

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

River. The objective function was set  at  Iwamoto gauge. Using hourly observed stream

flow from 2000 to 2005 the threshold discharge was found 200 m

3

/s. The upper boundary

of the decision variables for Sonohara and Fujiwara dams  were 50 and 80 respectively

according to the maximum recorded ratios  of release to inflow. The lower boundary for

both was zero, and the initial condition one. The flood peak surpassing the threshold was

identified at noon time of 21

st

. In order to separate both stages of the flood control as seen

in Fig. 1, one decision variable per stage per dam was used. Then, four decision variables

were used to start the system. The optimized decision values were obtained after the system

tried different combinations seeded by the SCE, Table 2. The very first 12 h, the release is

encouraged with high ratio magnitudes. Afterwards, they tend to zero according to

simulated inflow. The flood peak  of  21-23 August 2001 was reduced successfully at  the

Iwamoto gauge as seen in Fig. 3b by 21 % compared to the simulated without optimization.

The objective function Z was reduced by 41% for the first optimization horizon. This was

possible due to the release of water at stage I and storage of water at stage II. Fujiwara dam

operated following the optimized release during the entire flood event. Actually, Fujiwara

reservoir could have control larger intensities of rainfall due to its storage capacity. On the

other hand, the capacity of the Sonohara dam showed a limitation for flood control due to

larger drainage area and low storage capacity. Therefore, this dam operated  as free

overflow from 3 pm on 22 August as seen in Fig. 4. At the end, the simulated water level of

both reservoirs was higher than the observed ones which show the availability for future

hydro power generation and water uses. The initial condition of the decision variables was

set to one which allowed the first scenario analysis without dam effect. From there, it is

expected to reduce Z. If the decision variables are greater than 1, higher release than inflow

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

discharge was evaluated. If the values are between zero and one, lower release than inflow

is analyzed.

This event was considered as a flood warning by the reservoir operation office. Actually, a

special operation was performed by Fujiwara dam to reduce the flood peak downstream as

seen the fluctuation of the observed water level at Fig. 4a. On the other hand, the simulated

dam operation increased the release discharge and kept the gates almost closed during the

peak. This procedure enabled higher flood reduction at the control point and higher water

replenishment. Then, the system could have assisted the reservoir operation office to

improve the flood management during special events that require down stream

consideration and integrated reservoir operation. The distributed hydrological model

provides the analysis at the inlets to the reservoir, water level fluctuation and down stream

condition simultaneously.

Execution time of one-hundred iterations lasted about 60 minutes in a personal computer

Pentium IV 1.3 GHz processor which could be even reduced using parallel processors. This

shows the implementation feasibility in real-time operation.

CONCLUSIONS

From the  above application it can be concluded that the new dam operation scheme

coupling a distributed hydrological model with an optimization algorithm using a threshold

discharge can be applied to other small River basins with humid climate and moderate

vegetation with operating gated dams. During extreme events, the system could support the

reservoir operation office to define the integrated reservoir release. The objective function

could consider more than one control point. Actually, it could be set at discharge gauges

downstream form each dam to assure the flood peak  reduction. Then, the terms from

control point could be integrated using weights according to priority in flood control. For

Fig. 4

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

example, Murakami gauge could be added as a control point with the operation of Yamba,

nowadays under construction. Then, the flood reduction could be evaluated at Maebashi

station.

The threshold discharge defined at the protecting point was selected using the average river

discharge during the rainy season. This allowed the start of the system as special flood

management. However, this can be modified according to specific flood warning levels,

embankment risk failure and flood management. The policy could consider the threshold

overflow which might be harmful as flood damage.

It was possible to achieve optimal dam operation using observed rainfall, as seen in Fig. 3b,

reducing the simulated flood peak at the control point. In practice,  this means  a “perfect

forecast” with 24-h lead-time issued every 12 hours. In real-time operation, the

optimization time step might be modified according to the lead-time of the quantitative

precipitation forecast. Then, the  optimized decisions will be updated at issuing interval.

Also, the  error forecast should be predicted using real-time observations; for example,

Kalman filtering technique might be helpful.

In actual operation, the system should address the high water release impact downstream

and community flood warning. Also, the maximum release should be a function of the

water level elevation and characteristics of the spillways. Finally, it is desirable to test the

system as a reference tool parallel to actual operation and evaluate its effectiveness as a

support to dam operators.

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

REFERENCES

Chen, L. 2003. Real coded genetic algorithm optimization of long term reservoir operation.

Journal of American Water Resources Association. 39 (5), pp 1157-1165.

Chen, R.-S., Pi L.-C., Hsieh C.-C. 2005. Application of parameter optimization method for

calibrating tank model. Journal of the American Water Resources Association, 41 (2), pp.

389–402.

Cranmer, A.J., Kowen, N., and Mousavi, S.F. 2001. Proving WATFLOD: modeling the

nonlinearities of hydrologic response to storm intensities,  Canadian journal of Civil

Engineers. 28, pp. 837-855.

Duan, Q., Sorooshian, S., and Gupta, V.K. 1992. Effective and Efficient Global

Optimization for Conceptual Rainfall-Runoff Models.  Water Resources Research, 28(4),

pp. 1015-1031.

Hanasaki, N., Kanae, S., and, Oki, T. 2006. A reservoir operation scheme for global river

routing models, Journal of Hydrology, Vol. 327, pp. 22-41.

Hogue, T.S., Sorooshian, S., and, Gupta, V.K., Holz, A., and Braatz. 2000. A multistep

automatic calibration scheme for River forecasting models, Journal of Hydrometeorology,

1, 542-542.

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

IPCC. 2007. Climate Change - The Physical Science Basis. Cambridge University Press,

996.

Labadie, J. W. 2004.  Optimal Operation of Multireservoir Systems State-of-the-Art

Review,  Journal of Water Resources Planning and Management, ASCE, 130(2), pp. 93-

111.

MOC, 1995. Reservoir operation manuals for the upper Tone River basin, in Japanese. The

Reservoir Management Office of the Upper Tone River Basin, Kanto Bureau,

Ministry of Construction, Japan.

Nelder, J.A. 1965. and Mead, R.: A simplex method for function minimization, Computer

Journal, 7, pp. 308–313.

Ngo, L.L., Madsen, H., Rosbjerg, D. 2007. Simulation and optimisation modelling

approach for operation of the Hoa Binh reservoir, Vietnam, Journal of Hydrology, 336, pp.

269-281.

Oliveira, R. and Loucks, D. 1997. Operating rules for multireservoir systems,  Water

Resources Research, 33(4), pp. 839-852.

Ponce, V.M. 1989.  Engineering hydrology: principle and practices, first edition,

Cambridge University Press/Prentice Hall.

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersAccepted Manuscript

Not Copyedited

Saavedra, O., Koike, T. and Yang, D. 2006. Application of a distributed hydrological

model coupled with dam operation for flood control purposes, Annual Journal of Hydraulic

Engineering, Japan Society of Civil Engineers JSCE, 50, pp. 61-66.

Verdin, K.L. & Verdin J.P. 1999. A Topological System for Delineation and Codification

of the Earth's River Basins, Journal of Hydrology, 218, 1-12.

Wurbs, R. A., 1993. Reservoir-System Simulation and Optimization Models,  Journal of

Water Resources Planning and Management, ASCE, 119(4), pp. 455-472.

Yang, D., Herath, S. and Musiake K. 2002a. Hillslope-based hydrological model using

catchment area and width functions, Hydrological Sciences Journal, 47, pp. 49-65.

Yang, D., Oki, T. Herath, S. & Musiake K. 2002b. A Geomorphology-based hydrological

model and its applications. In Mathematical Models of Small Watershed Hydrology and

Applications (ed. by V. P. Singh & D. K. Frevert), Chap. 9, p. 259–300. Water Resources

Publications, Littleton, Colorado, USA.

Yang, D., Koike, T., and Tanizawa, H. 2004. Application of a distributed hydrological

model and weather radar observations for flood management, Hydrological Processes, 18,

pp.3119-3132.

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil EngineersYeh, W.W-G. 1985. Reservoir management and operation models: a state-of-the-art

review, Water Resources Research, 21(12), pp. 1797-1818.

Table 1. Characteristics of dams in upper Tone River

Name of Dam Complete [year] Drainage [km

2

] Capacity [Mm

3

]

1. Aimata 1958 111.2 25

2. Fujiwara 1958 401.5 90

3. Naramata 1990 60.7 90

4. Sonohara 1966 494.2 20.3

5. Yagisawa 1967 167.5 204.3

6. Yamba Not yet 703.8 107.5

Table 2. Optimized dam operation schedule

Decisions variables Min Z Iterations

Year Month Day Hour

Index1

Fujiwara

Index2

Sonohara reduction number

2001 8 21 13 79.120 42.994

41 % 887

2001 8 22 01 0.001 8.472

2001 8 22 13 0.022 0.005

12% 564

2001 8 23 01 0.004 0.65

Accepted Manuscript

Not Copyedited

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil Engineers)LJ2YHUYLHZRIFRXSOHG*%+05HVHUYRLU6&(V\VWHP

4WKUHVKROG

4

7LPH

4VLP

6WDJH, 6WDJH,,

&RQWURO3RLQW

4

4 RXW

LQ

LQGH[

*%+00RGHO

*ULGEDVHGEDVLQ
'(0VRLOW\SH

+LOOVORSH

+\GURORJLFDOSURFHVVHV

5LYHUURXWLQJ

,QSXWGDWD

2EVHUYHG

5DGDU5DLQIDOO

2XWSXWGDWD

'DP¶V9RO	ZO

'DPIXQFWLRQ

4

RXW 4

LQ

LQGH[

WRXW4

4 LQ 4 LQ

99 '

¹

·

©

§

¹

·

©

§

5LYHUGLVFKDUJH

2EMIXQFWLRQ

VDWLVILHG"

$GMXVWGHFLVLRQYDULDEOHV

LQGH[E\6&(

1R

<HV

2SWLPL]HGUHOHDVH

4VLP

9K

Fig1.pdf

Accepted Manuscript

Not Copyedited

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil Engineers)LJ/RFDWLRQRIGDPV
LQVTXDUHV

DQGGLVFKDUJHJDXJHV
LQWULDQJOHV

$LPDWD

)XMLZDUD

1DUDPDWD

6RQRKDUD

<DJLVDZD

<DPED

Fig2.pdf

Accepted Manuscript

Not Copyedited

Journal of Hydrologic Engineering. Submitted March 13, 2009; accepted November 16, 2009;

posted ahead of print November 18, 2009. doi:10.1061/(ASCE)HE.1943-5584.0000212

Copyright 2009 by the American Society of Civil Engineers