Differences in changes of potential evaporation in the

mountainous and oasis regions of the Tarim basin,

northwest China

HAN SongJun

1,2†

, HU HePing

2

, YANG DaWen

2

& LIU QunChang

1

1

Department of Irrigation and Drainage, China Institute of Water Resources and Hydropower Research, Beijing 100044, China;

2

State Key Laboratory of Hydro-Science and Engineering, Department of Hydraulic Engineering, Tsinghua University, Beijing

100084, China

Data from eleven meteorological stations in the  Tianshan mountains and the north slope of west

Kunlun mountains, and eighteen meteorological stations in the Kaidu- Kongque river, Akesu river, Kashiger river and Yankant river oases were examined to assess the differences in changes in potential

evaporation from 1960 to 2006 in the mountainous and oasis regions of the Tarim basin and the relationships of these changes to meteorological factors. The decreasing trends in potential evaporation

were primarily due to the decrease in the aerodynamic terms in both the mountainous and oasis regions, but the trends in the oasis regions were more pronounced. Based on the complementary relationship between potential and actual evaporation, the decreasing trends in potential evaporation appeared to be related to the increasing trends in precipitation in the mountainous regions and the increasing trends in water consumption in the oasis regions, thus reflecting the different impacts of

natural changes and anthropogenic influences.

potential evaporation, Tarim basin, climate change, anthropogenic influence

Potential evaporation is an important index in the study

of climate change and is related to several meteorological variables including radiation, air temperature, relative humidity and wind speed. Against a background of

global warming, obvious trends towards decreases in

potential evaporation have been found

[1―5]

, which have

prompted many studies to find the causes of these decreases

[5―7]

. Most of these studies have been conducted

in either regions without obvious human activities, such

as the Tibetan plateau

[6]

, or regions with substantial human activities, such as irrigation districts in arid or

sub-arid areas

[8]

. The decreasing trends in potential

evaporation can be influenced by natural large-scale

factors such as radiation, wind speed, etc.

[7,9]

, but can

also be a result of an increase in actual evaporation related to changes in the regional hydrological cycle influenced by human activities

[10]

.

In the last 50 years, significant trends in potential

evaporation have been found in the largest inland river

in China, the Tarim basin. Studying the trends in potential evaporation and their  contributions will provide

useful insights for ecological environment protection

and studies on the interactions of climate, hydrology

cycle and human activities. Nevertheless, large differences in hydrometeorological features as well as in human activities are found between the mountainous regions and plain oases of inland river basins in arid regions

[11,12]

. The Tarim basin shows significant changes in

the climate and hydrology characteristics in the surrounding mountains and oases, as well as anthro pogenic

Received September 6, 2008; accepted December 24, 2008

doi: 10.1007/s11431-009-0123-3

†

Corresponding author (email: hansj@iwhr.com)

Supported by the National Natural Science Foundation of China (Grant Nos.

50579031, 50721140161, 5067908) and the Key Projects of China in the National

Science & Technology Pillar Program (Grant No. 2006BAD11B08)

Sci China Ser E-Tech Sci | Jul. 2009 | vol. 52 | no. 7 | 1981-1989changes such as agricultural development and irrigation.

Trends in potential evaporation and their contributions

are also clearly different

[13]

.

In this study, the different changes in potential evaporation in the Tarim basin were examined and their origins in the mountainous and oasis regions were evaluated. The influences of air temperature, radiation, relative humidity and wind speed on potential evaporation

were also analyzed to determine the different impacts of

natural changes versus anthropogenic influences.

1  Study area and trend analysis method

1.1 Study area

Located in the east longitudes 71°39′―93°45′ and north

latitudes 34°20′―43°39′, the Tarim basin covers the

entire southern part of Xinjiang in western China. As the

largest inland river in China, the Tarim river consisted

historically of nine drainage systems although today there

are only three. The largest anabranch, the Akesu river,

originates from the Tianshan mountains in the northwest

of the basin, the Hotan river flows from the Kunlun

mountains and is located in the southwest of the basin,

while the Yarkant river is located between the Hotan and

Akesu rivers.

At the north end of the basin is the Tianshan mountain range and on the south is Kunlun mountain range,

and below the mountain range are alluvial plain oasis

areas and the Taklimakan desert. The characteristics of

terrain, land cover, climate and hydrology are distinctly

different in the mountainous and the oasis regions. In the

north and west mountainous regions, at altitude from

2000 to 5400 m, the land cover is mainly wasteland and

natural vegetation, while in the alluvial plains, at altitude

from 1000 to 1400 m, irrigated agricultural land is common in many oases. The oasis regions are extremely arid,

with annual precipitation less than 50 mm and pan

evaporation more than 2100 mm. A progressive increase

in precipitation to more than 400 mm and a progressive

decrease in pan evaporation to less than 1500 mm are

found at distance away from the oases and towards the

mountains. Rainfall-runoff is the primary hydrologic process in the mountainous regions, while runoff-evaporation is

the mainly hydrologic process in the oasis re- gions

[14,15]

.

Changes in potential evaporation in the Tianshan

mountains and the north slope of west Kunlun mountains, and in the oases along four anabranches have been

evaluated using meteorological data from 1960 to 2006

in the present study. Monthly meteorological data from

eight gauges in Tianshan mountain area (Baluntai, Bayinbuluk, Xiaoquzi, Daxigou, Tianci, Xinyuan, Zhaoshu

and Tekesi), one gauge (Aheqi station) on the south

slope of Tianshan mountain, one gauge (Tashikuergan

station) on the north slope of the west Kunlun mountains

and one gauge (Tuerhute station) on Pamirs plateau were

collected and used to represent the climate conditions in

mountainous regions of the Tarim basin

[13,16]

. The data

of the four gauges (Hesuo, Yanqi, Kuerle and Weili) in

the Kaidu-Kongque river basin, three gauges (Akesu,

Awati and Aler) in the Akesu river basin, seven gauges

(Yinjisha, Kashi, Yuepuhu, Jiashi, Atushi and Aketao) in

the Kashiger river basin, and five gauges (Yecheng,

Zepu, Shache, Maigaiti and Bachu) in the Yarkant river

basin were used to represent the climate conditions in

oases. A sketch map of the study area in Tarim basin is

shown in Figure 1.

1.2  Trend analysis

The non-parametric Mann-Kendall test was used to investigate possible trends in potential evaporation, meteorological variables and stream flows. In this test, it is

assumed that the observed data are serially independent.

However, certain meteorological and hydrological time

series may frequently display statistically significant se-

rial correlations and these correlations will increase the

probability that the Mann-Kendall test will detect a significant trend

[17]

. In order to limit the influence of serial

correlations on the Mann–Kendall test, a trend-free

pre-whitening method proposed by Yue et al.

[18]

was

used to remove this component.

In the analysis, the magnitude of the trend is given as

( )

median ,  ,

( )

X X j i

i j

j i

β

⎡ ⎤ −

= ⎢ ⎥ ∀ <

−

⎣ ⎦

(1)

where  Xj

and  Xi

are the time-series;  β is the slope. A

positive value indicates an “upward trend”, whereas a

negative value indicates a “downward trend”. The test

statistic ZMK is given as

( )

( )

MK

1 Var( ) ,              0,

0,                                        0,

1 Var( ) ,              0.

S S S

Z S

S S S

⎧ − >

= ⎨ =

⎪

+ <

⎩

(2)

When |ZMK|＞Z(1−α/2)

, where Z(1−α/2)

is the standard normal deviation and α /2 is the significance level for the

test, the hypothesis that there is no trend in the time se

1982 HAN SongJun et al. Sci China Ser E-Tech Sci | Jul. 2009 | vol. 52 | no. 7 | 1981-1989Figure 1  Sketch map of the study area in Tarim basin.

ries will be rejected. For example, when α =0.05 (or P=

0.05), the trend is significant when |ZMK|＞1.96. In eq. (2),

the Mann-Kendall’s statistic S is given by

( (3)

1

1 1

sgn ,

n n

k i

i k i

S X

−

= = +

= ∑ ∑ − X )

(4)

1,     0,

sgn( ) 0,    0,

1,   0,

θ

θ θ

θ

⎧ >

⎪

= = ⎨

⎪

⎩− <

2  Trends in potential evaporation

2.1  Difference in trends in potential evaporation

Different definitions and calculation methods exist for

the study of potential evaporation

[19,20]

. Among these,

the Penman potential evaporation is most widely

used in hydrology, agro-ecology and meteorology, as

it takes into consideration both the bulk mass transfer

and the energy budget for evaporation

[21,22]

. The Penman-Monteith method to estimate potential evaporation

for hypothetical reference grassland is also widely used

[22]

,

and its value is well-correlated with the potential evaporation

[23]

. In this study, the Penman potential evaporation is used to evaluate both the bulk mass transfer and energy budget influencing the trends in potential

evaporation. The long-term pan evaporation is also analyzed.

The Penman potential evaporation contains a

radiation term and a drying power term:

(5)

0 rad aero

E E E = + ,

( ) n

rad

,

R G

E

γ

Δ −

=

Δ +

(6)

( ) ( )(

*

aero 2 a

E f U e T 1 RH ),

γ

γ

=

Δ +

−

a

,

(7)

where E0 is the Penman potential evaporation, Erad and

Eaero are the radiation term and the drying power term,

respectively, Δ is the slope of the saturation vapor curve

at the temperature of the surface which evaporates at a

potential rate, γ is the psychrometric constant, Rn is the

net radiation, G is the ground heat flux,  and ea are the

saturated and actual vapor pressures of the air, respectively, and f (u) is the function of the wind speed at the

reference level U2. The radiation is the key to calculating

potential evaporation, and is usually calculated as follows:

*

a

e

(8)

s s s

R a b n N R = + ( / )

where Rs

is the shortwave radiation,  n/N is the relative

sunshine duration, Ra is the TOA radiation, as

and bs

are

parameters which are calibrated using the observed data

for each month at the radiation stations in the study area.

In the study of Penman potential evaporation, several

parameters and wind speed functions are calibrated in

different regions, while the equation modified by the

FAO in 1979 is used in this study.

Clear changes in the potential evaporation and pan

evaporation were found in the Tarim basin over the past

nearly 50 years. The trends and the significances of the

pan and Penman potential evaporation in the mountainous and oasis regions from 1960 to 2006 are listed in

Table 1, with the focus on analysis of the middle and

HAN SongJun et al. Sci China Ser E-Tech Sci | Jul. 2009 | vol. 52 | no. 7 | 1981-1989 1983Table 1  Trends and significance of Epan and E0 from 1960 to 2006 in the mountainous and the oasis regions of Tarim basin (mm/10a)

1960―2006  1960―1980  1995―2006

Epan E0 Epan E0 Epan E0

ZMK −1.65  −1.67  0.42  0.88  1.71  0.93

Middel

Trends  −16.88  −4.63  21.12  15.85  124.48  25.79

ZMK −2.59  −2.35  0.55  2.69  −1.25  2.96

Sorthwest

a)

Trends  −57.31  −13.50  3.89  41.88  −108.15  92.72

ZMK −3.75  −2.40  0.68  1.59  1.56  1.56

Mountainous region

Average

Trends  −39.32  −7.68  25.61  22.75  100.21  51.46

Kaidu-  ZMK −5.40  −6.65  −4.19  −2.95  1.71  2.34

Kongque  Trends  −97.89  −39.98  −177.03  −34.24  255.27  64.55

ZMK −2.39  −5.64  −3.08  −1.78  2.80  1.56

Akesu

Trends  −30.23  −32.06  −173.62  −9.36  169.37  45.51

ZMK −6.70  −6.25  −3.15  −0.94  −0.62  1.25

Karsh

Trends  −135.16  −41.98  −160.98  −8.50  10.73  84.80

ZMK −3.52  −6.14  −0.36  0.68  1.56  0.93

Yarkant

Trends  −46.94  −38.38  −40.94  10.18  185.33  48.07

ZMK −5.42  −6.53  −3.73  −1.65  0.78  2.02

Oases region

Average

Trends  −78.79  −36.68  −127.26  −8.96  185.13  52.71

a) The Epan trends are only for Tashkuergan station, as Epan data in the other gauges are unavailable.

southwest of the mountainous regions, and the oases

along the Kaidu-kongque river, Akesu river, Yarkant

river and the Karshiger river. Decreasing trends in pan

evaporation (Epan) and potential evaporation (E0) are

found in both the mountainous and the oasis regions, but

the decreasing trends in pan evaporation (78.79 mm/10a

averaged over all oasis stations) and potential evaporation (36.68 mm/10a) over oasis regions are more obvious. The trends in mountainous regions (39.32 mm/10a

and 7.68 mm/10a averaged over all mountainous stations) were not nearly as pronounced.

The station averaged annual pan evaporation and potential evaporation anomaly from 1960 to 2006 in the

mountainous and the oasis regions are shown in Figure 2.

The time series of the pan evaporation and potential

evaporation are similar in both regions and the calculated

correlations between the pan evaporation and the potential evaporation are 0.82 and 0.90 for mountains and oases, respectively. Therefore, only the changes in potential

evaporation were evaluated further. In the mountainous

Figure 2  Annual variations in anomaly of averaged potential evaporation and pan evaporation in (a) mountainous regions and (b) oasis regions of the

Tarim basin.

1984 HAN SongJun et al. Sci China Ser E-Tech Sci | Jul. 2009 | vol. 52 | no. 7 | 1981-1989regions, a slightly increasing trend in potential evaporation from 1960 to the end of the 1970s was found, then

the potential evaporation decreased continuously to the

middle of the 1990s, and it increased slightly to 2006. In

contrast, the change of average potential evaporation in

the oases regions is more obvious, decreasing continuously to the middle of the 1990s, followed by a more

obvious increase from the middle of the 1990s to 2006.

In order to compare the trends in E0 in the mountainous and oasis regions further, the trends in E0 for different stations are plotted with annual mean precipitation in

Figure 3. Although E0 decreased at most of the stations

in the mountainous regions, significant trends were

found only at three stations, while decreasing trends in

the oases regions are more obvious. The significance of

the tests for most stations is  P＞0.05, while slight increasing trends were only found at Akesu station, and no

obvious trend was found at Bachu station.

Figure 3  Plots of trends in E0 with respect to annual mean precipitation

for stations in the mountainous and oasis regions of the Tarim basin.

2.2  Factors influencing changing potential evaporation

The changing potential evaporation is related to several

meteorological variables, including radiation, cloudiness,

air temperature, wind speed, relative humidity, etc. Among

these, shortwave radiation is the main factor influencing

the radiation term, while the wind speed and relative

humidity are the main factors influencing the aerodynamic term. The change of  E0 in the Tarim basin is

strongly influenced by changes in these meteorological

variables.

The trends and significance in averaged air temperature, precipitation, short wave radiation, relative humidity, and wind speed for the mountainous and oasis regions are listed in Table 2. The pan evaporation paradox

with increasing air temperature and decreasing pan

evaporation (or potential evaporation) exists in both the

mountainous and oasis regions, while the trends in air

temperature and precipitation are in accord with that in

northwest China. Decreasing trends in radiation and

wind speed at 2 m, and increasing trends of relative humidity exist in the mountainous and oasis regions.

However, the increasing trends of air temperature, daily

temperature difference and precipitation are more significant in the mountainous regions than in oasis regions.

On the other hand, in the oasis regions, the trends of

relative humidity and wind speed are more obvious.

The trends and significance of the radiation (Erad) and

aerodynamic (Eaero) terms of E0 for the mountainous and

oasis regions are also listed in Table 2. The trends of the

aerodynamic term in the mountainous and oasis regions

are both clear, but the slope in the oases regions is

steeper than that for the mountainous regions. In contrast,

there is no significant trend in the radiation term in the

mountainous regions, and the slope of the radiation term

in the oasis regions is much smaller than that of the

aerodynamic term.

In order to analyze the influences of changes in meteorological variables on the potential evaporation, the

correlation coefficients between  E0,  Erad and  Eaero with

air temperature (Ta), radiation (Rs

) and relative humidity

(RH) and wind speed (U2) are listed in Table 3. High

correlations between  E0 and  Rs

,  U2 and  RH are found.

These correlations suggest that Rs

and RH are the major

environmental factors controlling  E0 in mountainous

regions, while U2 and RH are the major environmental

Table 2   Trends of averaged meteorological variables related to potential evaporation from 1960 to 2006 in the mountainous and oasis regions of the

Tarim basin

Ta (℃/10a) ΔTa (℃/10a) P (mm/10a) Rs

(W/(m

2

.10a)) RH (%/10a) U2

(m/(s.10a)) Erad (mm/10a) Eaero (mm/10a)

Mountainous  ZMK 3.86  −6.38  2.58  −4.62  3.24  −5.66  0.06  −3.12

region  Trends  0.27  −0.27  12.28  −1.42  0.66  −0.08  0.68  −8.49

ZMK 3.71  −4.15  2.29  −2.67  3.48  −8.92  3.2  −6.97

Oases region

Trends  0.22  −0.17  6.19  −0.98  1.01  −0.24  4.4  −41.7

Note: Ta is air temperature, ΔTa and P are average daily temperature differences and precipitation, respectively, and RH is relative humidity.

HAN SongJun et al. Sci China Ser E-Tech Sci | Jul. 2009 | vol. 52 | no. 7 | 1981-1989 1985Table 3  Correlation coefficients between annual E0 and meteorological variables in mountainous and oasis regions of Tarim basin

Region  Parameter  Ta Rs RH U2

Erad 0.57 0.50 −0.42 0.03

Mountainous region Eaero 0.00 0.83 −0.82 0.63

E0 0.17 0.82 −0.78 0.51

Erad 0.59  0.45 0.36  −0.56

Oasis region Eaero −0.30  0.29 −0.73  0.96

E0 −0.21  0.40 −0.72  0.93

factors in oasis regions.

To quantify the influence of Rs

, U2, Ta and RH on the

decreasing trend in  E0, a recovered stationary series

method

[6,7]

was applied. Trends in  Rs

,  U2,  Ta and  RH

were removed to obtain stationary time series, and  E0

was calculated from the detrended data series. E0 values

from the stationary and original time series were compared in Figure 4. The decreasing trends in E0 over the

mountainous and oasis regions are both more significant

in the recovered stationary series by  Ta, which means

that the increasing trends in Ta will increase E0, and the

influence is more obvious for the mountainous regions.

In the recovered stationary series by radiation, relative

humidity and wind speed, the decreasing trends in E0 are

weaker, while it is more obvious by radiation over

mountainous regions and by wind speed in the oases

region. The decreasing trends in  Rs

,  U2 and increasing

trend in RH were successively the causes of the decrease

of E0 over the mountainous regions, while the decreasing trends in  U2,  Rs

and increasing trends in  RH were

successively the causes of the decrease of E0 over oasis

regions. The influence of the decreasing trend in wind

speed is more obvious than the other two factors.

The different influences of meteorological variables

on E0 in the mountainous and oasis regions were evaluated in terms of the different impacts of the natural

changes and the anthropogenic influences on potential

evaporation. The annual variations in five-year anomaly

of E0 and U2 over the mountainous and oasis regions of

the Tarim basin are compared with the average value

over the whole of China in Figure 5. The variations of E0

and  U2 in the mountainous regions are similar to that

over the whole of China, while the variations in oasis

regions are clearly different. It could be concluded that a

change in E0 in the mountainous regions is more related

to natural changes at a large scale, while the change in

E0 over the oasis regions is related as well to natural

changes through local climate changes caused by human

activities such as irrigation.

The decreasing trend in U2 over the mountainous regions in the Tarim basin is 0.08 m/(s·10a). This is close

to the trends in  U2 over the Tibetan plateau

[6]

and

Yangze river basin

[24]

, as well as many other regions

reported by Roderick

[7]

. However, the decreasing trend

in  U2 over oases in the Tarim basin is much larger, at

0.24 m/(s·10a). Similar trends in E0 were also found by

Alpert and Mandelin in Israel

[25]

, as well as Ozdogan and

Salvucci in Turkey

[8]

. Ozdogan and Salvucci concluded

Figure 4  Annual variations in the original annual potential evaporation (E0) and E0 recalculated from detrended environmental variables over (a) the

mountainous regions and (b) oasis regions.

1986 HAN SongJun et al. Sci China Ser E-Tech Sci | Jul. 2009 | vol. 52 | no. 7 | 1981-1989Figure 5  Annual variations in five-year anomaly of E0 and U2 over the mountainous and oasis regions in the Tarim basin and over the whole of China.

two possible reasons for the obvious decline in U2 over

oases with the expansion of irrigation. First, irrigated

crops will change surface roughness, and decrease wind

effects. The second explanation is that irrigation can

influence local circulation though the “oasis effect”,

which may change both the direction and magnitude of

wind

[26]

. Du and Maki

[27]

found in Turpan in Tarim basin

that wind speed in the oasis is smaller than in the desert

because of “oasis effect”, and crops, especially the

Shelter forest, prevent wind. In the oases of Tarim basin,

irrigation areas have been enlarged over the past 50

years, and the decreasing trend in U2 may be a result of

the joint influence of the above two reasons.

3  Reasons for the different changing

potential evaporations

Because of the interaction between land surface and atmosphere, the changes in actual evaporation are influenced by changes in potential evaporation. These, in turn,

will influence the changes in potential evaporation. The

interaction between actual and potential evaporations could

be evaluated by the complementary relationship

[10,28]

,

which states that as the surface dries, without changes in

available energy, the actual evaporation decreases and

potential evaporation increases with increases in latent

heat. As the dominant hydrological process in the mountainous region is rainfall-runoff, the variation in actual

evaporation is closely related with the change in precipitation

[29]

. In contrast, the changes in actual evaporation in oasis regions are clearly influenced by irrigation

[14,15]

. Therefore, the different reasons for changes in

potential evaporation could be evaluated by coupling the

complementary relationship and the different hydrological processes in the mountainous and oasis regions,

respectively. Han

[30,31]

derived a dimensionless form of

the complementary relationship in which the ratio of

actual evaporation to Penman potential evaporation is

expressed as a function of the proportion of radiation

term in Penman potential evaporation, i.e., E/E0 = f (Erad

/E0).

In the Budyko hypothesis

[32,33]

, the ratio of actual

evaporation to Penman potential evaporation is expressed as a function of the ratio of annual precipitation

to potential evaporation, i.e., E/E0 = f (P/E0).

Annual precipitation increased and potential evaporation decreased in the past nearly 50 years in the mountainous regions, the wetness index P/E0 increased clearly.

An increasing trend was also found in Erad /E0. The close

relationship between the changes in precipitation and

potential evaporation is reflected by the similar variations of P/E0 and Erad /E0 from 1960 to 2006 (Figure 6)

and similar phenomena have also been found in

non-humid regions in China by Yang

[34]

.

For the oasis regions with scarce precipitation, irrigation is the dominant water supply and the changes in

actual evaporation primarily result from the changes of

irrigation. The trends and significance of the annual inflow to the four oases in Tarim basin, and the annual

runoff of Alar station are listed in Table 4. The inflow

for all the four oases increases, but the inflow to the

main stream (runoff in Alar station) noticeably decreases,

and significant increasing trends for actual evaporation

are observed in the Kaidu-Kongque, Akesu, Yankant, and

Kash oases

[12,35]

. Therefore, it can be concluded that the

changes in potential evaporation in oasis regions are

related to the changes in irrigation. Taking Akesu oasis,

for example, the relationship between the changes in

irrigation and potential evaporation can be analyzed.

With the annual runoff from Xidaqiao station as the

HAN SongJun et al. Sci China Ser E-Tech Sci | Jul. 2009 | vol. 52 | no. 7 | 1981-1989 1987Figure 6  (a) Variations of annual Erad

/E0 and P/E0 in the mountainous region; (b) variations of annual Erad

/E0 and (P+Eirr

)/E0 in Akesu oasis.

Table 4  Trends and significance of the annual inflow of the four oases

and the annual runoff from Alar station

Kaidu-Kongque Akesu Kashi Yankant Alar

ZMK 2.84  3.79  1.58  1.95  −1.52

Trend

(10

8

m

3

)

0.17  0.44  0.10  0.28  −0.19

inflow into Akesu oasis, and the annual runoff from Alar

as the outflow, the annual water consumption (Eirr

) is

calculated by the inflow minus the outflow. The similar

increasing trends of (P+Eirr

)/E0 and Erad

/E0 in the Akesu

oasis (Figure 6(b)) shows that the decreasing trend in

potential evaporation over the Akesu oasis is closely

related to the increase in irrigation.

4  Conclusions

The different changes in potential evaporation from

1960 to 2006 and their relationships to meteorological

factors over the mountainous and oasis regions in the

Tarim basin were evaluated, and the different impacts of

the natural changes and the human activities on potential

evaporation were analyzed. The average decreasing trends

in potential evaporation from the oases (36.68 mm/10a) is

more apparent than that over the mountainous region

(7.68 mm/10a). Among the meteorological variables, the

correlation coefficient between the radiation and potential evaporation is the highest in the mountainous region

(0.82), while that between the wind speed and potential

evaporation is the highest in the oases (0.93). The decreasing trends in E0 are weakened the most in the recovered stationary series by radiation over mountainous

regions and by wind speed in oasis regions. It is concluded that the decreasing in potential evaporation is

mainly influenced by natural changes such as the decrease in radiation over the mountainous region and is

closely related to the changes in precipitation. In oasis

regions, the anthropogenic influences are the most significant, and the changes in potential evaporation are

closely related to the changes in irrigation.

The change in potential evaporation is influenced by

both the natural changes in large scale and local anthropogenic influences. The natural and anthropogenic influences are different in the mountainous and oasis regions of the Tarim basin. However, both factors should

be considered in the analysis of the trends in potential

evaporation for other regions.

Significant impacts of irrigation on potential evaporation are found in oasis regions in Tarim basin. The

changes in potential evaporation will conversely influence the water demand and water consumption in oasis

regions. The analysis in this paper is important to understand the oasis effect in arid region and to analyze the

influences of irrigation on environment, and to analyze

the influences of irrigation on potential evaporation is

also very important in water demand prediction and irrigation water management in oasis regions.

1 Gao G, Chen D L, Xu C Y, et al. Trend of estimated actual

evapotranspiration over China during 1960―2002. J Geophys Res,

2007, 112, D11120[doi]

2 Ohmura A, Wild M. Is the hydrological cycle accelerating? Science,

2002, 298(5597): 1345―1346[doi]

3 Peterson T, Golubev V, Groisman P. Evaporation losing its strength.

Nature, 1995, 393(6551): 687―688[doi]

4 Qiu X F, Liu C M, Zeng Y. Changes of pan evaporation in the recent

1988 HAN SongJun et al. Sci China Ser E-Tech Sci | Jul. 2009 | vol. 52 | no. 7 | 1981-198940 years over the Yellow River Basin (in Chinese). J Nat Res, 2003,

18(4): 437―442

5 Zuo H C, Li D L, Hu Y Q, et al. Characteristics of climatic trends and

correlation between pan-evaporation and environmental factors in the

last 40 years over China. Chinese Sci Bull, 2005, 50(12): 1235―1241

6 Zhang Y Q, Li C M, Tang Y H, et al. Trends in pan evaporation and

reference and actual evapotranspiration across the Tibetan Plateau. J

Geophys Res, 2007, 112, D12110[ doi]

7 Roderick M L, Rotstayn L D, Farquhar G D, et al. On the attribution of

changing pan evaporation. Geophys Res Lett, 2007, 34, L17403[doi]

8 Ozdogan M, Salvucci G D. Irrigation-induced changes in potential

evapotranspiration in southeastern Turkey: Test and application of

Bouchet's complementary hypothesis. Water Resour Res, 2004, 40,

W04301[doi]

9 Roderick M L, Farquhar G D. The cause of decreased pan evaporation

over the past 50 years. Science, 2002, 298(5597): 1410―1411

10 Brutsaert W A M. Hydrologic cycle explains the evaporation paradox.

Nature, 1998, 396(6706): 30[doi]

11 Tang Q C, Qu Y G, Zhou Y C. Hydrology and Water Resources Utilization in Arid Land of China (in Chinese). Beijing: Science Press, 1992

12 Li J F. The Weather climate Research in Taklimakan Desert and Coteau All Around (in Chinese). Bejing: Science Press, 2003

13 Yang Q, Lei J Q, Wei W S, et al. Effects of artificial oases on climate

change trend (in Chinese). Acta Ecol Sin, 2004, 24(12): 2728―2734

14 Hu H P, Tang Q H, Lei Z D, et al. Runoff-evaporation hydrological

model for arid plain oasis, 1, the model structure (in Chinese). Adv

Water Sci, 2004, 15(2): 140―145

15 Lei Z D, Hu H, Yang S, et al. Analysis on water consumption in oases

of the Tarim Basin (in Chinese). J Hydr Eng, 2006, 37(12):

1470―1475

16 Wang S, Wang Y, Wang J, et al. Change of climate and hydrology in

the Tarim River Basin during past 40 years and their impact (in Chinese). J Glaci Geocry, 2003, 25(3): 315―320

17 von Storch H. Misuses of statistical analysis in climate research. In:

Storch H V, Navarra A, eds. Analysis of Climate Variability: Applications of Statistical Techniques. New York: Springer-Verlag, 1995

18 Yue S, Pilon P, Phinney B, et al. The influence of autocorrelation on

the ability to detect trend in hydrological series. Hydrol Process, 2002,

16(9): 1807―1829[doi]

19 Granger R J. An examination of the concept of potential evaporation. J

Hydrol, 1989, 111(1-4): 9―19

20 Lhomme J P. Towards a rational definition of potential evaporation.

Hydrol Earth Syst Sc, 1997, 1(2): 257―264

21 Penman H L. Natural Evaporation from open water, bare soil and

grass. In: Proc Royal Soc London, Ser A, Math Phy Sci. London:

Royal Society of London, 1948

22 Allen R G, Pereira L S, Raes D, et al. Crop Evapotranspiration:

Guidelines for Computing Crop Water Requirements. Rome: Food

and Agriculture Organization of the United Nations, 1998

23 Yu L, Pereira L S, Teixeira J L. Update definition and computation of

reference evapotranspiration comparison with former method (in

Chinese). J Hyd Eng, 1997, (6): 27―33

24 Xu C Y, Gong L B, Jiang T, et al. Analysis of spatial distribution and

temporal trend of reference evapotrans- piration and pan evaporation

in Changjiang (Yangtze River) catchment. J Hydrol, 2006, 327(1-2):

81―93[doi]

25 Alpert P, Mandel M. Wind variability—An indicator for a mesoclimatic change in Israel. J Clim Appl Met, 1986, 25(11):

1568―1576[doi]

26 Oke T R. Boundary Layer Climate. Ney York: Halsted, 1978

27 Du M, Maki T. Mutual influence between the exploitation of desert

oases and the environmental change (in Chinese). J Nat Res, 1999,

14(4): 368―371

28 Bouchet R. Evapotranspiration  reelle at potentielle, signification

climatique. Int Assoc Sci Hydro Pub, 1963, 62(1): 134―142

29 Dooge J C I, Bruen M, Parmentier B. A simple model for estimating

the sensitivity of runoff to long-term changes in precipitation without

a change in vegetation. Adv Water Resour, 1999, 23(2):

153―163[doi]

30 Han S, Hu H, Tian F. Evaluating the advection-aridity model of

evaporation using data from field-sized surfaces of HEIFE. IAHS Pub,

2008, 322(2): 9―14

31 Han S. Study on Complementary Relationship of Evapotranspiration

and its Application in Tarim River Basin. Beijing: Tsinghua University Press, 2008

32 Budyko M I. Climate and Life. San Diego: Academic Press, 1974

33 Yang D, Sun F, Liu Z, et al. Analyzing spatial and temporal variability

of annual water-energy balance in non-humid regions of China using

the Budyko hypothesis. Water Resour Res, 2007, 43, W04426[doi]

34 Yang D, Fubao S, Zhiyu L, et al. Interpreting the complementary relationship in non-humid environments based on the Budyko and

Penman hypotheses. Geophys Res Lett, 2006, 33, L18402[doi]

35 Lei Z D, Zhen B L, Shang S H, et al. Formation and utilization of

water resources of Tarim River. Sci China Ser E-Tech Sci, 2001, 44(6):

615―624