An operational method to estimate evapotranspiration using MODIS

data during winter wheat growing season

YONGHONG YI†‡ and DAWEN YANG*†

†State Key Laboratory of Hydro-Science and Engineering, Department of Hydraulic

Engineering, Tsinghua University, Beijing, 100084, PR China.

‡The Numerical Terradynamic Simulation Group, University of Montana,

Missoula, MT, 59812, USA

(Received 1 July 2009; in final form 28 September 2009)

The Penman–Monteith (P-M) model has been widely used to estimate actual evapotranspiration (ET). However, its application is mainly constrained to within field

scales because the surface resistance under water stress at large scales is difficult to

define. The Normalized Difference Water Index (NDWI) derived from Moderate

Resolution Imaging Spectroradiometer (MODIS) data was shown to be sensitive to

the crop water content and water deficit, and used to estimate the surface resistance in

the P-M model. The modelled latent heat fluxes matched well with the eddy correlation observations, and the spatial distributions also showed a similar pattern as the

results from the one-layer model in an irrigated area at the downstream of Yellow

River. To reduce the influence of cloud and other atmospheric disturbances, the daily

surface resistance was retrieved from 8-day temporal composite MODIS

NDWI. The modelled daily ET showed consistent temporal changes with the observations during the wheat growing season. This method showed advantages over the

other remote sensing models, for example, the one-layer model, which required daily

radiative temperature inputs and cannot be implemented under cloudy conditions.

1. Introduction

Water shortage and uneven distribution of precipitation in time and space are major

limiting factors for the economic development and agricultural production in the

Northern China Plain. Winter wheat is the major crop in this area from winter to

spring, and its growth is greatly influenced by the rainfall distribution during this

period. The decreasing precipitation and increasing air temperature in this area due

to climate change mean that more crop irrigation is necessary, especially during the

winter wheat season (Yang et al. 2004, Cracknell and Varotsos 2007), and the water

conflict between irrigation and industrial use is becoming severe in the Yellow River

basin. To better manage the limited water resources, accurate assessment of crop water

consumption is required. Field sampling has been extensively used to measure crop

water consumption or actual evapotranspiration (ET) and estimate water stress by

measuring soil moisture from a scale of several metres up to several hundreds of metres.

However, it is difficult to make regional estimates from field observations due to large

heterogeneities in land cover and plantation (Maayar and Chen 2006). Remote sensing

data have obvious advantages over field observations and are widely used for regional

*Corresponding author. Email: yangdw@tsinghua.edu.cn

International Journal of Remote Sensing

ISSN 0143-1161 print/ISSN 1366-5901 online # 2011 Taylor & Francis

http://www.tandf.co.uk/journals

DOI: 10.1080/01431161.2010.492252

International Journal of Remote Sensing

iFirst, 2011, 1–18

Downloaded by [Tsinghua University] at 06:44 07 July 2011 water cycle studies since they can provide measurements of land surface status over

large areas (Jupp et al. 1998, Jiang and Islam 1999, Nishida et al. 2003, Su et al. 2003).

Derivation of ET estimates from remote sensing data is based on assessing the

surface energy balance by observing surface properties such as albedo, vegetation

cover, leaf area index (LAI) and surface temperature (Bastiaanssen et al. 1998, Jupp

et al. 1998). The available net radiation energy is partitioned into soil heat and

atmospheric convective fluxes including sensible heat and latent heat. The main differences between remote sensing models lie in the treatment of the observed surface and the

parameterization of the radiant and convective fluxes (Courault et al. 2005). The onelayer approach considers the land surface as a single component, while the two-layer or

multilayer approaches discriminate the soil and vegetation components, with different

characterization of canopy structure. The one-layer model is easy to run, but the

aerodynamic temperature defined in the model is generally different from the surface

temperature derived from remote sensing especially under sparse vegetation conditions

(Chehbouni et al. 1996, Su et al. 2001). The two-layer model incorporates the difference

between the two temperatures. However, it is difficult to solve the model without

knowing the soil and vegetation component temperatures when only one observation

of radiometric temperature is available (Norman et al. 1995, Kustas and Norman 1999,

French et al. 2005). Therefore, empirical assumptions have to be introduced to solve the

model due to the absence of satellite multi-angle thermal-infrared sensors. Two methods

are usually used: one builds the empirical relationship between radiometric temperature

and the component temperatures (or aerodynamic temperature) (Chehbouni et al.

2001); the other method reduces the two-layer model into a modified single-layer

model by providing an extra condition (Norman et al. 1995, Jupp et al. 1998, Kustas

and Norman 1999, French et al. 2005). As an example of the second method, the

Priestley–Taylor (P-T) equation is usually applied to initialize the canopy transpiration,

assuming the vegetation has suffered no water stress (e.g. Norman et al. 1995).

All the above models are sensitive to the uncertainty of the surface temperature

retrieval, which relies on remote sensing techniques and shows great uncertainty (Wan

et al. 2002). The surface temperature is very sensitive to atmospheric movement; methods for describing the corresponding fluctuation in surface temperature have been

widely investigated but not on the satellite observed temperature (Katul et al. 1998,

Varotsos 2005, Varotsos et al. 2007). The Penman–Monteith (P-M) model eliminates the

need for surface temperature and has been widely used for evaporation modelling, but

mostly at field scales (Courault et al. 2005). This is because the surface resistance under

unsaturated surfaces at large scales is usually difficult to estimate without intensive

sampling of soil moisture and crop growth parameters (Moran et al. 1994, Cleugh

et al. 2007, Mu et al. 2007). Therefore, the main objective of this article is to retrieve

surface resistance from remote sensing data and extend the application of P-M model at

a regional scale.

The Moderate Resolution Imaging Spectroradiometer (MODIS) onboard the

Terra and Aqua satellites provides observations twice a day on a near-daily basis

(every other day at the equator) at moderate spatial resolutions from 250 to 1000 m,

which makes it appealing for regional water and energy cycles monitoring (Kustas et al.

2003, Cleugh et al. 2007, Mu et al. 2007). Although sensors with higher spatial resolution, for Example, Landsat Thematic Mapper (TM) or Enhanced Thematic Mapper

(ETM) and Advanced Spaceborne Thermal Emission and Reflection Radiometer

(ASTER), are more desirable, these sensors have much lower temporal resolution,

and cloud contamination limits their application to monitoring of crop water use on

2 Y. Yi and D. Yang

Downloaded by [Tsinghua University] at 06:44 07 July 2011 a regular basis, as is needed for irrigation management. Moreover, the publication of

MODIS land surface products facilitates their application to ecology and hydrology

modelling without needing to make atmospheric and radiometric correction.

The objective of this article is to develop an operational method based on the P-M

model and MODIS data to estimate daily crop water consumption in an irrigated area

located at the downstream part of the Yellow River, to provide support for optimized

irrigation management. A water index derived from MODIS data was used to estimate

the surface resistance in P-M model, and the results were validated using field flux

observations and compared with the popular one-layer model.

2. Methodology

2.1 Study area and field experiments

Field experiments have been carried out around an eddy flux tower (116

3

0

15.3

00

E,

36

38

0

55.5

00

N, 30 m elevation) in the Weishan Irrigation Zone (WIZ) (115

24

0

–116

30

0

E, 36

12

0

–37

00

0

N) since April 2005. The WIZ and the location and surroundings

of the field experiment site are shown in figure 1. Within a radius of several kilometres

around the flux tower the croplands area is almost homogeneously covered by the

same crop. This region is part of the Northern China Plain and also the largest

irrigation zone in the downstream area of the Yellow River with a total area of

3600 km

2

. Three major channels provide irrigation for most of the area, with water

taken from the Yellow River in the south-eastern part. The rotation of winter wheat

Figure 1. The study area and the field site. (a) Weishan irrigation zone along the downstream

part of the Yellow River and the locations of the flux tower and three weather stations. (b) The

location of the flux tower for validation and its surroundings. The background is a false-colour

composite Landsat ETM image on 16 May 2000 (30 m, bands 4, 3, 2).

An operational method to estimate evapotranspiration 3

Downloaded by [Tsinghua University] at 06:44 07 July 2011 and summer corn is the local primary agricultural practice with crop plantation

occupying over 80% of the total area. The winter wheat season occurs between

October and June. Multi-year averaged precipitation in this zone is around 571 mm,

of which over 60% falls in the summer and less than 20% falls in the spring. Two or

three applications of irrigation are usually made during the fast-growing period of

wheat in the dry season, from March to May.

The flux tower was equipped with a net radiometer, soil heat flux plates and an eddy

covariance system. The energy balance closure was around 80% from the spring to

autumn, dropping to 60% in the winter. This could result from the underestimation of

turbulent heat fluxes at the flux tower, which occurred at some sites according to

FLUXNET (Baldocchi et al. 2001). The remaining terms in the energy balance equation

are redistributed into the turbulent fluxes according to the observed Bowen ratio. A set of

automatic agro-meteorological equipment was also installed to measure routine climate

data, including air temperature, relative humidity and wind speed. A groundwater network was used to record the groundwater level and two soil moisture profiles were

measured at depths of 5, 10, 20, 40, 80 and 160 cm. The crop growth parameters including

LAI, root mass and crop height were sampled every two weeks.

2.2 Estimating actual ET using P-M model and MODIS data

The P-M model is based on the energy balance and aerodynamics theory (Monteith

1964):

lE ¼

ðRn  G0Þ þ rCpðe

ðTaÞ  eaÞ=ra

þ ð1 þ rs=raÞ

; (1)

where E is the mass water ET rate, l is the latent heat of vaporization, lE together

represents the latent heat fluxes (W m

-2

), Rn is net radiation (W m

-2

), G0 is soil heat flux

(W m

-2

), Ta is the air temperature (

C) at reference height, e

*

(Ta) and ea are the saturation

vapour pressure (kPa) at temperature Ta and the actual vapour pressure (kPa) respectively.  is the slope of the saturated vapour pressure at the air temperature (kPa

C

-1

), r

is the air density (kg m

-3

), Cp is the air specific heat (J kg

-1

C

-1

),  is the psychrometric

constant (kPa

C

-1

) and ra

is the aerodynamic resistance (S m

-1

) and rs

is the surface

resistance (S m

-1

), which was mainly influenced by water availability and canopy

photosynthesis process. Estimating the surface resistance under water stress was the

major difficulty when applying the P-M method on actual ET estimation. Cleugh et al.

(2007) and Mu et al. (2007) used the LAI derived from MODIS data to estimate the

surface resistance. However, LAI, similar to Normalized Difference Vegetation Index

(NDVI), is more sensitive to the canopy biophysical parameters and may not be able to

effectively characterize the surface resistance under water stress conditions.

The radiative transfer model showed that leaf water was the dominant factor

influencing the leaf reflectance in the shortwave infrared (SWIR) wavelengths

(Ceccato et al. 2002). The Normalized Difference Water Index (NDWI) is a combination of the near-infrared (NIR) and SWIR wavelengths, defined as:

NDWI ¼

rNIR  rSWIR

rNIR þ rSWIR

; (2)

where rSWIR and rNIR are the reflectance in SWIR and NIR wavelengths respectively.

NDWI was shown to be sensitive to the canopy water stress and also showed a

response to the crop growth at the same time (Fensholt and Sandholt 2003, Jackson

4 Y. Yi and D. Yang

Downloaded by [Tsinghua University] at 06:44 07 July 2011 et al. 2004, Chen et al. 2005). Moreover, NDWI was more resistant to cloud effect and

other atmospheric disturbances (Yi et al. 2008). Therefore, the following is more

suitable for surface resistance estimation:

rs ¼ rs maxfðNDWIÞ ¼ rs maxð1  aðNDWIÞÞ; (3)

where rs

is the surface resistance (S m

-1

), and rs_max

is the maximum resistance (S m

-1

)

and can be regarded as the resistance when there is no vegetation cover and the soil

moisture is close to the wilting point or under water stress. fðNDWIÞ is a linear

expression of NDWI (with a as an empirical coefficient subject to calibration), which

describes the influence of surface moisture condition and crop growth. For the crop at

the same growth period, NDWI would decrease and surface resistance would increase if

the crop suffered water stress. Here the MODIS bands 7 and 2 centred at 2130 nm

(SWIR) and 858 nm (NIR) were used to calculate the NDWI index.

A one-layer model was also applied in this area to compare with the P-M model. The

heat transfer process between the land surface and atmosphere can be expressed as:

H ¼ rCp

Ts  Ta

ra þ rex

; (4)

where Ts

is the radiometric surface temperature (K) and Ta was the air temperature at

reference height (K). The excess resistance rex or a dimensionless heat transfer coefficient

B

-1

(B-sublayer stanton number) was used to adjust the difference between the aerodynamic temperature and surface temperature derived from remote sensing (Stewart

et al. 1994). B1

is greatly affected by surface vegetation, topography and meteorological

condition (Lhomme et al. 1997). Here the parameterization scheme proposed in Su et al.

(2001) integrating the influences of these factors was used to estimate B

-1

:

kB

1

¼

kCd

4Ct

u

uðhÞ

ð1  enec=2

Þ

f

2

c

þ

k

u

uðhÞ

z0m

h

C

t

f

2

c

f

2

s

þ kB

1

s

f

2

s

; (5)

where k is the von-Karman constant, fc and fs are the coverage fraction of vegetation

and soil, respectively, Cd is the leaf dragging coefficient, Ct

is the leaf heat transfer

coefficient and Ct* is the soil heat transfer coefficient. u is the friction velocity (m s

-1

)

and z0m is the roughness height for momentum transfer (m), uðhÞ is the wind speed at

height, h, of the canopy (m s

-1

), nec

is the within-canopy wind speed profile extinction

coefficient, and Bs

–1

is the dimensionless heat transfer coefficient for bare soil.

2.3 Flow diagram of the ET models and data sources

Figure 2 shows flow diagrams of the model processing. Two datasets were required as

inputs to the two models. The first dataset consisted of land surface albedo, vegetation

indices (including NDWI and NDVI), LAI and surface temperature. These inputs

were derived from either daily or composite MODIS land products. The second

climate dataset included atmospheric pressure, air temperature, humidity, wind

speed, downward solar radiation or daily sunshine hour, which were interpolated

from the observations at weather stations.

The surface albedo and downward solar radiation (or daily sunshine hours) were

used to calculate the instantaneous (or daily) net shortwave radiation. The instantaneous net longwave radiation was estimated from the surface temperature and air

temperature, while only the maximum and minimum air temperatures were required

to estimate the daily net longwave radiation. The fractional coverage was used to

An operational method to estimate evapotranspiration 5

Downloaded by [Tsinghua University] at 06:44 07 July 2011 estimate the soil heat together with the net radiation. The NDVI and LAI provided

estimates of vegetation parameters influencing the surface heat transfer process, and a

bunch of meteorological variables was used to determine the aerodynamic resistance

for the turbulent heat fluxes. NDWI was used to estimate the surface resistance

required by the P-M model.

MODIS daily and composite images including surface temperature, surface reflectance, vegetation index (VI) and LAI from 2006 to 2007 were reprojected from the

sinusoidal (SIN) projection into the Universal Transverse Mercator (UTM) projection and resampled into 1 km resolution. Images with extensive cloud cover were

removed according to the quality flags in the MODIS datasets.

The meteorological data from 2006 to 2007 were also collected at three weather

stations as well as the field site (see figure 1). The inverse distance weighting method

was used to map the spatial distribution of the meteorological variables. The three

stations provided hourly observations in 2006, but only daily observations in 2007.

Thus in 2007, the daily data were first interpolated in the whole area and the hourly

data were derived, assuming the meteorological variables at all the four sites had

similar diurnal curves. This may be reasonable since there was only slight difference in

the topography and land cover types across this area. Besides, only the flux tower

provided observations of downward shortwave radiation. Therefore, the atmospheric

transmissivity was assumed the same across the area and the instantaneous downward

shortwave radiation varied solely with the geophysical parameters.

3. Vegetation parameterization using MODIS data

Surface albedo and LAI greatly influenced the energy balance at the surface. The

uncertainties in the MODIS albedo and LAI products were analysed and the method

to reduce the uncertainties in the input parameters for the ET models was discussed.

The MCD43B3 product provided temporal composite surface albedo at three

Incoming shortwave

radiation

Net shortwave

radiation

Net longwave

radiation

Vapour pressure

deficit

Resistance

Net radiation

Available energy

Turbulent heat

fluxes

Actual ET

MODIS

1 km data

Weather

data

Surface albedo

Surface

temperature

LAI/VI

Air temperature

Wind speed

Relative

humidity

Figure 2. Flow diagram of the evapotranspiration models including the inputs, data processing and the outputs. VI stands for vegetation index.

6 Y. Yi and D. Yang

Downloaded by [Tsinghua University] at 06:44 07 July 2011 wavelengths (0.3–0.7, 0.7–5.0 and 0.3–5.0 mm). This product was generated from the

MODIS level 1B surface reflectance data using Ross-Li model, combining Terra and

Aqua images to reduce the uncertainty in the input surface reflectance (Strahler et al.

1999). In the previous studies the surface albedo has usually been derived from the

narrowband surface reflectances, followed Liang (2001). Figure 3 shows a comparison of the composite albedo and the albedo calculated from MODIS bands 1–7 from

daily Terra and Aqua images in 2007. It can be observed from the figure that the daily

albedo fluctuated widely, and may not disclose the true changes in the surface

reflective conditions. This was due to large uncertainties in the input daily reflectances, which were sensitive to the changes in the view and azimuth angles of the

sensors, and also cloud and aerosol condition (Yi et al. 2008). Thus the daily albedo

was interpolated from the 8-day composite data as inputs to the ET models.

LAI has been estimated using a VI such as NDVI in most applications. However, the

VI was sensitive to atmospheric disturbances, and became saturated with LAI values

larger than 3 (Huete et al. 2002). TheMOD15A2 product provides 8-day composite LAI

data with 1-km resolution. This product uses the 3D radiative transfer model to model

the canopy bidirectional reflectance (BRDF) and generates a look-up table (LUT). The

LAI is retrieved based on the LUT and the MODIS surface reflectance data. However,

the empirical relationship between NDVI and LAI is still used when there is no reliable

reflectance data during the composite period due to cloud contamination. Thus, the

accuracy of LAI retrievals depends mainly on the input reflectance quality. The MODIS

Collection 5 land surface products are improved in atmospheric correction and also

in the definition of the radiative transfer model compared with Collection 4 products.

The effects of these improvements on LAI retrieval are discussed in the following

paragraph.

Figure 4 shows a comparison of the temporal series of LAI from different collections at the field site. LAI values in 2006 and 2005 were extracted from collection 4,

and the 2007 data were from collection 5. It can be seen from the figure that LAI

values in 2006 and 2005 were much smaller than LAI in 2007 especially during the

wheat growth period. The LAI series in 2007 were much closer to the ground truth.

Figure 5 shows a comparison of the LAI distribution in the study area at similar

growth stages. The LAI time series in 2007 (at date of year (DOY) 121) was 8 days

0.3

0.2

Albedo

0.1

0.0

40 60 80 100 120 140 160

Day of year

Composite

Terra

Aqua

Figure 3. Comparison between the temporal series of surface albedo derived from the

MOD43B3 product and the daily surface reflectance in 2007.

An operational method to estimate evapotranspiration 7

Downloaded by [Tsinghua University] at 06:44 07 July 2011 ahead of the LAI series in 2006 and 2005 (at DOY 129) due to the difference in the

crop growth cycles. It can be seen that most LAI values in the whole area in 2006 and

2005 were much lower than the values in 2007. However, the wheat was at its growing

peak and showed a high LAI at this stage according to the field experiment. From the

above analysis, it can be concluded improvements in the LAI retrieval algorithm and

also the reflectance quality had contributed greatly to the refinement in the LAI

retrievals. Therefore, the LAI values in 2006 were still estimated using the general

empirical relationship between the 8-day composite NDVI and LAI. The daily LAI

values were then temporally interpolated from the 8-day composite data.

4. Results and discussion

4.1 P-M model calibration and validation

Figure 6 shows a comparison of the observed and modelled net radiation and soil heat

fluxes in 2007 (a) and (b) and 2006 (c) and (d). The P-M model and the one-layer

model used the same parameterization for the two flux components, and this

7

6

5

4

LAI

3

2

1

0

0 50 100 150 200 250 300

Day of year

2007

2006

2005

Figure 4. Comparison between the temporal series of LAI extracted from the MODIS

products from 2005 to 2007.

Figure 5. Histogram of LAI distribution in the study area at similar growth periods from 2005

to 2007.

8 Y. Yi and D. Yang

Downloaded by [Tsinghua University] at 06:44 07 July 2011 parameterization scheme has been widely used in other remote sensing models

(Courault et al. 2005). In both years, the modelled net radiation results were very

close to the observations. In 2007, the root mean square errors (RMSEs) of modelled

net radiation were 16.3 and 23.9 W m

-2

for Terra and Aqua, respectively. In 2006, the

RMSE was 30.2 W m

-2

for Terra and 19.0 W m

-2

for Aqua, respectively. However,

there were large differences between the modelled and observed soil heat fluxes, and

the modelled results were generally larger than the observations especially for Terra

(in the morning). In 2007, the RMSE of modelled fluxes was as high as 52.1 W m

-2

for

Terra and the RMSE was 33.7 W m

-2

for Aqua. In 2006, the RMSEs were 60.0 and

47.4 W m

-2

for Terra and Aqua, respectively. The large discrepancy between the

modelled and observed soil heat may be caused by incorrect installation and calibration of the soil heat plates, which should be investigated further.

The flux observations at the overpass time of Aqua from 13:00 to 14:00 hours in 2007

were chosen to calibrate the surface resistance equation (3) and the results are shown

in figure 7(a). The NDWI and the surface resistance retrieved using the P-M equation

showed good linear correlation and the determination coefficient (R

2

) was as high as

0.70. The rs_max and a were calibrated as 208.32 S m

-1

and 1.12, respectively. The

calibrated value of surface resistance (rs_max) for bare soil under water stress was in a

reasonable range according to the experiment of Daamen and Simmonds (1996) and

also the field observations made by Mo et al. (2002). The flux observations at the

overpass time of Terra at 11:00–12:00 hours in 2007 and both Terra and Aqua in 2006

were used for validation and the modelling results are shown in figure 7(b). The

modelled latent heat fluxes agreed quite well with the observations. The R

2

values

between the modelled and measured latent heat fluxes were 0.94 and 0.84 for 2007

(b)

Terra

Aqua

Observed (Wm

–2

)

Modelled (Wm

–2

)

250

150

50

–50

–50

50 150 250

700

(a)

Terra

Aqua

600

500

400

300 400 500

Observed (Wm

–2

)

Modelled (Wm

–2

)

600 700

300

(d)

Terra

Aqua

Observed (Wm

–2

)

Modelled (Wm

–2

)

250

150

50

–50

–50 50 150 250

(c)

Terra

Aqua

300 400 500

Observed (Wm

–2

)

600 700 800

700

600

500

Modelled (Wm

400

–2

)

300

800

Figure 6. Comparison between the observed and modelled net radiation fluxes in (a) 2007 and

(c) 2006, and soil heat fluxes in (b) 2007 and (d) 2006, respectively.

An operational method to estimate evapotranspiration 9

Downloaded by [Tsinghua University] at 06:44 07 July 2011 Terra and 2006, respectively. The RMSE of the latent heat fluxes was 37.3 W m

-2

for

Aqua in 2007, and 44.7 W m

-2

in 2006. The RMSE values were comparable with the

results from Cleugh et al. (2007) but slightly higher than the results from Mu et al.

(2007). However, the vapour pressure deficit was introduced in Mu et al. (2007) to

describe the constraint of soil water on the evaporation, which could be reasonable at a

large scale. The sensible heat fluxes were derived as the residual of the energy balance

equation, so the results were not presented in this article.

Figure 8 shows a comparison of observed and modelled latent heat fluxes by the

one-layer model in 2007. The RMSE of the modelled latent heat fluxes was 43.7 W m

-2

for Terra and 68.8 W m

-2

for Aqua. The one-layer model showed larger RMSE values

than the P-M model, with larger bias under lower latent heat fluxes under smaller

vegetation fraction. The one-layer model assumes the land cover is homogeneous and

this may be one of the error sources when the land is only partly covered by the crop.

The modelling results using Aqua images showed a larger RMSE value than Terra

images. However, the relative errors in the morning and afternoon were close because

the crop had higher ET in the afternoon. The spatial comparison between the two

models was mainly made at the overpass time of Terra in 2007 since the above P-M

model was calibrated at the overpass time of Aqua.

650

(b)

500

2007 Terra

2006

350

200

50

50 200 350 500

Observed (Wm–2

)

650

Modelled (Wm–2

)

(a)

100

150

Resistance (Sm–1

)

50

0

0.2 0.4 0.6 0.8 1.0

NDWI

Figure 7. Calibration and validation of surface resistance equation in the P-M model in 2007

and 2006. (a) The linear relationship between the surface resistance and NDWI using Aqua data

in 2007. (b) The modelled latent heat fluxes using calibrated surface resistance for Terra data in

2007 and both Terra and Aqua data in 2006.

600

Terra

Aqua

500

400

300

200

100

0

0 100 200 300 400 500 600

Observed (Wm–1

)

Modelled (Wm–2

)

Figure 8. Comparison between the observed and modelled latent heat fluxes by the one-layer

model in 2007.

10 Y. Yi and D. Yang

Downloaded by [Tsinghua University] at 06:44 07 July 2011 Figure 9 shows comparisons of the spatial distribution of the latent heat fluxes

modelled by the two models at three selected dates from April to May in 2007 at the

overpass time of Terra. Figure 10 presents histograms of the difference between the

modelled latent heat fluxes by the two models at the three dates. The urban and village

built-up areas were excluded since the LAI values in these areas were very low and not

computed. The areas affected by cloud contamination were also masked as blank

areas. It can be seen from figure 9 that the spatial distributions of the fluxes from

the two models were quite similar. The latent heat fluxes were generally larger in the

irrigated area than the outside of the irrigation zone, and the latent heat fluxes in the

north and west areas were much smaller especially in April. These areas were far from

the irrigation drainage source at the south east part and usually less irrigated. It can be

seen from the figure 9 that typically the one-layer model showed higher ET in wet

surfaces and smaller ET in dry surfaces than the P-M model. However, the differences

of the modelled latent heat fluxes mainly fell in the range of –50 to þ50 W m

-2

, and

were acceptable. However, most of the area in one-layer model showed greater ET

than the P-M model on 14 May 2007. The NDWI showed a valley during this period,

indicating that the crop may suffer water stress during this period, while the one-layer

model showed most of the area had high ET. However, the daily NDWI values were

affected by the atmospheric condition and the view angles, which may contribute to

this discrepancy.

The above analysis shows the MODIS NDWI can provide reasonable estimation of

surface resistance under different soil moisture status and crop growth situations.

This was because the NDWI contains information from the SWIR and NIR wavelengths, which are sensitive to the crop water content, and also the accumulation of

the dry matter with crop growing (Yi et al. 2007).

4.2 The daily ET time series modelled by the P-M model

The P-M method was used to estimate the daily water consumption during the wheat

growing period in 2006 and 2007. The 8-day temporal composite NDWI was interpolated to daily data and used to estimate the daily surface resistance instead of using

the daily MODIS data. Good quality daily MODIS data may not be available due to

cloud or other factors, which was a major drawback to the one-layer model.

Moreover, the composite process can reduce greatly the uncertainty in the daily

surface reflectance caused by the changes in the view and zenith angles, cloud and

atmospheric conditions.

Figure 11 shows a comparison between the temporal series of the modelled and

observed daily actual ET during the wheat growth period in 2007 and 2006. The eddy

covariance observations at heavy rainy days (11 and 30 May 2007 and 25–27 May

2006) were excluded. It can be seen from the figure that the modelled and observed ET

time series showed similar trends during the period. The daily ET values showed

obvious temporal changes with the crop growth. In 2007, the modelled average daily

ET values increased from 2.10 mm day

-1

in March to 4.32 mm day

-1

in April and 4.84

mm day

-1

in May. In 2006, the changes in the daily ET values were similar to the

changes in 2007. In this year, the modelled average daily ET values from March to

May were 2.35, 3.75 and 4.55 mm day

-1

respectively. However, in 2006, the modelled

daily ET showed an increase during first March, while there was a decreasing trend in

the observed daily ET. The daily NDWI was interpolated from the neighbouring 8-

day composite NDWI. The quality of MODIS images was greatly affected by cloud in

An operational method to estimate evapotranspiration 11

Downloaded by [Tsinghua University] at 06:44 07 July 2011 409 Wm

–2

443 Wm

–2

104 Wm

–2

196 Wm 412 Wm

–2 –2

76 Wm

–2

(a) (b)

(c)

(e)

(d)

( f  )

Figure 9. Comparison of the spatial pattern of latent heat fluxes modelled from Terra images of

(a) 7 April 2007 by the one-layer model; (b) 7 April 2007 by the P-M model; (c) 25 April 2007 by

the one-layer model; (d) 25 April 2007 by the P-M model; (e) 14 May 2007 by the one-layer model;

(f) 14 May 2007 by the P-M model. The irrigation area boundary is marked using the black line.

12 Y. Yi and D. Yang

Downloaded by [Tsinghua University] at 06:44 07 July 2011 the winter and early spring in this area, and the influence of cloud cannot be totally

eliminated even after temporal composite. On the other hand, the 8-day composite

NDWI can capture the canopy water stress during a longer period than 8 days, but

may not respond to a short-term stress.

150

120

90

Frequency

60

30

0

–150 –100 –50 0 50 100 150

λE difference (Wm–2

)

7 April 2007

25 April 2007

14 May 2007

Figure 10. Histograms of the difference between the latent heat fluxes modelled by the P-M

model and the one-layer model at the selected dates in 2007.

10

ET (mm day

–1

)

8

6

4

2

0

1 March 21 March 10 April 30 April

Date

20 May 9 June

Observed

P-M model

(a)

ET (mm day

–1

)

10

8

6

4

2

0

1 March 21 March 10 April 30 April

Date

20 May 9 June

Observed

P-M model

(b)

Figure 11. Comparison between the temporal series of the observed and modelled daily

evapotranspiration using the P-M model during the wheat season in (a) 2007 and (b) 2006.

An operational method to estimate evapotranspiration 13

Downloaded by [Tsinghua University] at 06:44 07 July 2011 The temporal series of observed soil moisture, precipitation and irrigation during the

same periods are shown in figure 12. The statistics of the water balance components in the

two years are shown in table 1. The total crop water consumption from March to May

was estimated to be 344.9 mm in 2007 and 326.5 mm in 2006, while the rainfall amount

was lower than 100 mm in both years. The irrigation amount was estimated to be around

150 mm in 2007 and 80 mm in 2006 according to the temporal changes of measured soil

moisture profile and groundwater level. Due to water balance, the crop had to extract a

large amount of water from the deep soil layer and groundwater to sustain its growth in

both years, which were around 194 mm in 2006 and 117 mm in 2007. According to the

measured soil moisture and groundwater level, the changes in the total soil water storage

in 2006 and 2007 were estimated to be 169.2 and 89.8 mm respectively. The water

imbalance amount in 2006 was around 25 and 27 mm in 2007. The estimates of water

extraction may be not very accurate because it was difficult to separate the discharge and

recharge periods of the groundwater. Also, the horizontal water movement was ignored

Figure 12. Temporal series of the observed soil moisture, precipitation and irrigation in (a)

2007 and (b) 2006.

14 Y. Yi and D. Yang

Downloaded by [Tsinghua University] at 06:44 07 July 2011 during the calculation. Compared with 2007, the wheat consumed more water from the

root zone and deep soil layer in 2006 due to less irrigation, which was indicated by the

sharp decrease in the soil moisture and increase in the groundwater level. It can be also

seen from figure 12 that the initial soil moisture in 2006 was slightly higher than in 2007,

and correspondingly the actual ET in March 2006 was slightly larger than in 2007.

However, the rainfall and irrigation amounts were lower in 2006 than in 2007, and

therefore 2007 had larger ET during the later period.

5. Conclusions

An operational method using MODIS data was proposed to estimate the crop water

consumption, and was applied in an irrigated wheat area along the downstream part

of the Yellow River. MODIS NDWI was used to characterize the surface resistance

and the P-M model was used to model the daily actual ET during the wheat growing

season from March to April.

The ET models were quite sensitive to the input vegetation parameters, especially

albedo and LAI. It was found that the temporal composite MODIS products provided more reasonable estimates of these two parameters than the daily products.

Thus a vegetation parameterization retrieval scheme using the temporal-composite

MODIS data was employed.

NDWI was shown to provide reasonable estimation of surface resistance for P-M

model at different crop growth condition and soil moisture status. The latent heat

fluxes modelled by P-M agreed well with the field observations and showed similar

spatial pattern to those from the one-layer model. To avoid the discontinuousness in

the availability of the remote sensing images due to cloud effects, 8-day temporal

composite MODIS data were used to generate the daily NDWI and surface resistance

and the P-M model was used to estimate the daily actual ET. Compared with the

observed precipitation, irrigation and soil moisture curves, the modelled daily ET

curves provided reasonable estimation of crop consumption during the wheat major

growing period. Moreover, this model showed obvious advantages over the other

remote sensing models, which require inputs of radiometric temperature, since the

availability of these data was greatly influenced by the weather conditions and

subjected to great uncertainty. Therefore, this model can provide continuous estimation of daily crop water consumption at a regional scale and showed great potential in

precision irrigation management.

Acknowledgements

This research was supported by the National 973 Project of China (2006CB403405)

and the National Natural Science Founding Projects of China (50679029).

Table 1. The statistics of the water balance components (mm) during the major wheat growing

period from March to May in 2006 and 2007.

ET (model) Precipitation Irrigation SW Imbalance

2006 363 89 80 169.2 24.8

2007 353 86 150 89.8 27.2

Note: SW is the amount of water extracted by the crop from the deep soil layer and groundwater, calculated from the measured soil moisture profiles and groundwater level.

An operational method to estimate evapotranspiration 15

Downloaded by [Tsinghua University] at 06:44 07 July 2011 References

BALDOCCHI, D., FALGE, E., GU, L., OLSON, R., HOLLINGER, D., RUNNING, S., ANTHONI, P.,

BERNHOFER, C., DAVIS, K., EVANS, R., FUENTES, J., GOLDSTEIN, A., KATUL, G., LAW,

B., LEE, X., MALHI, Y., MEYERS, T., MUNGER, W., OECHEL, W., PAW, U.K., PILEGAARD,

K., SCHMID, H., VALENTINI, R., VERMA, S., VESALA, T., WILSON, K. and WOFSY, S., 2001,

FLUXNET: a new tool to study the temporal and spatial variability of ecosystem-scale

carbon dioxide, water vapor, and energy flux densities. Bulletin of American

Meteorological Society, 82, pp. 2415-2434.

BASTIAANSSEN, W.G.M., MENENTI, M., FEDDES R.A. and HOLTSLAG, A.A.M., 1998, A remote

sensing surface energy balance algorithm for land (SEBAL) (1. Formulation). Journal

of Hydrology, 212–213, pp. 198–212.

CECCATO, P., GOBRON, N., FLASSE, S., PINTY, B. and TARANTOLA, S., 2002, Designing a spectral

index to estimate vegetation water content from remote sensing data: Part 1.

Theoretical approach. Remote Sensing of Environment, 82, pp. 188–197.

CHEHBOUNI, A., LO SEEN, D., NJOKU, E.G. and MONTENY, B., 1996, Examination of the

difference between radiative and aerodynamic surface temperatures over sparsely

vegetated surface. Remote Sensing of Environment, 58, pp. 177–186.

CHEHBOUNI, A., NOUVELLON, Y., LHOMME, J., WATTS, C., BOULET, G., KERR, H., MORAN, S. and

GOODRICH, D., 2001, Estimation of surface sensible heat flux using dual angle observations

of radiative surface temperature. Agricultural and Forest Meteorology, 108, pp. 55–65.

CHEN, D., HUANG, J. and JACKSON, T.J., 2005, Vegetation water content estimation for corn and

soybeans using spectral indices derived from MODIS near- and short-wave infrared

bands. Remote Sensing of Environment, 98, pp. 225–236.

CLEUGH, H.A., LEUNING, R., MU, Q. and RUNNING, S.W., 2007, Regional evaporation estimates

from flux tower and MODIS satellite data. Remote Sensing of Environment, 106,

pp. 285–304.

COURAULT, D., SEGUIN, B. and OLIOSO, A., 2005, Review on estimation of evapotranspiration

from remote sensing data: from empirical to numerical modeling approaches. Irrigation

and Drainage Systems, 19, pp. 223–249.

CRACKNELL, A.P. and VAROTSOS C.A., 2007, The IPCC fourth assessment report and the fiftieth

anniversary of Sputnik. Environmental Science and Pollution Research, 14, pp. 384–387.

DAAMEN, C.C. and SIMMONDS, L.P., 1996, Measurement of evaporation from bare soil and its

estimation using surface resistance, Water Resources Research, 32, pp. 1393–1402.

FENSHOLT, R. and SANDHOLT, I., 2003, Derivation of a shortwave infrared water stress index

from MODIS near- and shortwave infrared data in a semiarid environment. Remote

Sensing of Environment, 87, pp. 111–121.

FRENCH, A.N., JACOB, F., ANDERSON, M.C., KUSTAS, W.P., TIMMERMANS, W., GIESKE, A., SU, Z.,

SU, H., MCCABE, M.F., LI, F., PRUEGER, J. and BRUNSELL, N., 2005, Surface energy fluxes

with the Advanced Spaceborne Thermal Emission and Reflection radiometer (ASTER)

at the Iowa 2002 SMACEX site (USA). Remote Sensing of Environment, 99, pp. 55–65.

HUETE, A., DIDAN, K., MIURA, T., RODRIGUEZ, E.P., GAO, X. and FERREIRA, L.G., 2002,

Overview of the radiometric and biophysical performance of the MODIS vegetation

indices. Remote Sensing of Environment, 83, pp. 195–213.

JACKSON, T.J., CHEN, D., COSH, M., LI, F., ANDERSON, M., WALTHALL, C., DORIASWAMY, P. and

HUNT, E.R., 2004, Vegetation water content mapping using Landsat data derived

normalized difference water index for corn and soybeans. Remote Sensing of

Environment, 92, pp. 475–482.

JIANG, L. and ISLAM, S., 1999, A methodology for estimation of surface evapotranspiration over

large areas using remote sensing observations. Geophysical Research Letters, 26, pp.

2773–2776.

JUPP, D.L.B., TIAN, G., MCVICAR, T.R., QIN, Y. and LI, F., 1998, Soil Moisture and Drought

Monitoring using Remote Sensing I: Theoretical Background and Methods. CSIRO Earth

Observation Centre Report 98/1 (CSIRO: Canberra).

16 Y. Yi and D. Yang

Downloaded by [Tsinghua University] at 06:44 07 July 2011 KATUL, G.G., SCHIELDGE, J., HSIEH, C.I. and VIDAKOVIC, B., 1998, Skin temperature perturbations induced by surface layer turbulence above a grass surface. Water Resources

Research, 34, pp. 1265–1274.

KUSTAS, W.P. and NORMAN J.M., 1999, Evaluation of soil and vegetation heat flux predictions

using a simple two-source with radiometric temperatures for partial canopy cover.

Agricultural and Forest Meteorology, 94, pp. 13–29.

KUSTAS, W.P., NORMAN, J.M., ANDERSON, M.C. and FRENCH, A.N., 2003, Estimating subpixel

surface temperatures and energy fluxes from the vegetation index-radiometric temperature relationship. Remote Sensing of Environment, 85, pp. 429–440.

LHOMME, J.P., MONTENY B., TROUFLEAU, D., CHEHBOUNI, A. and BAUDUIN S., 1997, Sensible

heat flux and radiometric surface temperature over sparse Sahelian vegetation II. A

model for the kB-1 parameter. Journal of Hydrology, 188–189, pp. 839–854.

LIANG, S., 2001, Narrowband to broadband conversions of land surface albedo I algorithms.

Remote Sensing of Environment, 76, pp. 213–238.

MAAYAR, M. and CHEN J., 2006, Spatial scaling of evapotranspiration as affected by heterogeneities in vegetation, topography, and soil texture. Remote Sensing of Environment,

102, pp. 33–51.

MO, X., LIU, S. and LIN, Z., 2002, Energy balance, water use efficiency and surface resistance in

a maize field. Chinese Journal of Applied Ecology, 13, pp. 551–554.

MONTEITH, J.L., 1964, Evaporation and environment. The state and movement of water in

living organisms. In Symposium of the Society of Experimental Biology, 19, pp. 205–234.

(Cambridge: Cambridge University Press).

MORAN, M.S., CLARKE, T.R., INOUE, Y. and VIDAL, A., 1994, Estimating crop water deficit

using the relation between surface air temperature and spectral vegetation index.

Remote Sensing of Environment, 49, pp. 246–263.

MU, Q., HEINSCH, F., ZHAO, M. and RUNNING, S., 2007, Development of a global evapotranspiration algorithm based on MODIS and global meteorology data. Remote Sensing of

Environment, 111, pp. 519–536.

NISHIDA, K., NEMANI, R.R., RUNNING, S.W. and GLASSY, J.M., 2003, An operational remote

sensing algorithm of land surface evaporation. Journal of Geophysical Research, 108,

pp. 4270–4283.

NORMAN, J.M., KUSTAS, W.P. and HUMES, K.S., 1995, A two-source approach for estimating

soil and vegetation energy fluxes in observations of directional radiometric surface

temperature. Agricultural and Forest Meteorology, 77, pp. 263–293.

STEWART, J.B., KUSTAS, W.P., HUMES, K.S., NICHOLS, W.D., MORAN, M.S. and de BRUIN,

H.A.R., 1994, Sensible heat flux-radiometric surface temperature relationship for

eight semiarid areas. Journal of Applied Meteorology, 33, pp. 111–117.

STRAHLER, A.H. and MULLER, J.P., 1999, MODIS BRDF/Albedo product: algorithm theoretical basis document (ATBD) Version 5.0. Available online at: modis.gsfc.nasa.gov/

data/atbd/atbd_mod09.pdf.

SU, Z., SCHMUGGE, T., KUSTAS, W.P. and MASSMAN, W.J., 2001, An evaluation of two models

for estimation of the roughness height for heat transfer between the land surface and the

atmosphere. Journal of Applied Meteorology, 40, pp. 1933–1951.

SU, Z., YACOB, A., WEN, J., ROERINK, G., HE, Y., GAO, B., BOOGAARD, H. and DIEPEN, C., 2003,

Assessing relative soil moisture with remote sensing data: theory, experimental validation, and application to drought monitoring over the North China Plain. Physics and

Chemistry of the Earth, 28, pp. 89–101.

VAROTSOS, C., 2005, Modern computational techniques for environmental data; Application to

the global ozone layer. In Lecture Notes in Computer Science, V.S. Sunderam (Ed.),

pp. 504–510 (Berlin: Springer).

VAROTSOS, C., ASSIMAKOPOULOS, M.-N. and EFSTATHIOU, M., 2007, Technical Note: Long-term

memory effect in the atmospheric CO2 concentration at Mauna Loa. Atmospheric

Chemistry and Physics, 7, pp. 629–634.

An operational method to estimate evapotranspiration 17

Downloaded by [Tsinghua University] at 06:44 07 July 2011 WAN, Z., ZHANG, Y., ZHANG, Q. and LI, Z.L., 2002, Validation of the land surface-temperature

products retrieved from Terra Mode rate Resolution Imaging Spectroradiometer data.

Remote Sensing of Environment, 83, pp. 163–180.

YANG, D., LI, C., HU, H., LEI, Z., YANG, S., KUSUDA, T., KOIKE, T. and MUSIAKE, K., 2004,

Analysis of water resources variability in the Yellow River of China during the last half

century using historical data. Water Resources Research, 40, pp. 13–19.

YI, Y., YANG, D., CHEN, D. and HUANG J., 2007, Retrieving crop physiological parameters and

assessing water deficiency using MODIS data during winter wheat growing period.

Canadian Journal of Remote Sensing, 33, pp. 189–202.

YI, Y., YANG, D., HUANG, J. and CHEN, D., 2008, Evaluation of MODIS surface reflectance

products for wheat leaf area index (LAI) retrieval. ISPRS Journal of Photogrammetry

and Remote Sensing, 63, pp. 661–677.